COUNTER AND BLINK LED

library ieee;
    use ieee.numeric_bit.all;

entity examples is port(
    clk : bit;
    count: out bit_vector(3 downto 0));
end examples;

architecture arch of examples is
begin
    process(clk)
        variable temp : natural range 0 to 10;
    begin
        if clk = '1' then
        temp := temp + 1;
        end if;
        if temp = 10 then
        temp := 0;
        end if;
        count <= bit_vector(to_unsigned(temp, 4));
    end process;
end arch;

FOR LOOP EXAMPLE – PRIMITIVE RIPPLE CARRY ADDER
library ieee;
    use ieee.numeric_bit.all;
    use ieee.std_logic_1164.all;

entity examples is
    generic(n : integer := 4);
    port( a,b : in bit_vector(n-1 downto 0);
       cin : in bit;
        cout : out bit;
        s : out bit_vector(n-1 downto 0));
end examples;

architecture arch of examples is
begin

    process(a,b,cin)
        variable c : bit_vector(n downto 0);
    begin
        c(0) := cin;
        for i in 0 to n-1 loop
        s(i) <= (a(i) xor b(i)) xor c(i);
        c(i+1) := (a(i) and b(i)) or (a(i) and c(i)) or (b(i) and c(i));
        end loop;
        cout <= c(n);
    end process;
end arch;

LEADING ZEROS COUNTER

entity examples is port(
    a : in bit_vector(7 downto 0);
    b : out natural range 0 to 8);
end examples;

architecture arch of examples is
begin

    process(a)
        variable c : natural range 0 to 8;
    begin
        c := 0;
        for i in a'range loop
        case a(i) is
        when '0' => c := c+1;
        when others => exit;
        end case;
        end loop;
        b <= c;
    end process;
end arch;

PARITY
entity examples is port(
    x : in bit_vector(7 downto 0);
    y : out bit);
end entity;

architecture ok of examples is
    signal temp: bit_vector(7 downto 0);
begin
    temp(0) <= x(0);
    gen: for i in 1 to 7 generate
        temp(i) <= temp(i-1) xor x(i);
    end generate;
    y <= temp(7);
end architecture;

PACKAGE EXAMPLE

library ieee;
    use ieee.std_logic_1164.all;

package my_package is
    constant flag: std_logic;
    function down_edge(signal s: std_logic) return boolean;
end my_package;

package body my_package is
    constant flag: std_logic := '1';
    function down_edge(signal s: std_logic) return boolean is
    begin
        return( s' event and s = '0');
    end down_edge;
end my_package;

BINARY DECADE COUNTER

–- reset clock enable load mode count when writing the process this reflects priority
-- 0 - - - - 0 highest priority - 1
-- 1 ^ 1 - - count 2
-- 1 ^ 0 0 - data 3
-- 1 ^ 0 1 0 count + 1 (binary) 4
-- 1 ^ 0 1 1 count + 1 (decade) 5
    use ieee.numeric_std.all; -- allows to use signed and unsigned

entity examples is port(
    clock, reset, enable, load, mode: in std_logic;
    data : in std_logic_vector (7 downto 0);
    count : out std_logic_vector(7 downto 0));
end entity;

architecture arch of examples is

    constant nibble_max : unsigned(3 downto 0) := "1111";
    constant decade_max : unsigned(3 downto 0) := "1001";
    constant zero_nibble: unsigned(3 downto 0) := "0000";
    constant zero_byte : unsigned(7 downto 0) := "00000000";
    signal Q : unsigned(7 downto 0);

begin
    process(clock, reset)
    begin
        if reset = '0' then -- reset register, Q <= 0
        Q <= zero_byte; --(others => '0');
        elsif rising_edge(clock) then -- increment register, Q <= Q + 1
        if enable = '0' then -- enable counter functionality
        if load = '0' then -- load data
        Q <= unsigned(data);
        elsif (mode = '0' and Q(3 downto 0) /= nibble_max) or (mode = '1' and Q(3 downto 0) /= decade_max) then --implement counting	based on mode signal
        Q(3 downto 0) <= Q(3 downto 0) + 1;
        else
        Q(3 downto 0) <= zero_nibble;
        if (mode = '0' and Q(7 downto 4) /= nibble_max) or (mode = '1' and Q(7 downto 4) /= decade_max) then --implement counting	based on mode signal
        Q(7 downto 4) <= Q(7 downto 4) + 1;--increment upper nibble
        else
        Q(7 downto 4) <= zero_nibble;-- wrap upper nibble back to 0
        end if;
        end if;
        end if;
        end if;
        count <= std_logic_vector(Q);
    end process;
end arch;

RAM INFEREING ON-CHIP RAM

library ieee;
    use ieee.std_logic_1164.all;

entity eq1 is
    generic()
    DATA_WIDTH : natural := 16;
    ADDR_WIDTH : natural := 5
    );
    port (
        clk : in std_logic;
        addr_a : in natural range 0 to 2**ADDR_WIDTH - 1;
        data_a : in std_logic_vector((DATA_WIDTH-1) downto 0);
        we_a : in std_logic := '1';
        q_a : out std_logic_vector((DATA_WIDTH -1) downto 0));

end eq1;

architecture rtl of eq1 is

    -- Build a 2-D array type for the RAM
    subtype word_t is std_logic_vector((DATA_WIDTH-1) downto 0);
    type memory_t is array(2**ADDR_WIDTH-1 downto 0) of word_t;

    -- Declare the RAM
    shared variable ram : memory_t;

begin
    -- Port A
    process(clk)
    begin
        if(rising_edge(clk)) then
        if(we_a = '1') then
        ram(addr_a) := data_a;
        end if;
        q_a <= ram(addr_a); --this is everything. ma tiktibx il hrug hekk tispicca ma tuzax il memorja ta gewwa
        end if;
    end process;
end rtl;

RAM WITH MAC
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

package math is
    type tw8 is array(7 downto 0) of std_logic;
    type tw10 is array(15 downto 0) of std_logic;

    function tw_add(a, b : tw10)return tw10;
    function tw_mul(a, b : tw8)return tw10;
end math;

package body math is
    function tw_add(a, b : tw10)return tw10 is
        variable y : tw10;
    begin
        y := tw10(unsigned(a) + unsigned(b));
        return y;
    end tw_add;

    function tw_mul(a, b : tw8)return tw10 is
        variable y : tw10;
    begin
y := tw10(unsigned(a) * unsigned(b));
        return y;
    end tw_mul;
end math;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;
    use work.math.all;

entity sync_ram is
    port (
        clock : in std_logic;
        we : in std_logic;
        address : in tw8;
        datain : in tw8;
        dataout : out tw8);
end entity sync_ram;

architecture RTL of sync_ram is

    type ram_type is array (0 to (2**address'length)-1) of tw8;
    signal ram : ram_type;
    signal read_address : std_logic_vector(address'range);

begin

    RamProc: process(clock) is

    begin
        if rising_edge(clock) then
        if we = '1' then
        ram(to_integer(unsigned(address))) <= datain;
        end if;
        end if;
    end process RamProc;

    dataout <= ram(to_integer(unsigned(address)));
end architecture RTL;

library ieee;
    use ieee.std_logic_1164.all;
    use work.math.all;

entity adder is port (
    data_a, data_b : in tw8;
    data_o : out tw10);
end adder;

architecture cpu_blk of adder is

begin
    alu : block
        port(
        abus, bbus : in tw8;
        d_out : out tw10);
        port map( abus => data_a, bbus => data_b, d_out => data_o);
        signal qbus, dbus : tw10;
    begin
        qbus <= tw_mul(abus, bbus);
        dbus <= tw_add(qbus, dbus);
        d_out <= dbus;
    end block alu;
end cpu_blk;

library ieee;
    use ieee.std_logic_1164.all;
    use work.math.all;

entity examples is port(

    clock : in std_logic;
    we_adc : in std_logic;
    we_coef : in std_logic;
    address : in tw8;
    data_adc : in tw8;
    data_coef : in tw8;
    cont : in bit;
    data_o : out tw10);
end examples;

architecture arch of examples is
    signal int_data_a, int_data_b : tw8;
begin

    unit0 : entity work.sync_ram
        port map (clock => clock, we => we_adc, address => address,	datain => data_adc, dataout => int_data_a);
     -- first component then input pin --first output pin	then signal
    unit1 : entity work.sync_ram
        port map (clock => clock, we => we_coef, address => address,	datain => data_coef, dataout => int_data_b);

    unit2 : entity work.adder
        port map (data_a => int_data_a, data_b => int_data_b, data_o	=> data_o);
end arch;

EXIT
process(a)
begin
    first_loop: for i in 0 to 100 loop
        second_loop: for j in 1 to 10 loop
        --. . . .
        exit second_loop; --exits the second loop only
        --. . . .
        exit first_loop; --exits first loop and second loop
        --or else
        exit first_loop when(i < 10); --This statement completes the execution of the loop labeled first_loop
        --when the expression i < 10 is true.
        end loop;
    end loop;
end process;

GLOBAL SIGNALS
library ieee;
    use ieee.std_logic_1164.all;

package sigdecl is
    type bus_type is array(0 to 7) of std_logic;

    signal vcc : std_logic := '1'; -- global signal
    signal gnd : std_logic := '0'; -- global signal

    function magic_function(a : in bus_type) return bus_type;
end sigdecl;

package body sigdecl is
    function magic_function(a : in bus_type) return bus_type is
        variable b : bus_type;
    begin
        b := a;
        return b;
    end magic_function;
end sigdecl;

ENUMERATED TYPE EXAMPLE
package instr is
    type instruction is (add, sub, lda, ldb, sta, stb, outa, xfr);
end instr;

use work.instr.all;

entity examples is port(
    instr : in instruction;
    addr : in integer;
    data : inout integer);
end examples;

architecture mp of examples is
begin
    process(instr)
        type regtype is array(0 to 255) of integer;
        variable a, b : integer;
        variable reg : regtype;
    begin
        --select instruction to execute
        case instr is
        when lda =>
        a := data; --load a accumulator
        when ldb =>
        b := data; --load b accumulator
        when add =>
        a := a + b; --add accumulator
        when sub =>
        a := a - b; --sub accumulator
        when sta =>
        reg(addr) := a; --put a accum in reg array
        when stb =>
        reg(addr) := b; --put b accum in reg array
        when outa =>
        data <= a; --output a accum
        when xfr =>
        a := b; --transfer b to a
        end case;
    end process;
end mp;

TRAFFIC LIGHT EXAMPLE WITH STATE MACHINE

library ieee;
    use ieee.std_logic_1164.all;

entity examples is port(
    sensor : in std_logic;
    clock : in std_logic;
    red_light : out std_logic;
    green_light : out std_logic;
    yellow_light : out std_logic);
end examples;

architecture simple of examples is
    type t_state is( red, yellow, green);
    signal present_state, next_state : t_state;
begin
   process(present_state, sensor)
    begin
        case present_state is
        when green =>
        next_state <= yellow;
        red_light <= '0';
        green_light <= '1';
        yellow_light <= '0';
        when red =>
        red_light <= '1';
        green_light <= '0';
        yellow_light <= '0';
        if sensor = '1' then
        next_state <= green;
        else
        next_state <= red;
        end if;
        when yellow =>
        red_light <= '0';
        green_light <= '0';
        yellow_light <= '1';
        next_state <= red;
        end case;
    end process;

    process
    begin
        wait until clock'event and clock = '1';
        present_state <= next_state;
    end process;
end simple;

PIPELINED EXAMPLE
library ieee;
    use ieee.std_logic_1164.all;
library floatfixlib;
    use floatfixlib.fixed_pkg.all;

entity example is port(
    clk : in std_logic;
    a, b, c :in sfixed(4 downto -8);
    avg : out sfixed(6 downto -8));
end example;

architecture rtl of example is
    signal saved_c : sfixed(4 downto -8);
    signal a_plus_b, saved_a_plus_b : sfixed(5 downto -8);
    signal saved_sum, sum : sfixed(6 downto -8);
    signal sum_div_3 : sfixed(6 downto -8);
begin
    a_plus_b <= a + b;
    reg1 : process(clk)
    begin
        if rising_edge(clk)then
        saved_a_plus_b <= a_plus_b;
        saved_c <= c;
        end if;
    end process;

    sum <= saved_a_plus_b + saved_c;
    reg2 : process(clk)
    begin
        if rising_edge(clk)then
        saved_sum <= sum;
        end if;
    end process;
    --saved_sum * to_fixed(1.0/3.0, sum_div_3'left, sum_div_3'right);
    sum_div_3 <= saved_sum;
    reg3 : process(clk)
    begin
        if rising_edge(clk)then
        avg <= sum_div_3;
        end if;
    end process;
end rtl;

UNCONSTRAINED TYPE

package mypack is
    subtype eightbit is bit_vector(0 to 7); --subtypes of unconstrained base type bit_vector
    subtype fourbit is bit_vector(0 to 3); --range 0 to 7...
    function shift_to_right(val : bit_vector) return bit_vector;
end mypack;

package body mypack is
    function shift_to_right(val : bit_vector) return bit_vector is
        variable result : bit_vector(0 to (val'length -1));
    begin
        result := val;
        if val'length > 1 then
        for i in 0 to (val'length -2)loop
        result(i) := result(i + 1);
        end loop;
        result(val'length -1) := '0';
        else
        result(0) := '0';
        end if;
        return result;
    end shift_to_right;
end mypack;

CPU WITH GENERAL PURPOSE REGS.
THIS PART NEEDS INSTRUCTION INPUT!
library ieee;
    use ieee.std_logic_1164.all;

package cpu_rom is
    constant memsize : integer := 3;

    type instruction is (add, sub, lda, ldb, sta, stb, outa, xfr);
    type mem_data_md is array(0 to 3) of instruction;
end cpu_rom;

library ieee;
    use ieee.std_logic_1164.all;
    use work.cpu_rom.all;

entity rom_data is port(
    clk : in std_logic;
    instr : out instruction);
end rom_data;

architecture md of rom_data is
    constant rom_data_md : mem_data_md :=
(lda, ldb, add, outa);
begin

    process(clk)
    begin
        if rising_edge(clk)then
        instr <= rom_data_md(0);
        instr <= rom_data_md(1);
        instr <= rom_data_md(2);
        instr <= rom_data_md(3);
        end if;
    end process;
end md;

library ieee;
    use ieee.std_logic_1164.all;
    use work.instr.all;

entity examples is port(
    instr : in instruction;
    addr : in integer;
    data : inout integer);
end examples;

architecture mp of examples is
begin
    process(instr)
        type regtype is array(0 to 255) of	integer;
        variable a, b : integer;
        variable reg : regtype;
    begin
        --select instruction to execute
        case instr is
        when lda =>
  --load a accumulator
        a := data;
        when ldb =>
  --load b accumulator
        b := data;
        when add =>
  --add accumulator
        a := a + b;
        when sub =>
  --sub accumulator
        a := a - b;
        when sta =>
  --put a accum in reg array
        reg(addr) := a;
        when stb =>
  --put b accum in reg array
        reg(addr) := b;
        when outa =>
        --output a accum
        data <= a;
        when xfr =>
        --transfer b to a
        a := b;
        end case;
    end process;
end mp;

library ieee;
    use ieee.std_logic_1164.all;
    use work.cpu_rom.all;

entity examples is port (
    clk : in std_logic;
    data : inout integer);
end examples;

architecture arch of examples is
    signal instr : instruction;
    signal addr : integer;
begin

    unit0: entity work.rom_data
        port map(clk => clk, instr => instr);

    unit1: entity work.cpu
        port map (instr => instr, addr => addr, data => data);

end arch;

DDR

library ieee;
    use ieee.std_logic_1164.all;

entity examples is port(

   clk, d1, d2 : in std_logic;
    q1 : out std_logic);

end examples;

architecture rtl of examples is
    signal t1, t2 : std_logic;
begin

    process(clk)
    begin
        if rising_edge(clk) then
        t1 <= d1;
        end if;

        if falling_edge(clk) then
        t2 <= d2;
        end if;
    end process;

    process(clk)
    begin
        q1 <= t1;
        if clk = '1' then
        q1 <= t2;
        end if;
    end process;

end rtl;

BARREL SHIFTER
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity examples is
    generic(
        DIST_WIDTH : natural := 3;
        NUM_STAGES : natural := 8);
    port(
        clk : in std_logic;
        enable : in std_logic;
        is_left : in std_logic;
        data : in std_logic_vector((NUM_STAGES-1) downto 0);
        distance : in unsigned((DIST_WIDTH-1) downto 0);
        sr_out : out std_logic_vector((NUM_STAGES-1) downto 0));
end entity;

architecture rtl of examples is
    -- Declare the shift register signal
    signal sr : unsigned ((NUM_STAGES-1) downto 0);
begin
    process (clk)
    begin
        if (rising_edge(clk)) then
        if (enable = '1') then

        -- Perform rotation with functions rol and ror
        if (is_left = '1') then
        sr <= unsigned(data) rol to_integer(distance);
        else
        sr <= unsigned(data) ror to_integer(distance);
        end if;

        end if;
        end if;
    end process;
    sr_out <= std_logic_vector(sr);
end rtl;

ATTRIBUTES – RECORDS – NONPRUNE:

--record
entity examples is port(
    flag: out bit_vector(1 to 4);
    sum : out natural range 0 to 15);
end examples;

architecture arch of examples is
    type pair is record a, b: natural range 0 to 7;
    end record;
    type stack is array(1 to 4) of pair;
    constant matrix: stack := ((1,2),(3,4),(5,6),(7,0));
begin
    gen: for i in 1 to 4 generate
        flag(i) <= '1' when matrix(i).a > matrix(i).b else '0';
    end generate;
    sum <= matrix(1).a + matrix(1).b;
end architecture;

--attribute
entity examples is port(
    clk: in bit;
    data_in: in bit_vector(3 downto 0);
    data_out: out bit_vector(3 downto 0));
end examples;

architecture data_register of examples is
    attribute chip_pin: string;
    attribute chip_pin of clk: signal is "n2";
    attribute chip_pin of data_in: signal is "a3, a4, a5, a6";
    attribute chip_pin of data_out: signal is "b3, b4, b5, b6";
begin
process(clk)
    begin
        if(clk'event and clk='1')then
        data_out <= data_in;
        end if;
    end process;
end architecture;

--preserve nonprune attribute
entity examples is port(
    clk,x:in bit;
    y: out bit);
end examples;

architecture arch of examples is
    signal a,b,c: bit;
    attribute preserve: boolean;
    attribute preserve of a,b,c: signal is true;
    -- attribute nonprune: boolean;
    -- attribute nonprune of a,b,c: signal is true;
begin
    process(clk)
    begin
        if(clk'event and clk='1')then
        a <= x;
        b <= x;
        c <= x;
        end if;
    end process;
    y <= a and b;
end architecture;

BARREL SHIFTER

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity examples is port(
    a_uns, b_uns : in unsigned(7 downto 0);
    sum : out unsigned(7 downto 0);
    cin: in std_logic;
    cout_sum: out std_logic);
end examples;
architecture sum of examples is
    signal sum_uns: unsigned(9 downto 0);
begin
    sum_uns <= ('0' & a_uns & cin) + ('0' & b_uns & '1');
    sum <= sum_uns(8 downto 1);
    cout_sum <= sum_uns(9);
end sum;

THE FIFO HAS FLAGS, EMPTY AND FULL , THAT SIGNIFY ITS STATE. IT USES A FUNCTION TO INCREMENT TWO CIRCULAR POINTERS. ONE POINTER KEEPS TRACK OF THE ADDRESS TO WRITE TO NEXT, THE OTHER POINTER TRACKS THE ADDRESS TO READ FROM. THE FIFO MEMORY MAY BE IMPLEMENTED IN A NUMBER OF WAYS IN HARDWARE. WE SHALL ASSUME FOR THE MOMENT THAT IT WILL BE SYNTHESIZED AS A BANK OF FLIP-FLOPS.
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity fifo is --first in first out register
    generic( b_width : integer := 12;
    depth : integer := 16);
    port( clk, rst, push, pop : in std_logic;
        di : in unsigned (b_width-1 downto 0);
      do : out unsigned (b_width-1 downto 0);
      empty, full : out std_logic);
end fifo;

architecture rtl of fifo is
    subtype ptype is integer range 0 to (depth-1);

    signal diff, ai, ao : ptype; --ai and ao are indexes. difference is
 a pointer.
    signal f, e : std_logic;

    type a is array(ptype) of unsigned(b_width-1 downto 0);
    signal mem : a;

    function bump(signal ptr : integer range 0 to (depth-1)) return	integer is
    begin
        if(ptr = (depth-1)) then
        return 0;
        else return(ptr +1);
        end if;
    end bump;
begin
    process(f,e)
    begin
        full <= f;
        empty <= e;
    end process;

    process(diff)
    begin
        if(diff = depth-1)then
        f <= '1';
        else f <= '0';
        end if;

        if(diff = 0)then
        e <= '1';
        else e <= '0';
        end if;
    end process;

    process(clk) --push and pop are synchronous with clk
    begin --read and write should not occur at the same time
        if rising_edge(clk)then
        if((push = '1') and (pop = '0') and (f = '0')) then
        mem(ai) <= di;
        end if;
        if((push = '0') and (pop = '1') and (e = '0')) then
        do <= mem(ao);
        end if;
        end if;
    end process;

    process(rst, clk)
    begin
        if(rst = '1')then
        ai <= 0;
        ao <= 0;
        diff <= 0;
        elsif rising_edge(clk) then
        if(push = '1') and (pop = '0') and (f = '0') then
        ai <= bump(ai);
        diff <= diff + 1;
        elsif(push = '0') and (pop = '1') and (e = '0') then
        ao <= bump(ao);
        diff <= diff-1;
        end if;
        end if;
    end process;
end rtl;

CRC GEN

library ieee;
    use ieee.std_logic_1164.all;

package crcpack is

    constant crcdim: integer := 16;
    constant crc16: std_logic_vector(crcdim downto 0) := "11000000000000101";
    constant crc: std_logic_vector(crcdim downto 0) := crc16;
    constant data_width: integer range 1 to crcdim := 16;

    type matrix is array(crcdim-1 downto 0) of std_logic_vector(crcdim-1 downto 0);
end crcpack;

library ieee;
    use ieee.std_logic_1164.all;
    use work.crcpack.all;

entity crcgen is port(
    res, clk: in std_logic;
    din: in std_logic_vector(data_width-1 downto 0);
    xout: out std_logic_vector(crcdim-1 downto 0));
end crcgen;

architecture rtl of crcgen is
    signal x,x1,x2,din_s : std_logic_vector(crcdim-1 downto 0);
begin

    process(din)
        variable din_v : std_logic_vector(crcdim-1 downto 0);
    begin
        din_v := (others => '0');
        din_v(data_width-1 downto 0) := din; --lfsr
        --din_v(crcdim-1 downto crcdim-data_width) := din; --lfsr2
        din_s <= din_v;
    end process;

    x2 <= x; --lfsr
    --x2 <= x xor din_s; lfsr2

    process(res, clk)
    begin
        if res = '0' then x <= (others => '0');
        elsif rising_edge(clk) then
        x <= x1 xor din_s; --lfsr
        --x <= x1; --lfsr2
    end if;
end process;
xout <= x;

--this process build matrix m = f^w
process(x2)
    variable xtemp, vect, vect2 : std_logic_vector(crcdim-1 downto 0);
    variable m, f : matrix;
begin
    --matrix f
    f(0) := crc(crcdim-1 downto 0);
    for i in 0 to crcdim-2 loop
        vect := (others => '0');
        vect(crcdim-i-1) := '1';
        f(i+1) := vect;
    end loop;
    --matrix m = f^w
    m(data_width-1) := crc(crcdim-1 downto 0);
    for k in 2 to data_width loop
        vect2 := m(data_width-k+1);
        vect := (others => '0');
        for i in 0 to crcdim-1 loop
        if vect2(crcdim-1-i) = '1' then
        vect := vect xor f(i);
        end if;
        end loop;
        m(data_width-k) := vect;
    end loop;

    for k in data_width-1 to crcdim-1 loop
        m(k) := f(k-data_width+1);
    end loop;
    --combinatinal logic equations: x1 = m(x)x
    xtemp := (others => '0');
    for i in 0 to crcdim-1 loop
        vect := m(i);
        for j in 0 to crcdim-1 loop
        if vect(j) = '1' then
        xtemp(j) := xtemp(j) xor x2(crcdim-1-i);
        end if;
        end loop;
    end loop;
    x1 <= xtemp;
end process;
end rtl;

MOORE
library ieee;
    use ieee.std_logic_1164.all;

entity moore is port( -- moore machine
    x, clock: in bit;
    z: out bit);
end moore;

architecture behavior of moore is
    type state_type is (s0, s1, s2, s3);
    signal current_state, next_state: state_type;
begin
    -- process to hold combinational logic
    combin: process(current_state, x)
    begin
        case current_state is
        when s0 =>
        z <= '0';
        if x = '0' then
        next_state <= s0;
        else
        next_state <= s2;
        end if;

        when s1 =>
        z <= '1';
        if x = '0' then
        next_state <= s0;
        else
        next_state <= s2;
        end if;

        when s2 =>
        z <= '1';
        if x = '0' then
        next_state <= s2;
        else
        next_state <= s3;
        end if;

        when s3 =>
        z <= '0';
        if x = '0' then
        next_state <= s3;
        else
        next_state <= s1;
     end if;
        end case;
    end process;

-- process to hold synchronous elements (flip–flops)
    synch: process
    begin
        wait until clock'event and clock = '1';
        current_state <= next_state;
    end process;
end behavior;

UNIVERSAL BINARY COUNTER
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity tdm is -- univ binary counter
    generic(n: integer :=8);
    port(
        clk, reset: in std_logic;
        syn_clr, load, en, up: in std_logic;
        d: in std_logic_vector(n-1 downto 0);
        max_tick, min_tick: out std_logic;
       q: out std_logic_vector(n-1 downto 0));
end tdm;
architecture arch of tdm is
    signal r_reg: unsigned(n-1 downto 0);
    signal r_next: unsigned(n-1 downto 0);
begin
    --register
    process(clk, reset)
    begin
        if reset = '1' then
        r_reg <= (others => '0');
        elsif rising_edge(clk) then
        r_reg <= r_next;
        end if;
    end process;
    --next state logic
    r_next <= (others => '0') when syn_clr = '1' else
        unsigned(d) when load = '1' else
        r_reg + 1 when en = '1' and up = '1' else
        r_reg - 1 when en = '1' and up = '0' else
        r_reg;
        --output logic
        q <= std_logic_vector(r_reg);
        max_tick <= '1' when r_reg = (2**n-1) else '0';
        min_tick <= '1' when r_reg = 0 else '0';
end arch;

HEX TO SSEG
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity hex_to_sseg is port(
    clk, rst : in std_logic;
    -- hex : in std_logic_vector(3 downto 0);
    -- hex : in natural (0 to 15);
    dp : in std_logic;
    seg_sel : out unsigned(3 downto 0);
    sseg: out std_logic_vector(7 downto 0));
end hex_to_sseg;

architecture arch of hex_to_sseg is

    type oned is array (0 to 15) of std_logic_vector(6 downto 0);
    constant seg_data : oned := ( "0000001", "1001111", "0010010", "0000110",
   "0000110", "1001100", "0100100", "0100000",
    "0001111", "0000000", "0000100", "0001000",
    "1100000", "0110001", "0110000", "0111000");

    signal seg_inc: unsigned(3 downto 0) := "0001" ;
    signal hex : unsigned(15 downto 0) := (others => '0');
    signal en : bit;

    subtype digit is unsigned(12 downto 0);
    constant zero : digit := (others => '0');

begin
    -- gen: for i in hex'range generate
    -- sseg(i) <= seg_data(i) when hex = i;
    -- end generate;
    process(clk, rst)
        variable inc : digit;
    begin
        if rst = '1' then
        inc := (others => '0');
        elsif rising_edge(clk) then
        inc := inc +1;
        seg_inc <= seg_inc(0) & seg_inc(3 downto 1);

        if inc = zero then
        hex <= hex +1;
        end if;
        end if;
    end process;

    seg_sel <= seg_inc;
    -- hex qed juri listes numru. irid jigi unsigned
    with seg_inc select
    sseg(6 downto 0) <= seg_data(to_integer(hex(3 downto 0))) when "0001",
        seg_data(to_integer(hex(7 downto 4))) when "0010",
       seg_data(to_integer(hex(11 downto 8))) when "0100",
        seg_data(to_integer(hex(15 downto 12))) when "1000",
      "1111111" when others;
        sseg(7) <= dp;

end arch;

ACCUMULATOR
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity accumulator is port (
    clk, rst : in std_logic;
    data_in : in std_logic_vector(3 downto 0);
    data_out : out std_logic_vector(3 downto 0));
end entity;

architecture arch of accumulator is
    signal reg : unsigned(3 downto 0);
begin

    process(clk,rst)
    begin
        if rst = '1' then
        reg <= (others => '0');
        elsif rising_edge(clk) then
        reg <= reg + unsigned(data_in);
        end if;
    end process;

    data_out <= std_logic_vector(reg);
end arch;

PWM LED MODULATION
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity disp_mux_test is port(
    clk, rst : std_logic;
    led0, led1 : out std_logic);
end entity;

architecture arch of disp_mux_test is
    signal clk_div_reg, clk_div_next : unsigned (13 downto 0);
    signal pwm0_reg, pwm0_next, pwm1_reg, pwm1_next : unsigned (7 downto 0);
    signal led_inv_0, led_inv_1, clk_div : std_logic;
begin

    process(clk, rst)
    begin
        if rst = '0' then
        clk_div_reg <= (others => '0');
        elsif rising_edge(clk) then
        clk_div_reg <= clk_div_next;
        end if;
    end process;

    clk_div_next <= (others => '0') when clk_div_reg = 5000 else clk_div_reg + 1;

    clk_div <= '1' when clk_div_reg = 5000 else '0';

    process(clk_div, rst)
    begin
        if rst = '0' then
        pwm0_reg <= (others => '0');
        pwm1_reg <= (others => '0');
        elsif rising_edge(clk_div) then
        pwm0_reg <= pwm0_next;
        pwm1_reg <= pwm1_next;
        end if;
    end process;

    pwm0_next <= (others => '0') when pwm0_reg = 254 else pwm0_reg + 1;
    pwm1_next <= (others => '0') when pwm1_reg = 252 else pwm1_reg + 1;

    led_inv_0 <= '1' when pwm0_reg > 127 else '0';
    led_inv_1 <= '1' when pwm1_reg > 126 else '0';
    led0 <= led_inv_0 xor led_inv_1;

end arch;
NOISE GENERATOR
library ieee;
use ieee.std_logic_1164.all;

entity acnt is port(
rstn, en : in std_logic;
cntr	: out std_logic_vector(7 downto 0));
end acnt;

architecture rtl of acnt is
component my_jkff is port(
clk, rstn, j, k : in std_logic;
q, qn : out std_logic);
end component;

signal ffq : std_logic_vector(8 downto 0);
signal ffqn : std_logic_vector(8 downto 0);
signal vdd : std_logic;

begin
vdd <= '1'; ffqn(0) <= en;
jk0 : for j in 1 to 8 generate
b17 : my_jkff port map(clk => ffqn(j-1), rstn => rstn, j => vdd,
k => vdd, q => ffq(j), qn => ffqn(j));
end generate;
cntr <= ffq(8 downto 1);
end rtl;

HOW TO USE IF – ELSE IF

HOW TO USE IF – ELSE IF
library ieee;
use ieee.std_logic_1164.all;

entity fa is port(
    s1, s2, s3, x, y, z : in std_logic;
    clk, rst, clk_ena : in std_logic;
    data_in : in std_logic_vector(7 downto 0);
    data_out : out std_logic_vector(7 downto 0);
    Out1, Out2, Out3 : out std_logic);
end fa;

architecture beh of fa is
begin

    process (s1, s2, s3, x, y, z)
    begin
        Out1 <= '0';
        Out2 <= '0';
        Out3 <= '0';

        if s1 = '1' then Out1 <= x; end if;
        if s2 = '1' then Out2 <= y; end if;
        if s3 = '1' then Out3 <= z; end if;
    end process;
end beh;

# Signal Assignments in VHDL: with/select, when/else and case
### With / Select
The most specific way to do this is with as selected signal assignment. Based on several possible values of a, you assign a value to b. No redundancy in the code here. The official name for this VHDL with/select assignment is the selected signal assignment.
with a select b <=
    "1000" when "00",
    "0100" when "01",
    "0010" when "10",
    "0001" when "11";
### When / Else Assignment
The construct of a conditional signal assignment is a little more general. For each option, you have to give a condition. This means that you could write any boolean expression as a condition, which give you more freedom than equality checking. While this construct would give you more freedom, there is a bit more redundancy too. We had to write the equality check (a =) on every line. If you use a signal with a long name, this will make your code bulkier. Also, the separator that's used in the selected signal assignment was a comma. In the conditional signal assignment, you need the else keyword. More code for the same functionality. Official name for this VHDL when/else assignment is the conditional signal assignment
b <= "1000" when a = "00" else
     "0100" when a = "01" else
     "0010" when a = "10" else
     "0001" when a = "11";
Combinational Process with Case Statement
The most generally usable construct is a process. Inside this process, you can write a case statement, or a cascade of if statements. There is even more redundancy here. You the skeleton code for a process (begin, end) and the sensitivity list. That's not a big effort, but while I was drafting this, I had put b in the sensitivity list instead of a. Easy to make a small misstake. You also need to specify what happens in the other cases. Of course, you could do the same thing with a bunch of IF-statements, either consecutive or nested, but a case statement looks so much nicer.
process(a)
begin
    case a is
        when "00" => b <= "1000";
        when "01" => b <= "0100";
        when "10" => b <= "0010";
        when "11" => b <= "0001";
        when others => report "unreachable" severity failure;
    end case;
end process;
While this last code snippet is the largest and perhaps most error-prone, it is probably also the most common. It uses two familiar and often-used constructs: the process and the case statements.

CLOCK DIV – EDGE DETEC – SHIFT BIT COUNT – CONSTANT MEM SHIFT
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity shft is port(
    clk: in std_logic;
    rst: in boolean;
    bit_cnt_view : out unsigned(2 downto 0);
    my_data_view : out std_logic_vector(7 downto 0);
    sdo, sclk, r_e: out std_logic);
end shft;

architecture arch of shft is
    type data is array (0 to 15) of std_logic_vector(7 downto 0);
    signal my_data : data := ( "10101010","10110100",
        "10001010","10101001",
        "10101101","11010011",
        "10010100","10100101",
        "10001010","11101010",
        "10010011","00100110",
        "10001010","11001101",
        "10010110","00011010");

    signal clk_div : unsigned(9 downto 0);
    signal new_clk, hold, rise_edge : std_logic;
    signal shft_reg : std_logic_vector(8 downto 0);
    signal bit_cnt : unsigned(2 downto 0);

begin
    --clock division
    process(clk, rst)
    begin
        if not rst then
        clk_div <= (others => '0');
        new_clk <= '0';
        elsif rising_edge(clk) then
        clk_div <= clk_div +1;
        if clk_div = 0 then
        new_clk <= not new_clk;
        end if;
        end if;
    end process;

    --rising edge detector for new clock
    process(clk, rst)
    begin
        if not rst then
        hold <= '0';
        elsif rising_edge(clk) then
        hold <= new_clk;
        end if;
    end process;

    rise_edge <= new_clk and (not hold);

    --bit counter
    process(clk, rst)
    begin
        if not rst then
        bit_cnt <= (others => '1');
        elsif rising_edge(clk) then
        if rise_edge = '1' then
        bit_cnt <= bit_cnt -1;
        end if;
        end if;
    end process;

    --shift register
    process(clk, rst)
        variable my_data_count : unsigned(3 downto 0);
    begin
        if not rst then
        shft_reg <= (others => '0');
        my_data_count := (others => '0');
        my_data_view <= (others => '0');
        elsif rising_edge (clk) then
        if rise_edge = '1' then
        shft_reg <= shft_reg(7 downto 0) & '1';
        if bit_cnt = 0 then
        shft_reg(7 downto 0) <=	my_data(to_integer(my_data_count));
        my_data_view <= my_data(to_integer(my_data_count));
        my_data_count := my_data_count +1;
        end if;
        end if;
        end if;
    end process;

    sdo <= shft_reg(8);
    sclk <= new_clk;
    r_e <= rise_edge;
    bit_cnt_view <= bit_cnt;

end arch;

UART FROM BOOK

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;
    use ieee.math_real.all;

package defines is
    constant dbit: natural := 8;
    constant sb_tick: natural := 16;
    constant gesu: natural := natural(log2(real(dbit)));

    type data_size is array (dbit-1 downto 0) of std_logic;
    -- type data_width is array (gesu-1 downto 0) of unsigned;
end defines;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;
--use work.defines.all;

entity uart_rx is
    generic(
        dbit: integer := 8; --# data bits
        sb_tick: integer := 16); -- # ticks for stop bits

        port(
        clk, rst: in std_logic;
        s_tick, rx: in std_logic; --s_tick is the enable tick from the baud rate gen and there are 16 ticks in a bit interval
        data_out: out std_logic_vector(7 downto 0); --data_size;
        rx_done_tick: out std_logic);
end uart_rx;

architecture arch of uart_rx is
    type state_type is(idle, start, data, stop);
    signal state_reg, state_next: state_type;
    signal s_reg, s_next: unsigned(3 downto 0); --(sb_tick-1 downto 0); --tracks # of sampling ticks: 7 start state, 15 data state, sb_tick stop state
    signal n_reg, n_next: unsigned(2 downto 0);--(gesu-1 downto 0);-- data_width; --tracks # of data bits received in the data state.
    signal b_reg, b_next: std_logic_vector(7 downto 0); --data_size; --serial shift register
begin
    --FSMD state & data registers
    process(clk, rst)
    begin
        if rst = '1' then
        state_reg <= idle;
        s_reg <= (others => '0');
        n_reg <= (others => '0');
        b_reg <= (others => '0');
        elsif rising_edge(clk) then
        state_reg <= state_next;
        s_reg <= s_next;
        n_reg <= n_next;
        b_reg <= b_next;
        end if;
    end process;
    --next state logic & data path functional units/routing
    process(state_reg, s_reg, n_reg, b_reg, rx, s_tick, b_next)
    begin

        state_next <= state_reg;
        s_next <= s_reg;
        n_next <= n_reg;
        b_next <= b_reg;
        rx_done_tick <= '0';

        case state_reg is
        when idle => --start bit '0', stop bit '1'
        if rx = '0' then
        state_next <= start;
        s_next <= (others => '0');
        end if;

        when start =>
        if s_tick = '1' then
        if s_reg = 7 then
        state_next <= data;
        s_next <= (others => '0');
        n_next <= (others => '0');
        else
        s_next <= s_reg +1;
        end if;
        end if;

        when data =>
        if (s_tick = '1') then
        if s_reg = 15 then
        b_reg <= rx & b_reg(7 downto 1);
        s_next <= (others => '0');

        if n_reg = dbit-1 then
        state_next <= stop;
        else
        n_next <= n_reg +1;
        end if;
        s_next <= s_reg +1;
        end if;
        end if;
when stop =>
tx_next <= '1';
if s_tick = '1' then
if s_reg = sb_tick -1 then
state_next <= idle;
tx_done_tick <= '1';
else
s_next <= s_reg +1;
end if;
end if;
        end case;
 end process;
data_out <= b_reg;
end arch;

I2S - TX
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity i2s_tx is
    port( clk: in std_logic;
    fall_edge, rise_edge: in std_logic;
    rst: in boolean;
    it_sel: in std_logic_vector(1 downto 0);
    it_data: in std_logic_vector(7 downto 0);
    it_ws, it_sclk, it_sd: out std_logic);
end entity;

architecture arch of i2s_tx is

    signal ssclk, s_ws, sel, lr_edge, sel_rise: std_logic;
    signal bit_count: unsigned(3 downto 0);

    signal shift, shift_nxt, shift_lft, shift_rht: std_logic_vector
    (7 downto 0);
    signal int_rise_e, int_fall_e, int_edge_reg: std_logic;

begin

    process(clk, rst, sel_rise)
    begin
        if rst or sel_rise = '1' then
        ssclk <= '0';
        elsif rising_edge(clk) then
        if rise_edge = '1' then
        ssclk <= not ssclk;
        end if;
        end if;
    end process;

    process(clk, rst)
    begin
        if rst then
        int_edge_reg <= '0';
        elsif rising_edge(clk) then
        int_edge_reg <= ssclk;
        end if;
    end process;

    int_fall_e <= (not int_edge_reg) nor ssclk;
    int_rise_e <= (not int_edge_reg) and ssclk;

    process(clk, rst, sel_rise)
    begin
        if rst or sel_rise = '1' then
        bit_count <= (others => '0');
        s_ws <= '0';
        elsif rising_edge(clk) then
        if int_fall_e = '1' then
        bit_count <= bit_count +1;

        if bit_count = 6 or bit_count = 14 then
        s_ws <= not s_ws;
        end if;
        end if;
        end if;
    end process;

    it_sclk <= ssclk;
    it_ws <= s_ws;

    sel <= it_sel(0) nor it_sel(1);

    process(clk, rst)
    begin
        if rst then
        lr_edge <= '0';
        elsif rising_edge(clk) then
        lr_edge <= sel;
        end if;
    end process;

    sel_rise <= sel and (not lr_edge);

    --main shift register
    process(clk)
    begin
        if rising_edge(clk) then
        shift <= shift_nxt;
        end if;
    end process;

    shift_nxt <= shift(6 downto 0) & '0' when int_fall_e = '1' else
        shift_lft when bit_count = 0 and int_rise_e = '1' else
        shift_rht when bit_count = 8 and fall_edge = '1' else -- change to bit_count 7 and int fall
        shift;

        process(clk, rst)
        begin
        if rst then
        shift_lft <= (others => '0');
        shift_rht <= (others => '0');
        elsif rising_edge(clk) then
        if it_sel = "00" then
        shift_lft <= it_data;
        end if;

        if it_sel = "01" then
        shift_rht <= it_data;
        end if;
        end if;
        end process;

        it_sd <= shift(7);

end arch;

I2S – RX
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity i2s_rx is
    generic( n: natural := 8 );
    port( clk, ir_sd: in std_logic;
    rst: in boolean;
    data: out std_logic_vector(n-1 downto 0);
    ir_ws, ir_sclk: in std_logic);
end entity;

architecture arch of i2s_rx is
    signal rx_shift: std_logic_vector(n-1 downto 0);
    signal rise_edge, fall_edge, wsd, wsp, pl, ssclk, ena_reg: std_logic;
    signal bit_count: unsigned(2 downto 0);
begin

    process(clk, rst)
    begin
        if rst then
        ena_reg <= '0';
        elsif rising_edge(clk) then
        ena_reg <= ssclk;
        end if;
    end process;
    rise_edge <= (not ena_reg) and ssclk;
    fall_edge <= (not ena_reg) nor ssclk;

    process(clk, rst, fall_edge, wsp)
    begin
        if rst or (fall_edge = '1' and wsp = '1') then
        bit_count <= (others => '0');

        elsif rising_edge(clk) then
        if fall_edge = '1' then
        bit_count <= bit_count +1;
        end if;
        end if;
    end process;

    process(clk, rst)
    begin
        if rst then
        wsd <= '0';
        wsp <= '0';
        elsif rising_edge(clk) then
        if fall_edge = '1' then
        wsd <= ir_ws;
        wsp <= wsd;
        end if;
        end if;
    end process;

    pl <= wsp xor wsd;

    process(clk, rst)
    begin
        if rst then
        rx_shift <= (others => '0');
        data <= (others => '0');
        elsif rising_edge(clk) then
        if rise_edge = '1' then
        rx_shift <= rx_shift(n-2 downto 0) & ir_sd;

        if (pl = '1' and ir_ws = '1') then
        data <= rx_shift;
        end if;

        if (pl = '1' and ir_ws = '0') then
        data <= rx_shift;
        end if;

        end if;
        end if;
    end process;

    ssclk <= ir_sclk;

end arch;

http://www.labbookpages.co.uk/fpgas/modules/i2cController.html

GRAY COUNTER
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity mem_ctrl is
    generic( n : natural := 4);
    port(
        clk, rst : in std_logic;
        count_ld : in std_logic;
        cout_ena : in std_logic;
        index : in std_logic_vector(n downto 0);
        add_out : out std_logic_vector(n downto 0));
end mem_ctrl;

architecture arch of mem_ctrl is
    signal count, gray : unsigned(n downto 0);
begin
    process(clk,rst)
    begin
        if rst = '0' then
        count <= (others => '0');
        elsif rising_edge(clk) then
        if cout_ena = '1' then
        count <= gray +1;
        if count_ld = '1' then
        count <= unsigned(index);
        end if;
        end if;
        end if;
    end process;
    gray <= count xor('0' & count(n -1 downto 1));
    add_out <= std_logic_vector(count);
end arch;	.

DEBOUNCING / LFSR / GRAYCODE / RESIZE / OVF

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity button_int is port(
    clk, rst : in std_logic;
    sw_in : in std_logic;
    edge_out : out std_logic);
end button_int;

architecture rtl of button_int is
    constant n : natural := 4;

    signal synchro : std_logic_vector(2 downto 0);
    signal lfsr : unsigned(n -1 downto 0);
    signal lfsr_sum: unsigned(n downto 0);

    signal cout_ena: std_logic;
    signal count : unsigned(n -1 downto 0);
    signal sum : unsigned(n -1 downto 0);

    signal latch, rise_reg : std_logic;
begin

    process(clk, rst)
    begin
        if rst = '0' then
        lfsr <= (0 => '1', others => '0');
        synchro <= (others => '0');
        elsif rising_edge(clk) then
        lfsr <= lfsr(n-2 downto 0) & (lfsr(n-1) xor lfsr(n-2));

        synchro <= sw_in & synchro(2 downto 1);
        end if;
    end process;

    lfsr_sum <= resize(lfsr,n +1) +1;
    cout_ena <= lfsr_sum(n) and synchro(0);

    process(clk,rst)
    begin
        if synchro(0) = '0' then
        count <= (others => '0');
        elsif rising_edge(clk) then
        if cout_ena = '1' and count /= X"F" then
        count <= count +1;
        end if;
        end if;
    end process;

    sum <= count xor('0' & count(n -1 downto 1));

    latch <= count(0) and count(1) and count(2) and count(3);

    process(clk, rst)
    begin
        if rst then
        rise_reg <= '0';
        elsif rising_edge(clk) then
        rise_reg <= latch;
        end if;
    end process;
    edge_out <= (not rise_reg) and latch;

end rtl;

UNIVERSAL BIT COUNTER
--syn_clr load en up q* operation
---- 1 - - - 00...00 synchronous clear sampled at rising_edge
---- 0 1 - - d parallel load
---- 0 0 1 1 q+1 count up
---- 0 0 1 0 q-1 count down
---- 0 0 0 - q pause

library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

entity univ_bit_counter is
    generic ( n : integer := 8);
    port( clk, rst : in std_logic;
        syn_clr, load, en, up : in std_logic;
        d : in std_logic_vector(n-1 downto 0);
        max_tick, min_tick : out std_logic;
        q : out std_logic_vector(n-1 downto 0));
end univ_bit_counter;

architecture arch of univ_bit_counter is
    signal r_reg, r_next : unsigned(n-1 downto 0);
    signal comb : std_logic_vector(2 downto 0);
begin

    process(rst, clk)
    begin
        if rst = '1' then
        r_reg <= (others => '0');
        elsif rising_edge(clk)then
        if syn_clr = '1' then
        r_reg <= (others => '0');
        else r_reg <= r_next;
        end if;
        end if;
    end process;

comb <= load & en & up;
with (comb) select
r_next <=
unsigned(d) when "100",
r_reg + 1 when "011",
r_reg - 1 when "010",
r_reg when others;

-- r_next <= unsigned(d) when (load = '1') else
-- r_reg + 1 when (en = '1' and up = '1') else
-- r_reg - 1 when (en = '1' and up = '0') else
-- r_reg;

q <= std_logic_vector(r_reg);
max_tick <= '1' when r_reg = 2**n - 1 else '0';
min_tick <= '1' when r_reg = 0 else '0';
end arch;

SIGN MAGNITUDE ADDER
--A signed magnitude adder performs an addition operation in this format:
-- - if the two operands have the same signs, add the magnitudes and keep the sign.
-- - if the two operands have different signs, subtract the smaller magnitude from
-- the large one and keep the sign of the numner that has the larger magnitude.
--One way of doing it is in two stages: First stage sorts the two inputs according to
--their magnitudes and routes them to the max and min signals. The second stage examines
--the signs and performs addition or subtraction on the magnitude accordingly. Note that
--since the two numbers have been sorted, the magnituse of max is always larger then that
--of min and the final sign is the sign max. Also note that the relevant magnituse signals
--are declared as unsigned to facilitate the arithmetic operation, and type conversions
--are performed at the beginning and end of the code.

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

package define is
    constant n : integer := 4;
    subtype digit is std_logic_vector(n-1 downto 0);
    subtype size is unsigned(n-2 downto 0);
end define;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;
    use work.define.all;

entity sign_mag_add is port(
    a, b: in digit;
    sum: out digit);
end entity;

architecture arch of sign_mag_add is
    signal mag_a, mag_b: size;
    signal mag_sum, max, min : size;
    signal sign_a, sign_b, sign_sum: std_logic;
begin
    mag_a <= unsigned(a(n-2 downto 0));
    mag_b <= unsigned(b(n-2 downto 0));
    sign_a <= a(n-1);
    sign_b <= b(n-1);
    --sort according to magnitude
    process(mag_a, mag_b, sign_a, sign_b)
    begin
        if mag_a > mag_b then
        max <= mag_a;
        min <= mag_b;
        sign_sum <= sign_a;
        else
        max <= mag_b;
        min <= mag_a;
        sign_sum <= sign_b;
        end if;
    end process;
    -- add/sub magnitude
    mag_sum <= max + min when sign_a = sign_b else
        max - min;
        --form output
        sum <= std_logic_vector(sign_sum & mag_sum);
    end arch;

SIGN MAGNITUDE ADDER - TEST BENCH
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity sm_add_test is port(
    clk : in std_logic;
    btn : in std_logic_vector(1 downto 0);
    sw : in std_logic_vector(7 downto 0);
    an : out std_logic_vector(3 downto 0);
    sseg : out std_logic_vector(7 downto 0));
end sm_add_test;

architecture arch of sm_add_test is
    signal sum, mout, oct : std_logic_vector(3 downto 0);
    signal led3, led2, led1, led0: std_logic_vector(7 downto 0);
begin
    --instantiate adder
    sm_adder_unit : entity work.sign_mag_add
        -- generic map(n => 4)
        port map(a => sw (3 downto 0), b => sw (7 downto 4), sum => sum);

    --3-to-1 mux to select a number to display
    with btn select
    mout <= sw(3 downto 0) when "00", --a
    sw(7 downto 4) when "01", --b
    sum when others;

    --magnitude display on rightmost 7-seg led0
    oct <= '0' & mout(2 downto 0);
    sseg_unit: entity work.hex_to_sseg
        port map(hex => oct, dp => '0', sseg => led0);
    --sign display on 2nd 7-seg led0

    led1 <= "11111110" when mout(3) = '1' else --middle bar
        "11111111";
        --other tw0 7-seg leds blank
        led2 <= "11111111";
        led3 <= "11111111";

        --instantiate display multiplexer
        disp_unit: entity work.disp_mux
        port map(
        clk => clk, reset => '0', in0 => led0, in1 => led1,
        in2 => led2, in3 => led3, an => an, sseg => sseg);
    end arch;

DISPLAY MUX
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity disp_mux is port(
    clk, reset: in std_logic;
    in3, in2, in1, in0: in std_logic_vector(7 downto 0);
    an : out std_logic_vector(3 downto 0);
    sseg: out std_logic_vector(7 downto 0));
end disp_mux;

architecture arch of disp_mux is
    --refreshing rate around 800hz (50Mhz/2^16)
    constant n : integer := 18;
    signal q_reg, q_next: unsigned(n-1 downto 0);
    signal sel: std_logic_vector(1 downto 0);
begin
    --register
    process(clk,reset)
    begin
        if reset = '1' then
        q_reg <= (others => '0');
        elsif (clk'event and clk ='1')then
        q_reg <= q_next;
        end if;
    end process;

    --next-state logic for the counter
    q_next <= q_reg + 1;

    --2 MSBs of counter to control 4-to-1 multiplexing
    --and to generate active-low enable signal
    sel <= std_logic_vector(q_reg(n-1 downto n-2));
    process(sel, in0, in1, in2, in3)
    begin
        case sel is
        when "00" =>
        an <= "1110";
        sseg <= in0;
        when "01" =>
        an <= "1101";
        sseg <= in1;
        when "10" =>
        an <= "1011";
        sseg <= in2;
        when others =>
        an <= "0111";
        sseg <= in3;
        end case;
    end process;
end arch;

HEX TO SEVEN SEGMENT
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity hex_to_sseg_test is port(
    clk : in std_logic;
    sw : in std_logic_vector(7 downto 0);
    an : out std_logic_vector(3 downto 0);
    sseg: out std_logic_vector(7 downto 0));
end hex_to_sseg_test;

architecture arch of hex_to_sseg_test is
    signal inc: std_logic_vector(7 downto 0);
    signal led3, led2, led1, led0 : std_logic_vector(7 downto 0);
begin
    --increment input
    inc <= std_logic_vector(unsigned(sw) +1);
    --instantiate four instaces of hex decoders

    --instance for 4 lsbs of input
    sseg_unit_0: entity work.hex_to_sseg
        port map(hex => sw(3 downto 0), dp => '0', sseg => led0);
    --instance for 4 msbs of input
    sseg_unit_1: entity work.hex_to_sseg
        port map(hex => sw(7 downto 4), dp => '0', sseg => led1);
    --instance for 4 lsbs of input
    sseg_unit_2: entity work.hex_to_sseg
        port map(hex => sw(3 downto 0), dp => '1', sseg => led2);
    --instance for 4 msbs of input
    sseg_unit_3: entity work.hex_to_sseg
        port map(hex => sw(7 downto 4), dp => '1', sseg => led3);

    --instantiate 7-seg led display time-multiplexing module
    disp_unit: entity work.disp_mux
        port map(
        clk => clk, reset => '0',
        in0 => led0, in1 => led1, in2 => led2, in3 => led3,
        an => an, sseg => sseg);
end arch;

BARREL SHIFTER
library ieee;
    use ieee.std_logic_1164.all;

entity barrel_shifter is port (
    a : in std_logic_vector(7 downto 0);
    amt : in std_logic_vector(2 downto 0);
    y: out std_logic_vector(7 downto 0));
end barrel_shifter;

--architecture sel_arch of barrel_shifter is
--begin
-- with amt select
-- y <= a when "000",
-- a(0) & a(7 downto 1) when "001",
-- a(1 downto 0) & a(7 downto 2) when "010",
-- a(2 downto 0) & a(7 downto 3) when "011",
-- a(3 downto 0) & a(7 downto 4) when "100",
-- a(4 downto 0) & a(7 downto 5) when "101",
-- a(5 downto 0) & a(7 downto 6) when "110",
-- a(6 downto 0) & a(7) when others; --111

architecture multi_stage_arch of barrel_shifter is
    signal s0, s1: std_logic_vector(7 downto 0);
begin
    -- stage 0, shift 0 or 1 bit
    s0 <= a(0) & a(7 downto 1) when amt(0) = '1' else
        a;
        --stage 1, shift 0 or 2 bits
        s1 <= s0(1 downto 0) & s0(7 downto 2) when amt(1) = '1' else
        s0;
        -- stage 2, shift 0 or 4 bits
        y <= s1(3 downto 0) & s0(7 downto 4) when amt(2) = '1' else
        s1;
        end multi_stage_arch;

--parameterized register file
--the write address signal, w_addr, specifies where to store data,
--and the read address signal, r_addr, specifies where to retrieve data.
--the register file is generally used ads fast temporary storage. This
--code is for 2^w - by b parameterized register file.

REGISTER FILE
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity reg_file is generic(
    b: integer := 8; --use integer to define generic number of bits
    w: integer := 2); --use integer to define generic number of address bits
port( clk, reset: in std_logic;
      wr_en: in std_logic;
      w_addr, r_addr, r_addr_2: in std_logic_vector(w-1 downto 0);
      w_data: in std_logic_vector(b-1 downto 0);
      r_data, r_data2: out std_logic_vector(b-1 downto 0));
end reg_file;

architecture arch of reg_file is
    type reg_file_type is array (2**w-1 downto 0) of std_logic_vector(b-1 downto 0);
    signal array_reg: reg_file_type;
begin
    process(clk, reset)
    begin
        if(reset = '1') then
        array_reg <= (others => (others => '0'));
        elsif rising_edge(clk) then
        if wr_en = '1' then
        array_reg(to_integer(unsigned(w_addr))) <= w_data; -- address decoder
        end if;
        end if;
    end process;
    --read port
    r_data <= array_reg(to_integer(unsigned(r_addr))); -- data multiplexing
    r_data2 <= array_reg(to_integer(unsigned(r_addr_2))); -- data multiplexing
end arch;

FREE RUN SHIFT REGISTER
library ieee;
    use ieee.std_logic_1164.all;

entity free_run_shift_reg is port(
    reset, d, clk : in std_logic;
    q : out std_logic);
end free_run_shift_reg;

architecture arch of free_run_shift_reg is
    signal r_reg, r_next : std_logic_vector(7 downto 0);
begin
    process(clk, reset)
    begin
        if (reset = '1') then
        r_reg <= (others => '0');
        elsif rising_edge(clk) then
        r_reg <= r_next;
        end if;
    end process;

    r_next <= d & r_reg(7 downto 1);
    q <= r_reg(0);

end arch;

library ieee;
    use ieee.std_logic_1164.all;

entity univ_shift_reg is port(
    clk, rst, en : in std_logic;
    ctrl : in std_logic_vector(1 downto 0);
    din : in std_logic_vector(7 downto 0);
    dout : out std_logic_vector(7 downto 0));
end univ_shift_reg;

architecture arch of univ_shift_reg is
    signal r_reg, r_next : std_logic_vector(7 downto 0);
begin
    process(clk, rst)
    begin
        if rst = '1' then
        r_reg <= (others => '0');
        elsif rising_edge (clk) then
        if en = '1' then
        r_reg <= r_next;
        end if;
        end if;
    end process;

    with ctrl select
    r_next <=
    r_reg when "00", -- no op
    r_reg (6 downto 0) & din(0) when "01", -- shift_left
    din(7) & r_reg(7 downto 1) when "10", --shift_right
    din when others; -- load

    --output
    dout <= r_reg;
end arch;

UNIVERSAL SHIFT REGISTER
library ieee;
    use ieee.std_logic_1164.all;

entity univ_shift_reg is port(
    clk, rst, en1, en2 : in std_logic;
    ctrl, ctrl1 : in std_logic;
    sin : in std_logic;
    din : in std_logic_vector(7 downto 0);
    sout, sout2 : out std_logic);
end univ_shift_reg;

architecture arch of univ_shift_reg is
    signal r_reg, r_next : std_logic_vector(7 downto 0);
    signal r_reg_1, r_next_1 : std_logic_vector(7 downto 0);
    signal dout : std_logic_vector(7 downto 0);
begin

    process(clk, rst)
    begin
        if rst = '1' then
        r_reg <= (others => '0');
        elsif rising_edge (clk) then
        if en1 = '1' then
        r_reg <= r_next;
        end if;
        end if;
    end process;

    r_next <= din when (ctrl = '1') else -- no op
        sin & r_reg(7 downto 1); --shift_right
        --output
        sout <= r_reg(0);

        process(clk, rst)
        begin
        if rst = '1' then
        r_reg_1 <= (others => '0');
        elsif rising_edge (clk) then
        if en2 = '1' then
        r_reg_1 <= r_next_1;
        end if;
        end if;
        end process;

        r_next_1 <= r_reg when (ctrl1 = '1') else -- no op
        '0' & r_reg_1(7 downto 1); --shift_right
        --output
        sout2 <= r_reg_1(0);

        end arch;

FREE RUNNING BINARY COUNTER
-- A free running binary counter circulates through a binary sequence repeatedly.
--For example, a 4-bit binary counter counts from "0000" to "1111" and wraps around.
--The next state logic is an incrementor which adds 1 to the register's current vlaue.
--By definition of the + operator in the numeric_std package, the operation
--implicitly wraps around after the r_reg reaches "1111". The circuit also outputs
--status - max_tick - which is asserted when the counter reaches the maximal value
--which is equal to 2^n-1 and deaserrted when value is "0000". The max_tick signal
--represents a special type of signal that is asserted from a single clock cycle.

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity free_run_bin_counter is
    generic( n: integer := 7);
    port( clk, rst: in std_logic;
        max_tick: out std_logic;
        q: out std_logic_vector(n downto 0));
end free_run_bin_counter;

architecture arch of free_run_bin_counter is
    signal r_reg, r_next : unsigned(7 downto 0);
begin

    process(clk, rst)
    begin
        if rst = '1' then
        r_reg <= (others => '0');
        elsif rising_edge (clk) then
        r_reg <= r_next;
        end if;
    end process;

    r_next <= r_reg + 1;

    max_tick <= '1' when r_reg = (2**8 -1) else '0';
    q <= std_logic_vector(r_reg);
end arch;

MOD-M COUNTER
--example of pwm
--a mod-m counter counts from 0 to m-1 and wraps around. generic m specifies the
--limit and n specifies the number of bits needed and should be equal to [log2 m]

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity mod_m_counter is
    generic( m : integer := 10; --number of bits
        n : integer := 4); --mod-m
    port( clk, rst : in std_logic;
        max_tick : out std_logic;
        q : out std_logic_vector(n-1 downto 0));
end mod_m_counter;

architecture arch of mod_m_counter is
    signal r_reg, r_next : unsigned(n-1 downto 0);
begin

    process(clk, rst)
    begin
        if rst = '0' then
        r_reg <= (others => '0');
        elsif rising_edge(clk) then
        r_reg <= r_next;
        end if;
    end process;
    --next state logic
    -- the next state logic is constructed by a conditional signal assignment statement.
    -- If the counter reaches m-1 the new value is cleared to 0. otherwise it is incremented by 1.
    r_next <= (others => '0') when r_reg = m-1 else r_reg +1;

    --output logic
    q <= std_logic_vector(r_reg);
    max_tick <= '1' when r_reg = m-1 else '0';

end arch;

BINARY COUNTER - TESTBENCH

library ieee;
    use ieee.std_logic_1164.all;

entity bin_counter_tb is
end bin_counter_tb;

architecture arch of bin_counter_tb is
    constant three : integer := 3;

    --since the operation of a synchronous system is synced by a clock signal,
    --we define a constant with a built in data type time for the clock period:
    constant t: time := 20 ns; -- clk period

    signal clk, rst : std_logic;
    signal syn_clr, load, en, up: std_logic;
    signal d: std_logic_vector(three -1 downto 0);
    signal max_tick, min_tick: std_logic;
    signal q: std_logic_vector(three -1 downto 0);
begin
    --instatiation
    --the code consists of a component instatiation statement, which creates an
    --instance of a 3-bit counter and three segments which generate a stimulus for a
    --clock, reset, and regular inputs.

    counter_unit: entity work.univ_bit_counter(arch)
        generic map( n => three)
        port map(clk => clk, rst => rst, syn_clr => syn_clr,
        load => load, en => en, up => up, d => d,
        max_tick => max_tick, min_tick => min_tick,
        q => q);

    --clock
    --20 ns clock running forever
    --the clock generation is specified by a process:
    --the clk signal is assigned between '0' and '1' alternativley,
    --and each value lasts for half a period. note that the process has no
    --sensitivity list and repeats itself forever.
    process
    begin
        clk <= '0';
        wait for t/2;
        clk <= '1';
        wait for t/2;
    end process;

    --reset
    --reset assert for t/2
    rst <= '1', '0' after t/2;

    --other stimulus
    process
    begin
        --initial input
        syn_clr <= '0';
        load <= '0';
        en <= '0';
        up <= '1'; --count up
        d <= (others => '0');

        --DIN WASALT GHALIJA WAHDI GHAX BIL BAJT. For a synchronous system with positive
        -- edge triggered FFs an input signal must be stable around the rising_edge to satisfy
        -- the setup and hold time constraints. one way is to change an input signal during
        -- the falling edge.
        wait until falling_edge(clk);
        wait until falling_edge(clk);
        --test load
        load <= '1';
        d <= "011";
        wait until falling_edge(clk);
        load <= '0';
        --pause 2 clocks
        wait until falling_edge(clk);
        wait until falling_edge(clk);
        --test syn_clr
        syn_clr <= '1'; -- clear
        wait until falling_edge(clk);
        syn_clr <= '0';
        --test up counter and pause
        en <= '1'; -- count
        up <= '1';
        for i in 1 to 10 loop -- count 10 clocks
        wait until falling_edge(clk);
        end loop;
        en <= '0';
        wait until falling_edge(clk);
        wait until falling_edge(clk);
        en <= '1';
        wait until falling_edge(clk);
        wait until falling_edge(clk);
        --test down counter
        up <= '0';
        for i in 1 to 10 loop -- run 10 clocks
        wait until falling_edge(clk);
        end loop;
        --other wait conditions
        --continue until q=2

        -- wait until a special condition
        wait until q = "010";
        wait until falling_edge(clk);
        up <= '1';
        --continue until min_tick changes value

        --wait until a signal changes
        wait on min_tick;
        wait until falling_edge(clk);
        up <= '0';
        wait for 4*t; --wait for 80ns
        en <= '0';
        wait for 4*t;
        --terminate simulation
        --an additional assertion statement is added to the end of the process.
        --It generates an " artificial failure" and stops the simulation
        assert false
        report "Simulation Completed"
        severity failure;

    end process;
end arch;

DIPLAY MUX - TESTBENCH
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.math_real.all;

entity disp_mux_tb is
end entity;

architecture arch of disp_mux_tb is

    constant t : time := 1302.083333 ns;
    signal clk, reset: std_logic;
    signal in3, in2, in1, in0: std_logic_vector(7 downto 0);
    signal an : std_logic_vector(3 downto 0);
    signal sseg: std_logic_vector(7 downto 0);
begin

    uut: entity work.disp_mux(arch)
        port map ( clk => clk, reset => reset, in3 => in3,
        in2 => in2, in1 => in1, in0 => in0, an => an, sseg => sseg);

    process
    begin
        clk <= '0';
        wait for t/2;
        clk <= '1';
        wait for t/2;
    end process;

    process
    begin
        reset <= '1';
        wait for t *2;
        wait for t *2;
        reset <= '0';

        wait until an = "0111";
        wait for t *2;
        wait for t *2;
        wait until an = "0111";
        wait for t *2;
        wait for t *2;

        assert false
        report "Simulation Completed"
        severity failure;

    end process;

end arch;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity disp_mux_test is port(
    clk: in std_logic;
    btn: in std_logic_vector(3 downto 0);
    sw: in std_logic_vector(7 downto 0);
    an: out std_logic_vector(3 downto 0);
    sseg: out std_logic_vector(7 downto 0));
end disp_mux_test;

architecture arch of disp_mux_test is
    signal d3_reg, d2_reg, d1_reg, d0_reg: std_logic_vector(7 downto 0);
begin

    disp_unit : entity work.disp_mux
        port map ( clk => clk, reset => '0', in3 => d3_reg, in2 => d2_reg,
        in1 => d1_reg, in0 => d0_reg, an => an, sseg => sseg);
    --registers for 4 led patterns

    process(clk)
    begin
        if rising_edge(clk) then
        if btn(3) = '1' then
        d3_reg <= sw;
        end if;

        if btn(2) = '1' then
        d2_reg <= sw;
        end if;

        if btn(1) = '1' then
        d1_reg <= sw;
        end if;

        if btn(0) = '1' then
        d0_reg <= sw;
        end if;
        end if;
    end process;
end arch;

DISPLAY HEX MUX
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity disp_hex_mux is port(
    clk, rst : in std_logic;
    hex3, hex2, hex1, hex0 : in std_logic_vector(3 downto 0);
    dp_in: in std_logic_vector(3 downto 0);
    an : out std_logic_vector(3 downto 0);
    sseg: out std_logic_vector(7 downto 0));

end disp_hex_mux;

architecture arch of disp_hex_mux is
    --each 7-seg led enabled (2^18/4) * 25 ns (40 ms)
    constant n: integer := 18;
    signal q_reg, q_next: unsigned (n-1 downto 0);
    signal sel: std_logic_vector(1 downto 0);
    signal hex: std_logic_vector(3 downto 0);
    signal dp: std_logic;
begin
    --register
    process(clk,rst)
    begin
        if rst = '1' then
        q_reg <= (others => '0');
        elsif rising_edge(clk) then
        q_reg <= q_next;
        end if;
    end process;

    --next state logic for the conter
    q_next <= q_reg +1;

    --2 MSBs of counter to control 4-to-1 muxing
    sel <= std_logic_vector(q_reg(n-1 downto n-2));

    process(sel)--, hex0, hex1, hex2, hex3, dp_in)
    begin
        case sel is
        when "00" =>
        an <= "1110";
        hex <= hex0;
        dp <= dp_in(0);
        when "01" =>
        an <= "1101";
        hex <= hex1;
        dp <= dp_in(1);
        when "10" =>
        an <= "1011";
        hex <= hex2;
        dp <= dp_in(2);
        when "11" =>
        an <= "0111";
        hex <= hex3;
        dp <= dp_in(3);
        end case;
    end process;

    -- hex to 7 segment led decoding
    with hex select
    sseg(6 downto 0) <=
    "0000001" when "0000",
    "1001111" when "0001",
    "0010010" when "0010",
    "0000110" when "0011",
    "0000110" when "0100",
    "1001100" when "0101",
    "0100100" when "0110",
    "0100000" when "0111",
    "0001111" when "1000",
    "0000000" when "1001",
    "0000100" when "1010",
    "0001000" when "1011",
    "1100000" when "1100",
    "0110001" when "1101",
    "0110000" when "1110",
    "0111000" when others;
    -- decimal point
    sseg(7) <= dp;
end arch;

HEX MUX TESTBENCH

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity hex_mux_test is port(
    clk: in std_logic;
    sw: in std_logic_vector(7 downto 0);
    an: out std_logic_vector(3 downto 0);
    sseg: out std_logic_vector(7 downto 0));
end entity;

architecture arch of hex_mux_test is
    signal a, b: unsigned(7 downto 0);
    signal sum: std_logic_vector(7 downto 0);
begin
    disp_unit: entity work.disp_hex_mux
        port map( clk => clk, rst => '0',
        hex3 => sum(7 downto 4), hex2 => sum(3 downto 0),
        hex1 => sw(7 downto 4), hex0 => sw(3 downto 0),
        dp_in => "1011", an => an, sseg => sseg);

    a <= "0000" & unsigned(sw(3 downto 0));
    b <= "0000" & unsigned(sw(7 downto 4));
    sum<= std_logic_vector(a + b);
end arch;

STOP WATCH
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity stopwatch is port(
    clk : in std_logic;
    go, clr: in std_logic;
    d2, d1, d0: out std_logic_vector(3 downto 0));
end stopwatch;

architecture cascade_arch of stopwatch is
    constant dvsr : integer := 5000000;
    signal ms_reg, ms_next: unsigned(22 downto 0);
    signal d2_reg, d1_reg, d0_reg: unsigned(3 downto 0);
    signal d2_next, d1_next, d0_next: unsigned(3 downto 0);
    signal d1_en, d2_en, d0_en: std_logic;
    signal ms_tick, d0_tick, d1_tick: std_logic;
begin
    --register
    process(clk)
    begin
        if rising_edge(clk) then
        ms_reg <= ms_next;
        d2_reg <= d2_next;
        d1_reg <= d1_next;
        d0_reg <= d0_next;
        end if;
    end process;

    --next-state logic
    --0.1 sec tick generator: mod-5000000

    ms_next <= (others => '0') when clr = '1' or (ms_reg = dvsr and go = '1') else
        ms_reg + 1 when go = '1' else
        ms_reg;

        ms_tick <= '1' when ms_reg = dvsr else '0';

    --0.1 sec counter
    d0_en <= '1' when ms_tick = '1' else '0';
    d0_next <= "0000" when (clr = '1') or (d0_en = '1' and d0_reg = 9) else
        d0_reg + 1 when d0_en = '1' else d0_reg;

        d0_tick <= '1' when d0_reg = 9 else '0';

    --1 sec counter
    d1_en <= '1' when ms_tick = '1' and d0_tick = '1' else '0';
    d1_next <= "0000" when (clr = '1') or (d1_en = '1' and d1_reg = 9) else
        d1_reg + 1 when d1_en = '1' else d1_reg;

        d1_tick <= '1' when d1_reg = 9 else '0';

    --10 sec counter
    d2_en <= '1' when ms_tick = '1' and d1_tick = '1' else '0';
    d2_next <= "0000" when (clr = '1') or (d2_en = '1' and d2_reg = 9) else
        d2_reg + 1 when d2_en = '1' else d2_reg;

    --output logic
    d0 <= std_logic_vector(d0_reg);
    d2 <= std_logic_vector(d2_reg);
    d1 <= std_logic_vector(d1_reg);
end cascade_arch;

--architecture if_arch of stopwatch is
-- constant dvsr : integer := 5000000;
-- signal ms_reg, ms_next: unsigned (22 downto 0);
-- signal d2_reg, d1_reg, d0_reg: unsigned(3 downto 0);
-- signal d2_next, d1_next, d0_next: unsigned(3 downto 0);
-- signal ms_tick: std_logic;
--begin
-- --register
-- process(clk)
-- begin
-- if rising_edge(clk) then
-- ms_reg <= ms_next;
-- d2_reg <= d2_next;
-- d1_reg <= d1_next;
-- d0_reg <= d0_next;
-- end if;
-- end process;
--
-- ms_next <= (others => '0') when clr = '1' or (ms_reg = dvsr and go = '1') else
-- ms_reg + 1 when go = '1' else
-- ms_reg;
--
-- ms_tick <= '1' when ms_reg = dvsr else '0';
--
-- --3-digit incrementor
-- process(d0_reg, d1_reg, d2_reg, ms_tick, clr)
-- begin
-- --default
-- d0_next <= d0_reg;
-- d1_next <= d1_reg;
-- d2_next <= d2_reg;
-- if clr = '1' then
-- d0_next <= "0000";
-- d0_next <= "0000";
-- d0_next <= "0000";
-- elsif ms_tick = '1' then
-- if(d0_reg /= 9) then
-- d0_next <= d0_reg + 1;
-- else -- reach XX9
-- d0_next <= "0000";
-- if(d1_reg /= 9) then
-- d1_next <= d1_reg + 1;
-- else -- reach X99
-- d1_next <= "0000";
-- if(d2_reg /= 9) then
-- d2_next <= d2_reg + 1;
-- else -- reach 999
-- d2_next <= "0000";
-- end if;
-- end if;
-- end if;
-- end if;
-- end process;
--
-- --output logic
-- d0 <= std_logic_vector(d0_reg);
-- d2 <= std_logic_vector(d2_reg);
-- d1 <= std_logic_vector(d1_reg);
--end if_arch;
--
--
--

FIFO
--A FIFO buffer is an elastic storage between two subsystems. It has two control
--signals, wr and rd for write and read operations. When wr is asserted, the input
--data is written into the buffer. The head of the FIFO buffer is normally always
--available to read at any time. The rd signal actually acts a remove signal. When
--it is asserted the first item is removed of the buffer and the next item becomes
--available.
--
--The registers in the register file are arranges as a circular queue with two pointers.
--The write pointer points to the head of the queue, and the read pointer points to the
--tail of the queue. The pointer advances one position for each write or read operation.
--Two status signals, full and empty, are used to indicate the buffer is full and cant be
--written or empty and cant be read. One of the two conditions occurs when both signals
--are equal.
--
--One scheme to distinguish between conditions is to use two ffs to keep track of the empty
--and full statuses. These ffs are set to '1' and '0' during system initialization and then
--modified in each clock cycle according to the values of the wr and rd signals.
--
--The code is divided into a register file and a fifo controller. Considering the ???10??? case,
--which implies that only a write operation occurs. The status ff is checked first to ensure
--that the buffer is not full. If the condition is met, we advance the write pointer by one
--position and clear the empty status ff. Storing one extra word to the buffer may make it full.
--This happens if the new write pointer ???catches??? the read pointer, which is expressed by the
--w_ptr_succ = r_ptr_reg expression.

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity fifo is
    generic( b: natural := 8; -- number of bits
        w: natural := 4); -- number of address bits
    port( clk, rst: in std_logic;
        rd, wr: in std_logic;
        w_data: in std_logic_vector(b-1 downto 0);
        r_data: out std_logic_vector(b-1 downto 0);
        empty, full: out std_logic);
end fifo;

architecture arch of fifo is
    type reg_file_type is array (2**w -1 downto 0) of std_logic_vector(b-1 downto 0);
    signal array_reg : reg_file_type;
    signal w_ptr_reg, w_ptr_next, w_ptr_succ : std_logic_vector (w-1 downto 0);
    signal r_ptr_reg, r_ptr_next, r_ptr_succ : std_logic_vector (w-1 downto 0);
    signal full_reg, empty_reg, full_next, empty_next, wr_en : std_logic;
    signal wr_op: std_logic_vector(1 downto 0);
begin
    --register file
    process(clk, rst)
    begin
        if(rst = '1') then
        array_reg <= (others => (others => '0'));
        elsif rising_edge(clk) then
        if wr_en = '1' then
        array_reg(to_integer(unsigned(w_ptr_reg))) <= w_data;
        end if;
        end if;
    end process;

    --read port
    r_data <= array_reg(to_integer(unsigned(r_ptr_reg)));
    --write enabled only when fifo is not full
    wr_en <= wr and (not full_reg);

    --fifo control logic
    --register for read and write pointers
    process(clk, rst)
    begin
        if(rst = '1')then
        w_ptr_reg <= (others => '0');
        r_ptr_reg <= (others => '0');
        full_reg <= '0';
        empty_reg <= '1';

        elsif rising_edge(clk)then
        w_ptr_reg <= w_ptr_next;
        r_ptr_reg <= r_ptr_next;
        full_reg <= full_next;
        empty_reg <= empty_next;
        end if;
    end process;

    --successive pointer values
    w_ptr_succ <= std_logic_vector(unsigned(w_ptr_reg) + 1);
    r_ptr_succ <= std_logic_vector(unsigned(r_ptr_reg) + 1);

    --next state logic for read and write pointers
    wr_op <= wr & rd;
    process(w_ptr_reg, w_ptr_succ, r_ptr_reg, r_ptr_succ, wr_op, empty_reg, full_reg)
    begin
        w_ptr_next <= w_ptr_reg;
        r_ptr_next <= r_ptr_reg;
        full_next <= full_reg;
        empty_next <= empty_reg;

        case wr_op is
        when "00" => --no op
        when "01" => --read
        if(empty_reg /= '1') then --not empty
        r_ptr_next <= r_ptr_succ;
        full_next <= '0';
        if(r_ptr_succ = w_ptr_succ) then
        empty_next <= '1';
        end if;
        end if;
        when "10" => -- write
        if(full_reg /= '1') then --not full
        w_ptr_next <= w_ptr_succ;
        empty_next <= '0';
        if (w_ptr_succ = r_ptr_reg) then
        full_next <= '1';
        end if;
        end if;
        when others => -- write/read
        w_ptr_next <= w_ptr_succ;
        r_ptr_next <= r_ptr_succ;
        end case;
    end process;
    --output
    full <= full_reg;
    empty <= empty_reg;
end arch;

FIFO -TESTBENCH
library ieee;
    use ieee. std_logic_1164.all;
    use ieee.numeric_std.all;

entity fifo_tb is
    generic( b: natural := 8; -- number of bits
        w: natural := 4); -- number of address bits
end entity;

architecture arch_tb of fifo_tb is
    signal clk, rst: std_logic;
    signal rd, wr: std_logic;
    signal w_data: std_logic_vector(b-1 downto 0);
    signal r_data: std_logic_vector(b-1 downto 0);
    signal empty, full: std_logic;
    constant t : time := 100 ps;
begin
    fifo_unit: entity work.fifo(arch)
        port map( clk => clk, rst => rst, rd => rd, wr => wr,
        w_data => w_data, r_data => r_data, empty => empty,
        full => full);
    process
    begin
        clk <= '1';
        wait for t/2;
        clk <= '0';
        wait for t/2;
    end process;

    process
    begin

        rst <= '1';
        wait until falling_edge(clk);
        rst <= '0';

        wr <= '1';
        rd <= '0';
        w_data <= "00010010"; --18
        wait until falling_edge(clk);
        w_data <= "00010100"; --20
        wait until falling_edge(clk);
        w_data <= "00000100"; --4
        wait until falling_edge(clk);
        -- wr <= '0';
        -- rd <= '1';
        -- wait until falling_edge(clk);
        -- wait until falling_edge(clk);
        -- rd <= '0';
        -- wr <= '1';
        w_data <= "00001100"; --12
        wait until falling_edge(clk);
        w_data <= "00010011"; --19
        wait until falling_edge(clk);
        w_data <= "00010110"; --22
        wait until falling_edge(clk);
        w_data <= "00100011"; --35
        wait until falling_edge(clk);
        w_data <= "00111111"; --63
        -- rd <= '1';
        wait until falling_edge(clk);
        w_data <= "01001110"; --78
        wait until falling_edge(clk);
        w_data <= "01010001"; --81
        wait until falling_edge(clk);
        w_data <= "00000101"; --5
        wait until falling_edge(clk);
        w_data <= "01011101"; --93
        wait until falling_edge(clk);
        w_data <= "01100011"; --99
        wait until falling_edge(clk);
        w_data <= "01101110"; --110
        wait until falling_edge(clk);
        w_data <= "01010101"; --84
        wait until falling_edge(clk);
        w_data <= "10000101"; --133
        wait until falling_edge(clk);
        w_data <= "11011101"; --221
        wait until falling_edge(clk);
        w_data <= "01101011"; --107
        wait until falling_edge(clk);

        assert false
        report "simulation completed"
        severity failure;
    end process;
end arch_tb;

FSM
library ieee;
    use ieee.std_logic_1164.all;

entity eg_fsm is port(
    a, b: in std_logic;
    clk, rst: in std_logic;
    y0, y1: out std_logic);
end eg_fsm;

architecture arch of eg_fsm is
    type fsm is (s0, s1, s2);
    signal state_reg, state_next: fsm;
begin
    --state register
    process(clk, rst)
    begin
        if rst = '1' then
        state_reg <= s0;
        elsif rising_edge(clk) then
        state_reg <= state_next;
        end if;
    end process;

    --next state logic
    process(state_reg, a, b)
    begin
        case state_reg is
        when s0 =>
        if a = '1' then
        if b = '1' then
        state_next <= s2;
        else state_next <= s1;
        end if;
        else state_next <= s0;
        end if;
    when s1 =>
        if a = '1' then
        state_next <= s0;
        else
        state_next <= s1;
        end if;
    when s2 =>
        state_next <= s0;
        end case;
    end process;

    --moore output logic
    process(state_reg)
    begin
        case state_reg is
        when s0 | s2 => y1 <= '0';
        when s1 => y1 <= '1';
        end case;
    end process;

    --mealy output logic
    process(state_reg, a, b)
    begin
        case state_reg is
        when s0 =>
        if (a = '1') and (b = '1') then
        y0 <= '1';
        else y0 <= '0';
        end if;
        when s1 | s2 => y0 <= '0';
        end case;
    end process;
end arch;
--The key part is the next-state logic. it uses a case statement with
--the state_reg signal as the selection expressiom. The next state signal
--is determined by the current state and external input.

library ieee;
    use ieee.std_logic_1164.all;

entity two_eg_fsm is port(
    a, b: in std_logic;
    clk, rst: in std_logic;
    y0, y1: out std_logic);
end two_eg_fsm;

architecture arch of two_eg_fsm is
    type fsm is (s0, s1, s2);
    signal state_reg, state_next: fsm;
begin
    --state register
    process(clk,rst)
    begin
        if rst = '1' then
        state_reg <= s0;
        elsif rising_edge(clk) then
        state_reg <= state_next;
        end if;
    end process;

    --next-state / output logic
    process(state_reg, a, b)
    begin
        state_next <= state_reg; -- default back to same state;
        y0 <= '0'; -- defailts 0
        y1 <= '0';

        case state_reg is
        when s0 =>
        if a = '1' then
        if b = '1' then
        state_next <= s2;
        y0 <= '1';
        else state_next <= s1;
        end if;
        --no else branch
        end if;
        when s1 => y1 <= '1';
        if a = '1' then
        state_next <= s0;
        -- no else branch
        end if;
    when s2 => state_next <= s0;
        end case;
    end process;
end arch;

EDGE DETECT
library ieee;
    use ieee.std_logic_1164.all;

entity edge_detect is port(
    clk, rst: in std_logic;
    level: in std_logic;
    tick: out std_logic);
end edge_detect;

--moore architecture
--architecture moore_arch of edge_detect is
-- type fsm is (zero, edge, one);
-- signal state_reg, state_next: fsm;

--mealy architecture
architecture moore_arch of edge_detect is
    type fsm is (zero, one);
    signal state_reg, state_next: fsm;
    signal q, z: std_logic;
begin
    process(clk, rst)
    begin
        if rst = '1' then
        state_reg <= zero;
        elsif rising_edge(clk) then
        state_reg <= state_next;
        end if;
    end process;

    -- --moore machine
    -- process(state_reg, level)
    -- begin
    -- -- state_next <= state_reg; --stay in the current state until utherwise told
    -- tick <= '0';
    -- -- tick goes one when level is one and clock is rising edge
    -- case state_reg is
    -- when zero =>
    -- if level = '1' then
    -- state_next <= edge;
    -- end if;
    -- when edge => tick <= '1';
    -- if level = '1' then
    -- state_next <= one;
    -- else state_next <= zero;
    -- end if;
    -- when one =>
    -- if level = '0' then
    -- state_next <= zero;
    -- end if;
    -- end case;
    -- end process;

    --mealy machine
    -- process(state_reg, level)
    -- begin
    -- state_next <= state_reg;
    -- tick <= '0';
    --
    -- case state_reg is
    -- when zero =>
    -- if level = '1' then
    -- state_next <= one;
    -- tick <= '1';
    -- end if;
    -- when one =>
    -- if level = '0' then
    -- state_next <= zero;
    -- end if;
    -- end case;
    -- end process;

    -- gate level implementaion of an edge detector
    process(clk)
    begin
        if rising_edge(clk) then
        q <= level;
        z <= (not q) and level;
        end if;

    end process;

    tick <= z;
end moore_arch;

library IEEE;
    use IEEE.STD_LOGIC_1164.all;
    use IEEE.NUMERIC_STD.all;

entity delay_increment is
    generic ( delay_ports : natural := 3;
        width_ports : natural := 3);
    port ( clk,reset: in STD_LOGIC;
        update : in STD_LOGIC;
        in_data : in STD_LOGIC_VECTOR (7 downto 0);
        led : out STD_LOGIC_VECTOR (2 downto 0);
        out_data : out STD_LOGIC_VECTOR (7 downto 0);
        d_big,d_mini,d_opo : out STD_LOGIC_VECTOR (25 downto 0);
        w_big,w_mini,w_opo : out STD_LOGIC_VECTOR (25 downto 0));
end delay_increment;

architecture fsm_arch of delay_increment is
    type state_type is (idle,channel,d_or_w,delay_channel,delay_channel_inc,width_channel,width_channel_inc);
    type delay_file_type is array (delay_ports-1 downto 0) of unsigned (25 downto 0);
    type width_file_type is array(width_ports-1 downto 0) of unsigned (25 downto 0);
    signal d_reg, d_succ: delay_file_type;
    signal w_reg, w_succ: width_file_type;
    signal state_reg : state_type;
    signal which_channel : natural;

    function to_slv(C : Character) return STD_LOGIC_VECTOR is
    begin
        return STD_LOGIC_VECTOR(to_unsigned(Character'pos(c),8));
    end to_slv;

    function "=" (A : STD_LOGIC_VECTOR(7 downto 0); B : Character)
        return boolean is
    begin
        return (A = to_slv(B));
    end function "=";

begin

    --------------------------------------
    --State Machine
    --------------------------------------
    process(clk,reset)
    begin
        if reset='1' then
        state_reg <= idle;
        d_reg <= (others => (others => '0'));
        w_reg <= (others => (others => '0'));
        which_channel <= 0;
        elsif rising_edge(clk) then
        -- default actions ... update if asked
        if update ='1' then
        d_reg <= d_succ;
        w_reg <= w_succ;
        end if;
        case state_reg is
        when idle =>
        if in_data = 'c' then
        state_reg <= channel;
        which_channel <= 0;
        end if;
        when channel =>
        if (Character'pos('0') <= unsigned(in_data)) and (unsigned(in_data)<= Character'pos('9')) then
        which_channel <= (to_integer(unsigned(in_data)) - Character'pos('0'));
        state_reg <= d_or_w;
        elsif in_data = '#' then
        state_reg <= idle;
        which_channel <= which_channel;
        end if;
        when d_or_w =>
        if in_data = 'd' then
        state_reg <= delay_channel;
        elsif in_data = 'w' then
        state_reg <= width_channel;
        elsif in_data = '#' then
        state_reg <= idle;
        end if;
        when delay_channel =>
        if in_data = 'i' then
        state_reg <= delay_channel_inc;
        elsif in_data = '#' then
        state_reg <= idle;
        end if;
        when delay_channel_inc =>
        if in_data = 'u' then
        d_succ(which_channel) <= d_reg(which_channel) + 250;
        state_reg <= idle;
        elsif in_data = 'd' then
        d_succ(which_channel) <= d_reg(which_channel) - 250;
        state_reg <= idle;
        else
        d_succ(which_channel) <= d_reg(which_channel); -- wait for any of 'u', 'd', '#'
        end if;
        if in_data = '#' then
        state_reg <= idle;
        end if;
        when width_channel =>
        if in_data = 'i' then
        state_reg <= width_channel_inc;
        elsif in_data = '#' then
        state_reg <= idle;
        end if;
        when width_channel_inc =>
        if in_data = 'u' then
        w_succ(which_channel) <= w_reg(which_channel) + 250;
        state_reg <= idle;
        elsif in_data = 'd' then
        w_succ(which_channel) <= w_reg(which_channel) - 250;
        state_reg <= idle;
        else
        w_succ(which_channel) <= w_reg(which_channel); -- wait for any of 'u', 'd', '#'
        end if;
        if in_data = '#' then
        state_reg <= idle;
        end if;
        end case;
        end if;
    end process;

    --------------------------------------
    --Output Logic
    --------------------------------------
    d_big <= std_logic_vector(d_reg(0));
    d_mini <= std_logic_vector(d_reg(1));
    d_opo <= std_logic_vector(d_reg(2));
    w_big <= std_logic_vector(w_reg(0));
    w_mini <= std_logic_vector(w_reg(1));
    w_opo <= std_logic_vector(w_reg(2));
end fsm_arch;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity db_fsm is port(
    sw, clk, rst: in std_logic;
    db: out std_logic);
end db_fsm;

architecture arch of db_fsm is
    type fsm is (zero, one, wait0_1, wait0_2, wait0_3, wait1_1, wait1_2, wait1_3);
    signal state_reg, state_next: fsm;
    signal m_tick: std_logic;
    signal count_reg, count_next: unsigned(18 downto 0);
begin

    process(clk)
    begin
        if rst = '1' then
        state_reg <= zero;
        elsif rising_edge(clk) then
        state_reg <= state_next;
        count_reg <= count_next;
        end if;
    end process;

    count_next <= count_reg +1;
    m_tick <= '1' when count_reg = 0 else '0';

    process(state_reg, sw, m_tick)
    begin
        state_next <= state_reg;
        db <= '0';

        case state_reg is
        when zero =>
        if sw = '1' then
        state_next <= wait1_1;
        end if;

        when wait1_1 =>
        if sw = '1' then
        if m_tick = '1' then
        state_next <= wait1_2;
        else state_next <= wait1_1;
        end if;
        else state_next <= zero;
        end if;

    when wait1_2 =>
        if sw = '1' then
        if m_tick = '1' then
        state_next <= wait1_3;
        else state_next <= wait1_2;
        end if;
    else state_next <= zero;
end if;

when wait1_3 =>
    if sw = '1' then
        if m_tick = '1' then
        state_next <= one;
        else state_next <= wait1_3;
    end if;
else state_next <= zero;
end if;

when one => db <= '1';
if sw = '0' then
    state_next <= wait0_1;
end if;

when wait0_1 => db <= '1';
if sw = '0' then
    if m_tick = '1' then
        state_next <= wait0_2;
    else state_next <= wait0_1;
end if;
else state_next <= one;
end if;

when wait0_2 => db <= '1';
if sw = '0' then
    if m_tick = '1' then
        state_next <= wait0_3;
    else state_next <= wait0_2;
end if;
else state_next <= one;
end if;

when wait0_3 => db <= '1';
if sw = '0' then
    if m_tick = '1' then
        state_next <= zero;
    else state_next <= wait0_3;
end if;
else state_next <= one;
end if;

        end case;
    end process;
end arch;

--library ieee;
--
--use ieee.std_logic_1164.all;
--
--entity SReg is
--
--generic ( n : integer := 4);
--
--port( clk: in std_logic;
-- reset: in std_logic;
-- enable: in std_logic; --enables shifting
-- parallel_in: in std_logic_vector(n-1 downto 0);
-- s_in: in std_logic; --serial input
-- s_out: out std_logic --serial output
--
--);
--end SReg;
--
--architecture behavioral of SReg is
--
--signal temp_reg: std_logic_vector(n-1 downto 0) := (Others => '0');
--TYPE POSSIBLE_STATES IS (waiting, shifting);
--signal state : POSSIBLE_STATES;
--begin
--
--process(clk,reset)
-- variable shift_clkdiver: integer := 0;
--begin
--
-- if(reset = '1') then
-- temp_reg <= (others => '0');
-- state <= waiting;
-- shift_clkdiver := 0;
-- elsif(clk'event and clk='1') then
-- case state is
-- when waiting =>
-- shift_clkdiver := 0;
-- temp_reg <= parallel_in;
-- s_out <= '0';
-- if(enable = '1') then
-- state <= shifting;
-- else
-- state <= waiting;
-- end if;
-- when shifting =>
-- shift_clkdiver := shift_clkdiver + 1;
-- s_out <= temp_reg(0);
-- temp_reg <= s_in & temp_reg(n-1 downto 1);
-- if (shift_clkdiver >= n-1) then
-- state <= waiting;
-- else
-- state <= shifting;
-- end if;
-- end case;
-- end if;
--end process;
--
--end behavioral;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity sreg is port(
    din : in std_logic_vector(7 downto 0);
    load: in std_logic;
    dout, tx_busy : out std_logic;
    clk, rst : in std_logic);
end sreg;

architecture arch of sreg is
    constant width_1 : natural := 8;
    constant width_2 : natural := 3;

    signal clkdiv : unsigned(width_1 downto 0);
    signal clkdiv_sum : unsigned(width_1 +1 downto 0);
    signal ticktx : std_logic;
    signal tickbit : std_logic;
    signal load_bitcount : std_logic;
    signal bitcount : unsigned(width_2 downto 0);
    signal bitcount_sum : unsigned(width_2 +1 downto 0);

    signal data_shift : std_logic_vector(9 downto 0);
begin

    clkdiv_sum <= resize(clkdiv,width_1 +2) -1;
    process(clk,rst)
    begin
        if rst = '0' then
        clkdiv <= (others => '0');
        elsif rising_edge(clk) then
        if ticktx = '1' then
        clkdiv <= "110110010";
        else
        clkdiv <= clkdiv_sum(width_1 downto 0);
        end if;
        end if;
    end process;
    ticktx <= clkdiv_sum(width_1 +1);

    bitcount_sum <= resize(bitcount, width_2 +2) -1;
    process(clk, rst)
    begin
        if rst = '0' then
        bitcount <= (others => '0');
        elsif rising_edge(clk) then
        if ticktx = '1' then --enable
        if tickbit = '1' then
        bitcount <= "1001";
        else
        bitcount <= bitcount_sum(width_2 downto 0);
        end if;
        end if;
        end if;
    end process;
    tickbit <= bitcount_sum(width_2 +1);

    process(clk, rst)
    begin
        if rst = '0' then
        data_shift <= (others => '0');
        elsif rising_edge(clk) then
        tx_busy <= '0';
        if ticktx = '1' then
        if load = '1' and tickbit = '1' then
        data_shift <= '1' & din & '0'; --stop bit & data & start bit
        -- load_bitcount <= '1';
        -- elsif tickbit = '1' then
        else
        data_shift <= '1' & data_shift(data_shift'high downto 1);
        end if;
        end if;
        end if;
    end process;

    dout <= data_shift(0);

end arch;

library IEEE;
    use IEEE.STD_LOGIC_1164.all;

entity random_uniform is
    generic ( SEED : STD_LOGIC_VECTOR(30 downto 0):= (others => '0');
        OUT_WIDTH : integer := 11);
    port ( clk : in STD_LOGIC;
        random : out STD_LOGIC_VECTOR (OUT_WIDTH-1 downto 0);
        reset : in STD_LOGIC);
end random_uniform;

architecture Behavioral of random_uniform is

    signal rand : std_logic_vector(30 downto 0) := SEED;
    signal feedback : std_logic;

begin

    feedback <= not((rand(0) xor rand(3)));

    process(clk,reset)
    begin
        if reset = '1' then
        rand <= SEED;
        elsif rising_edge(clk) then
        rand <= feedback&rand(30 downto 1);
        end if;
    end process;

    random <= rand(OUT_WIDTH-1 downto 0);

end Behavioral;

library ieee;
    use ieee.math_real.all;

entity rand_gen is
end rand_gen;

architecture behavior of rand_gen is

    signal rand_num : integer := 0;

begin

    process
        variable seed1, seed2: positive; -- seed values for random generator
        variable rand: real; -- random real-number value in range 0 to 1.0
        variable range_of_rand : real := 250.0; -- the range of random values created will be 0 to +1000.
    begin
        uniform(seed1, seed2, rand); -- generate random number
        rand_num <= integer(rand*range_of_rand); -- rescale to 0..1000, convert integer part
        wait for 10 ns;
    end process;

end behavior;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_signed.all;

entity example is
    port ( clock_50, read_s : in std_logic;
        noise : out std_logic_vector(23 downto 0));
end example;

architecture behavior of example is
    signal counter : std_logic_vector(2 downto 0);
    signal q : std_logic_vector(9 downto 0);
begin
    process (clock_50)
    begin
        if rising_edge(clock_50) then
        if (read_s = '1') then
        counter <= counter + 1;
        end if;
        end if;
    end process;
    q <= (others => counter(2));
    noise <= q & counter & "00000000000";
end behavior;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity i2s_tx_48 is
    port( clk: in std_logic;
        fall_edge, rise_edge: in std_logic;
        rst: in boolean;
        it_sel, clk_sel: in std_logic_vector(1 downto 0);
        it_data: in std_logic_vector(7 downto 0);
        it_ws, it_sclk, it_sd: out std_logic);
end entity;

architecture arch of i2s_tx_48 is

    signal ssclk, s_ws, sel, lr_edge, sel_rise: std_logic;
    signal count_reg: unsigned(1 downto 0);
    signal bit_count: unsigned(3 downto 0);

    signal shift, shift_nxt: std_logic_vector(15 downto 0);
    signal shift_lft, shift_rht: std_logic_vector(7 downto 0);
    signal int_rise_e, int_fall_e, int_edge_reg: std_logic;

begin

    sel <= it_sel(0) and it_sel(1);

    process(clk, rst)
    begin
        if rst then
        lr_edge <= '0';
        elsif rising_edge(clk) then
        lr_edge <= sel;
        end if;
    end process;

    sel_rise <= sel and (not lr_edge);

    process(clk, rst, sel_rise)
    begin
        if rst or sel_rise = '1' then
        count_reg <= (others => '0');
        ssclk <= '0';
        elsif rising_edge(clk) then
        if rise_edge = '1' then
        count_reg <= count_reg +1;

        if count_reg = 3 then
        ssclk <= not ssclk;
        end if;
        end if;
        end if;
    end process;

    process(clk, rst)
    begin
        if rst then
        int_edge_reg <= '0';
        elsif rising_edge(clk) then
        int_edge_reg <= ssclk;
        end if;
    end process;

    int_fall_e <= (not int_edge_reg) nor ssclk;
    int_rise_e <= (not int_edge_reg) and ssclk;

    process(clk, rst, it_sel, clk_sel)
    begin
        if rst or (it_sel = "11" and clk_sel = "00") then
        bit_count <= (others => '0');
        s_ws <= '0';
        elsif rising_edge(clk) then
        if int_fall_e = '1' then
        bit_count <= bit_count +1;

        if bit_count = 6 or bit_count = 14 then
        s_ws <= not s_ws;
        end if;
        end if;
        end if;
    end process;

    it_sclk <= ssclk;
    it_ws <= s_ws;

    --main shift register
    process(clk)
    begin
        if rising_edge(clk) then
        --shift <= shift_nxt;
        if int_fall_e = '1' then
        shift <= shift(14 downto 0) & '0';
        end if;
        if bit_count = 0 and int_rise_e = '1' then
        shift(7 downto 0) <= shift_lft;
        end if;

        if bit_count = 8 and fall_edge = '1' then
        shift(7 downto 0) <= shift_rht;
        end if;
        end if;
    end process;

    -- shift_nxt <= shift(14 downto 0) & '0' when int_fall_e = '1' else
    -- shift_lft when bit_count = 0 and int_rise_e = '1' else
    -- shift_rht when bit_count = 8 and fall_edge = '1' else -- change to bit_count 7 and int fall
    -- shift;

    process(clk, rst)
    begin
        if rst then
        shift_lft <= (others => '0');
        shift_rht <= (others => '0');
        elsif rising_edge(clk) then
        if it_sel = "11" and clk_sel = "00" then
        shift_lft <= it_data;
        end if;

        if it_sel = "11" and clk_sel = "01" then
        shift_rht <= it_data;
        end if;
        end if;
    end process;

    it_sd <= shift(15);

end arch;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity i2s_tx_48_2 is
    port( clk: in std_logic;
        fall_edge, rise_edge: in std_logic;
        rst: in boolean;
        it_sel, clk_sel: in std_logic_vector(1 downto 0);
        it_data: in std_logic_vector(7 downto 0);
        it_ws, it_sclk, it_sd: out std_logic);
end entity;

architecture arch of i2s_tx_48_2 is

    signal ssclk, s_ws, sel, lr_edge, sel_rise: std_logic;
    signal count_reg: unsigned(1 downto 0);
    signal bit_count: unsigned(3 downto 0);

    signal shift, shift_nxt, shift_lft, shift_rht: std_logic_vector(7 downto 0);
    signal int_rise_e, int_fall_e, int_edge_reg: std_logic;

begin

    sel <= it_sel(0) and it_sel(1);

    process(clk, rst)
    begin
        if rst then
        lr_edge <= '0';
        elsif rising_edge(clk) then
        lr_edge <= sel;
        end if;
    end process;

    sel_rise <= sel and (not lr_edge);

    process(clk, rst, sel_rise)
    begin
        if rst or sel_rise = '1' then
        count_reg <= (others => '0');
        ssclk <= '0';
        elsif rising_edge(clk) then
        if rise_edge = '1' then
        count_reg <= count_reg +1;

        if count_reg = 3 then
        ssclk <= not ssclk;
        end if;
        end if;
        end if;
    end process;

    process(clk, rst)
    begin
        if rst then
        int_edge_reg <= '0';
        elsif rising_edge(clk) then
        int_edge_reg <= ssclk;
        end if;
    end process;

    int_fall_e <= (not int_edge_reg) nor ssclk;
    int_rise_e <= (not int_edge_reg) and ssclk;

    process(clk, rst, it_sel, clk_sel)
    begin
        if rst or (it_sel = "11" and clk_sel = "10") then
        bit_count <= (others => '0');
        s_ws <= '0';
        elsif rising_edge(clk) then
        if int_fall_e = '1' then
        bit_count <= bit_count +1;

        if bit_count = 6 or bit_count = 14 then
        s_ws <= not s_ws;
        end if;
        end if;
        end if;
    end process;

    it_sclk <= ssclk;
    it_ws <= s_ws;

    --main shift register
    process(clk)
    begin
        if rising_edge(clk) then
        shift <= shift_nxt;
        end if;
    end process;

    shift_nxt <= shift(6 downto 0) & '0' when int_fall_e = '1' else
        shift_lft when bit_count = 0 and int_rise_e = '1' else
        shift_rht when bit_count = 8 and int_rise_e = '1' else -- change to bit_count 7 and int fall
        shift;

        process(clk, rst)
        begin
        if rst then
        shift_lft <= (others => '0');
        shift_rht <= (others => '0');
        elsif rising_edge(clk) then
        if it_sel = "11" and clk_sel = "10" then
        shift_lft <= it_data;
        end if;

        if it_sel = "11" and clk_sel = "11" then
        shift_rht <= it_data;
        end if;
        end if;
        end process;

        it_sd <= shift(7);

        end arch;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity pwm_mod is port(
    clk, rst : std_logic;
    led0: out std_logic);
end entity;

architecture arch of pwm_mod is
    signal clk_div_reg, clk_div_next : unsigned (13 downto 0);
    signal pwm0_reg, pwm0_next, pwm1_reg, pwm1_next : unsigned (7 downto 0);
    signal led_inv_0, led_inv_1, clk_div : std_logic;
begin

    process(clk, rst)
    begin
        if rst = '0' then
        clk_div_reg <= (others => '0');
        elsif rising_edge(clk) then
        clk_div_reg <= clk_div_next;
        end if;
    end process;

    clk_div_next <= (others => '0') when clk_div_reg = 5000 else clk_div_reg + 1;

    clk_div <= '1' when clk_div_reg = 5000 else '0';

    process(clk_div, rst)
    begin
        if rst = '0' then
        pwm0_reg <= (others => '0');
        pwm1_reg <= (others => '0');
        elsif rising_edge(clk_div) then
        pwm0_reg <= pwm0_next;
        pwm1_reg <= pwm1_next;
        end if;
    end process;

    pwm0_next <= (others => '0') when pwm0_reg = 254 else pwm0_reg + 1;
    pwm1_next <= (others => '0') when pwm1_reg = 252 else pwm1_reg + 1;

    led_inv_0 <= '1' when pwm0_reg > 127 else '0';
    led_inv_1 <= '1' when pwm1_reg > 126 else '0';
    led0 <= led_inv_0 xor led_inv_1;

end arch;

library ieee;
    use ieee.std_logic_1164.all;

entity flag_buf is
    generic(w: integer := 8);
    port(
        clk, rst: in std_logic;
        clr_flag, set_flag: in std_logic;
        din: in std_logic_vector(w-1 downto 0);
        dout: out std_logic_vector(w-1 downto 0);
        flag: out std_logic);
end flag_buf;

architecture arch of flag_buf is
    signal buf_reg, buf_next: std_logic_vector(w-1 downto 0);
    signal flag_reg, flag_next: std_logic;
begin
    --ff & register
    process(clk, rst)
    begin
        if rst = '1' then
        buf_reg <= (others => '0');
        flag_reg <= '0';
        elsif(rising_edge(clk)) then
        buf_reg <= buf_next;
        flag_reg <= flag_next;
        end if;
    end process;
    --next-state logic
    process(buf_reg, flag_reg, set_flag, clr_flag, din)
    begin
        buf_next <= buf_reg;
        flag_next <= flag_reg;
        if (set_flag = '1') then
        buf_next <= din;
        flag_next <= '1';
        elsif (clr_flag = '1') then
        flag_next <= '0';
        end if;
    end process;
    --output logic
    dout <= buf_reg;
    flag <= flag_reg;
end arch;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee. numeric_std.all;

entity uart_tx is
    generic(
        dbit: integer := 8; --# data bits
        sb_tick: integer := 16); --# ticks for stop bits
    port(
        clk, rst: in std_logic;
        tx_start: in std_logic;
        s_tick: in std_logic;
        din: in std_logic_vector(7 downto 0);
        tx_done_tick: out std_logic;
        tx: out std_logic);

end uart_tx;

architecture arch of uart_tx is
    type state_type is(idle, start, data, stop);
    signal state_reg, state_next: state_type;
    signal s_reg, s_next: unsigned(3 downto 0);
    signal n_reg, n_next: unsigned(2 downto 0);
    signal b_reg, b_next: std_logic_vector(7 downto 0);
    signal tx_reg, tx_next: std_logic;
begin
    --FSMD state & data registers
    process(clk, rst)
    begin
        if rst = '1' then
        state_reg <= idle;
        s_reg <= (others => '0');
        n_reg <= (others => '0');
        b_reg <= (others => '0');
        tx_reg <= '1';
        elsif rising_edge(clk) then
        state_reg <= state_next;
        s_reg <= s_next;
        n_reg <= n_next;
        b_reg <= b_next;
        tx_reg <= tx_next;
        end if;
    end process;
    --next-state logic & data path function units/routing
    process(state_reg, s_reg, n_reg, b_reg, s_tick, tx_reg, tx_start, din)
    begin
        state_next <= state_reg;
        s_next <= s_reg;
        n_next <= n_reg;
        b_next <= b_reg;
        tx_next <= tx_reg;
        tx_done_tick <= '0';

        case state_reg is
        when idle =>
        tx_next <= '1';
        if tx_start = '1' then
        state_next <= start;
        s_next <= (others => '0');
        b_next <= din;
        end if;

        when start =>
        tx_next <= '0';
        if (s_tick = '1') then
        if s_reg = 15 then
        state_next <= data;
        s_next <= (others => '0');
        n_next <= (others => '0');
        else
        s_next <= s_reg +1;
        end if;
        end if;

        when data =>
        tx_next <= b_reg(0);
        if s_tick = '1' then
        if s_reg = 15 then
        s_next <= (others => '0');
        b_next <= '0' & b_reg(7 downto 1);
        if n_reg = dbit-1 then
        state_next <= stop;
        else
        n_next <= n_reg +1;
        end if;
        else
        s_next <= s_reg +1;
        end if;
        end if;

        when stop =>
        tx_next <= '1';
        if s_tick = '1' then
        if s_reg = sb_tick -1 then
        state_next <= idle;
        tx_done_tick <= '1';
        else
        s_next <= s_reg +1;
        end if;
        end if;

        end case;
    end process;
    tx <= tx_reg;
end arch;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity uart is
    generic(
        --default setting:
        --19200 baud, 8 data bits, 1 stop bit, 2^2 FIFO
        dbit: integer := 8; --# data bits
        sb_tick: integer := 16; --# ticks for stop bits, 16/24/32
        --for 1/1.5/2 stop bits
        dvsr: integer := 163; --baud rate divisor
        --dvsr = 50M/(16*baud rate)
        dvsr_bit: integer := 8; --#bits of dvsr
        fifo_w: integer := 2); --#addr bits of FIFO
    --#words in FIFO = 2^fifo_w
    port(
        -- clk, rst: in std_logic;
        -- rd_uart, wr_uart: in std_logic;
        -- rx: in std_logic;
        -- w_data: in std_logic_vector(7 downto 0);
        -- tx_full, rx_empty: out std_logic;
        r_data: out std_logic_vector(7 downto 0);
        -- tx: out std_logic);
        clk, rst: in std_logic;
        rx_done_tick: out std_logic;
        rx: in std_logic);
end uart;

architecture str_arch of uart is
    signal tick: std_logic;
    -- signal rx_done_tick: std_logic;
    -- signal tx_fifo_out: std_logic_vector(7 downto 0);
    signal rx_data_out: std_logic_vector(7 downto 0);
    -- signal tx_empty, tx_fifo_not_empty: std_logic;
    -- signal tx_done_tick: std_logic;

begin
    baud_gen_unit: entity work.mod_m_counter(arch)
        generic map(m => dvsr, n => dvsr_bit)
        port map(clk => clk, rst => rst, q => open, max_tick => tick);

    uart_rx_unit: entity work.uart_rx(arch)
        generic map(dbit => dbit, sb_tick => sb_tick)
        port map(clk => clk, rst => rst, rx => rx, s_tick => tick,
        rx_done_tick => rx_done_tick, data_out => r_data);

    -- fifo_rx_unit: entity work.fifo(arch)
    -- generic map(b => dbit, w => fifo_w)
    -- port map(clk => clk, rst => rst, rd => rd_uart, wr => rx_done_tick,
    -- w_data => rx_data_out, empty => rx_empty, full => open, r_data => r_data);

    -- fifo_tx_unit: entity work.fifo(arch)
    -- generic map(b => dbit, w => fifo_w)
    -- port map(clk => clk, rst => rst, rd => tx_done_tick, wr => wr_uart, w_data => w_data,
    -- empty => tx_empty, full => tx_full, r_data => tx_fifo_out);
    --
    -- uart_tx_unit: entity work.uart_tx(arch)
    -- generic map(dbit => dbit, sb_tick => sb_tick)
    -- port map(clk => clk, rst => rst, tx_start => tx_fifo_not_empty, s_tick => tick,
    -- din => tx_fifo_out, tx_done_tick => tx_done_tick, tx => tx);
    --
    -- tx_fifo_not_empty <= not tx_empty;
end str_arch;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity uart is port(
    clk, rx : in std_logic;
    rst : in boolean;
    tx : out std_logic);
end uart;

architecture str_arch of uart is
    signal ld, rxready, load, ready: std_logic;
    signal din, dout, data_in, data_out: std_logic_vector(7 downto 0);

begin
    tx_rx_unit: entity work.uartmodule(arch)
        port map(clk => clk, rst => rst, tx => tx, rx => rx, ld => ld, din => din, dout => dout, rxready => rxready);

    acc_unit: entity work.accumulator(arch)
        port map(clk => clk, rst => rst, data_out => din, data_in => dout,
        load => ld, ready => rxready);

end str_arch;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity uart_test is port(
    clk, rst: in std_logic;
    btn: std_logic_vector(2 downto 0);
    rx: in std_logic;
    tx: out std_logic;
    led: out std_logic_vector(7 downto 0);
    sseg: out std_logic_vector(7 downto 0);
    an: out std_logic_vector(3 downto 0));
end uart_test;

architecture arch of uart_test is
    signal tx_full, rx_empty: std_logic;
    signal rec_data, rec_data1: std_logic_vector(7 downto 0);
    signal btn_tick: std_logic;
begin
    --instantiate uart
    uart_unit: entity work.uart(str_arch)
        port map(clk => clk, rst => rst, rd_uart => btn_tick,
        wr_uart => btn_tick, rx => rx, w_data => rec_data1,
        tx_full => tx_full, rx_empty => rx_empty,
        r_data => rec_data, tx => tx);

    --increment data loop back
    rec_data1 <= std_logic_vector(unsigned(rec_data)+1);
    --led display
    led <= rec_data;
    an <= "1110";
    sseg <= '1' & (not tx_full) & "11" & (not rx_empty) & "111";
end arch;

--https://www.youtube.com/watch?v=Fimf3jypV_o

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity uartmodule is port(
    clk, ld, rx : in std_logic;
    rst : in boolean;
    din : in std_logic_vector(7 downto 0);
    dout : out std_logic_vector(7 downto 0);
    tx, txbusy, rxready : out std_logic);
end uartmodule;

architecture arch of uartmodule is
    constant width_1 : natural := 8;
    constant width_2 : natural := 7;

    type tx_state is (idle_tx, shift_tx);
    signal txfsm : tx_state;

    type rx_state is (idle_rx, shift_rx);
    signal rxfsm : rx_state;

    signal tx_reg : std_logic_vector(9 downto 0);
    signal txbitcnt : unsigned(3 downto 0);
    signal txclkdiv : unsigned(width_1 downto 0);
    signal txclkdiv_sum : unsigned(width_1 +1 downto 0);
    signal ticktx : std_logic;
    signal txclkena : std_logic;

    signal rx_reg : std_logic_vector(9 downto 0);
    signal rxbitcnt : unsigned(4 downto 0);
    signal rxclkdiv : unsigned(width_2 downto 0);
    signal rxclkdiv_sum : unsigned(width_2 +1 downto 0);
    signal tickrx : std_logic;
    signal rxclkena : std_logic;

begin

    --clk divider tx
    txclkdiv_sum <= resize(txclkdiv,width_1 +2) -1;
    process(clk,rst)
    begin
        if not rst then
        txclkdiv <= "110110010";
        elsif rising_edge(clk) then
        if ticktx = '1' then
        txclkdiv <= "110110010";
        elsif txclkena = '1' then
        txclkdiv <= txclkdiv_sum(width_1 downto 0);
        end if;
        end if;
    end process;
    ticktx <= txclkdiv_sum(width_1 +1);

    --clk divider rx
    rxclkdiv_sum <= resize(rxclkdiv,width_2 +2) -1;
    process(clk,rst)
    begin
        if not rst then
        rxclkdiv <= "01101001";
        elsif rising_edge(clk) then
        if tickrx = '1' then
        rxclkdiv <= "01101001";
        elsif rxclkena = '1' then
        rxclkdiv <= rxclkdiv_sum(width_2 downto 0);
        end if;
        end if;
    end process;
    tickrx <= rxclkdiv_sum(width_2 +1);

    --transmit state machine
    tx_fsm: process(clk, rst)
    begin
        if not rst then
        tx_reg <= (others => '1');
        txbitcnt <= (others => '0');
        txfsm <= idle_tx;
        txbusy <= '0';
        elsif rising_edge(clk) then
        case txfsm is
        when idle_tx =>
        if ld = '0' then --latch the input data immediately
        tx_reg <= '1' & din & '0'; --stop bit & data & start bit
        txbusy <= '1';
        txbitcnt <= "1010";
        txfsm <= shift_tx;
        txclkena <= '1';
        else
        txbusy <= '0';
        txclkena <= '0';
        end if;

        when shift_tx =>
        txbitcnt <= txbitcnt -1;
        tx_reg <= '1' & tx_reg(tx_reg'high downto 1);
        if txbitcnt = 0 then
        txfsm <= idle_tx;
        end if;

        when others =>
        txfsm <= idle_tx;
        end case;
        end if;
    end process;
    tx <= tx_reg(0);

    --receive state machine
    rx_fsm: process(clk, rst)
    begin
        if not rst then
        rx_reg <= (others => '0');
        rxbitcnt <= (others => '0');
        rxfsm <= idle_rx;
        elsif rising_edge(clk) then
        case rxfsm is
        when idle_rx => --wait on start bit
        if rx = '0' then
        rxfsm <= shift_rx;
        rxbitcnt <= "10101";
        rxclkena <= '1'; --synchronize the divisor
        else
        rxclkena <= '0';
        end if; --else false start, stay in idle

        when shift_rx => --sample data
        if tickrx = '1' then
        rxbitcnt <= rxbitcnt -1; --shift right
        rx_reg <= rx & rx_reg(rx_reg'high downto 1);
        if rxbitcnt <= 0 then
        rxfsm <= idle_rx;
        rxready <= '1';
        else rxready <= '0';
        end if;
        end if;

        when others =>
        rxfsm <= idle_rx;
        end case;
        end if;
    end process;
    dout <= rx_reg(8 downto 1);
end arch;

library ieee;
    use ieee.std_logic_1164.all;

entity bigger is
    generic(n : natural := 7);
    port( a, b: in std_logic_vector(n downto 0);
        big : out std_logic);
end entity;

architecture rtl1 of bigger is
begin
    po : process(a,b)
        variable big_so_far : std_logic;
begin
    big_so_far := '0';
    for i in a'length-1 downto 0 loop --left to right
        if (a(i) = '1') and (b(i) = '0') then
        big_so_far := '1';
        exit;
        elsif (a(i) = '0') and (b(i) = '1') then
        exit;
        end if;
    end loop;
    big <= big_so_far;
end process;
end rtl1;

architecture rtl2 of bigger is
    signal eachbit : std_logic_vector(n downto 0);
begin
    xnor_gen : for i in a'range generate
        eachbit(i) <= not (a(i) xor b(i));
    end generate;
    p0: process(eachbit, a, b)
        variable equal_so_far, big_so_far : std_logic;
    begin
        equal_so_far := '1';
        big_so_far := '0';
        for i in a'range loop
        big_so_far := (equal_so_far and a(i) and (not b(i))) or big_so_far;
        equal_so_far := equal_so_far and eachbit(i);
        end loop;
        big <= big_so_far;
    end process;
end rtl2;

architecture rtl3 of bigger is
begin
    big <= '1' when a > b else '0';
end rtl3;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_arith.all;

entity tbbigger is
end entity;

architecture beh of tbbigger is
    component bigger
    generic(n : natural := 7);
    port( a, b: in std_logic_vector(n downto 0);
        big : out std_logic);
end component;

constant n : natural := 8;
signal a, b: std_logic_vector(n-1 downto 0);
signal big1,big2,big3, big_c : std_logic;

constant period : time := 5 ns;
constant strobe : time := period - 1 ns;

begin

    p0: process
    begin
        for i in a'range loop
        a <= conv_std_logic_vector(i,n);
        for j in b'range loop
        b <= conv_std_logic_vector(j,n);
        wait for period;
        end loop;
        end loop;
        wait;
    end process;

    big_c <= '1' when a > b else '0';
    check : process
        variable pass_cnt : integer := 0;
    begin
        wait for strobe;
        assert false report "comparing..." severity note;
        if (big1 /= big_c) or (big2 /= big_c) or (big3 /= big_c)then
        assert false report "not match" severity warning;
        pass_cnt := pass_cnt +1;
        end if;
        wait for period;
        assert (pass_cnt = 0) report "test failed" severity error;
        assert (pass_cnt /= 0) report "test pass" severity note;
        wait;
    end process;

    bigger1 : bigger
        port map(a => a, b => b, big => big1);
    bigger2 : bigger
        port map(a => a, b => b, big => big2);
    bigger3 : bigger
        port map(a => a, b => b, big => big3);
end beh;

configuration cfg_tbbigger of tbbigger is
    for beh
    for bigger1 : bigger
    use entity work.bigger(rtl1);
end for;
for bigger2 : bigger
use entity work.bigger(rtl2);
end for;
for bigger3 : bigger
use entity work.bigger(rtl3);
end for;
end for;
end configuration;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity gle is port(
    a, b: in std_logic_vector(31 downto 0);
    equal, greater, less: out std_logic);
end entity;

architecture rtl1 of gle is
begin
    p0: process(a, b)
        variable eq, gt, lt : std_logic;
    begin
        equal <= '1';
        greater <= '0';
        less <= '0';

        for j in a'range loop
        if(a(j) and (not b(j))) = '1' then
        greater <= '1';
        equal <= '0';
        exit;
        elsif((not a(j)) and b(j)) = '1' then
        less <= '1';
        equal <= '0';
        exit;
        end if;
        end loop;
    end process;
end rtl1;

architecture rtl2 of gle is
begin
    p1: process(a,b)
    begin
        equal <= '0';
        greater <= '0';
        less <= '0';
        if(a > b) then
        greater <= '1';
        elsif(a < b) then
        less <= '1';
        else
        equal <= '1';
        end if;
    end process;
end rtl2;

architecture rtl3 of gle is
begin
    p2: process(a,b)
    begin
        equal <= '0';
        greater <= '0';
        less <= '0';
        if a = b then
        equal <= '1';
        elsif a > b then
        greater <= '1';
        else
        less <= '1';
        end if;
    end process;
end rtl3;

architecture rtl4 of gle is
begin
    equal <= '1' when a = b else '0';
    greater <= '1' when a > b else '0';
    less <= '1' when a < b else '0';
end rtl4;

architecture rtl5 of gle is
    signal eq_temp, gt_temp, lt_temp : std_logic;
begin
    eq_temp <= '1' when a = b else '0';
    gt_temp <= '1' when a > b else '0';
    lt_temp <= eq_temp nor gt_temp;

    equal <= eq_temp;
    greater <= gt_temp;
    less <= lt_temp;

end rtl5;

architecture rtl6 of gle is
    signal eq_temp : std_logic;
    signal sub : std_logic_vector(a'length downto 0);
begin
    eq_temp <= '1' when a = b else '0';
    sub <= ('0' & a) - ('0' & b);
    less <= sub(a'length) and (not eq_temp);
    greater <= (not sub(a'length)) and (not eq_temp);
    equal <= eq_temp;
end rtl6;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_arith.all;

entity tbgle is
end entity;

architecture beh of tbgle is
    component gle
    generic(n : natural := 32);
    port( a, b: in std_logic_vector(n-1 downto 0);
        equal, greater, less: out std_logic);
end component;

constant w : natural := 5; --signal width

signal a, b: std_logic_vector(2**w-1 downto 0);
signal equal, greater, less: std_logic;
signal e_c, e1, e2, e3, e4, e5, e6 : std_logic;
signal g_c, g1, g2, g3, g4, g5, g6 : std_logic;
signal l_c, l1, l2, l3, l4, l5, l6 : std_logic;

constant period : time := 5 ns;
constant strobe : time := period -1 ns;

begin
    p0: process
    begin
        for i in 0 to 2**w-1 loop
        a <= conv_std_logic_vector(i,2**w);
        for j in 0 to 2**w-1 loop
        b <= conv_std_logic_vector(j,2**w);
        wait for period;
        end loop;
        end loop;
        wait;
    end process;

    e_c <= '1' when a = b else '0';
    g_c <= '1' when a > b else '0';
    l_c <= '1' when a < b else '0';

    check: process
        variable pass_cnt : natural := 0;
    begin
        wait for strobe;
        if(e_c /= e1) or (e_c /= e2) or (e_c /= e3) or (e_c /= e4) or (e_c /= e5) or (e_c /= e6) or
        (g_c /= g1) or (g_c /= g2) or (g_c /= g3) or (g_c /= g4) or (g_c /= g5) or (g_c /= g6) or
        (l_c /= l1) or (l_c /= l2) or (l_c /= l3) or (l_c /= l4) or (l_c /= l5) or (l_c /= l6) then
        assert false report "no match" severity warning;
        end if;
        pass_cnt := pass_cnt +1;
        wait for period;
        assert(pass_cnt = 0) report "test fail" severity error;
        assert(pass_cnt /=0) report "test pass" severity note;
        wait;
    end process;

    gle1 : gle
        port map(a => a, b => b, equal => e1, greater => g1, less => l1);
    gle2 : gle
        port map(a => a, b => b, equal => e2, greater => g2, less => l2);
    gle3 : gle
        port map(a => a, b => b, equal => e3, greater => g3, less => l3);
    gle4 : gle
        port map(a => a, b => b, equal => e4, greater => g4, less => l4);
    gle5 : gle
        port map(a => a, b => b, equal => e5, greater => g5, less => l5);
    gle6 : gle
        port map(a => a, b => b, equal => e6, greater => g6, less => l6);

end beh;

configuration cfg_tbgle of tbgle is
    for beh
    for gle1 : gle
    use entity work.gle(rtl1);
end for;
for gle2 : gle
use entity work.gle(rtl1);
end for;
for gle3 : gle
use entity work.gle(rtl1);
end for;
for gle4 : gle
use entity work.gle(rtl1);
end for;
for gle5 : gle
use entity work.gle(rtl1);
end for;
for gle6 : gle
use entity work.gle(rtl1);
end for;
end for;
end configuration;

library ieee;
    use ieee.std_logic_1164.all;

entity rpadder is
    generic(n : natural := 8);
    port( a, b : in std_logic_vector(n-1 downto 0);
        ci : in std_logic := '0';
        s : out std_logic_vector(n-1 downto 0);
        cout : out std_logic);
end rpadder;

architecture rtl1 of rpadder is
    component fa
    port( a, b, ci : in std_logic;
        s, cout : out std_logic);
end component;
signal c : std_logic_vector(a'length-1 downto 1);

begin
    gen : for j in a'range generate
        genlsb : if j = 0 generate
        fa0 : fa port map(a => a(0), b => b(0),
        ci => ci, s => s(0), cout => c(1));
        end generate;
        genmid : if j /= 0 and j < a'length-1 generate
        fa0 : fa port map(a => a(j), b => b(j),
        ci => c(j), s => s(j), cout => c(j +1));
        end generate;
        genmsb : if j = a'length-1 generate
        fa0 : fa port map(a => a(j), b => b(j),
        ci => c(j), s => s(j), cout => cout);
        end generate;
    end generate;
end rtl1;

--architecture rtl2 of rpadder is
-- procedure fadder(
-- signal a, b, ci : in std_logic;
-- signal s, cout : out std_logic) is
-- begin
-- s <= a xor b xor ci;
-- cout <= ((a or b) and ci) or (a and b);
-- end fadder;
-- signal c : std_logic_vector(a'length-1 downto 1);
--
--begin
-- gen : for j in a'range generate
-- genlsb : if j = 0 generate
-- fadder(a => a(0), b => b(0),
-- ci => ci, s => s(0), cout => c(1));
-- end generate;
-- genmid : if j /= 0 and j < a'length-1 generate
-- fadder(a => a(j), b => b(j),
-- ci => c(j), s => s(j), cout => c(j +1));
-- end generate;
-- genmsb : if j = a'length-1 generate
-- fadder(a => a(j), b => b(j),
-- ci => c(j), s => s(j), cout => cout);
-- end generate;
-- end generate;
--end rtl2;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_arith.all;
    use ieee.std_logic_unsigned.all;

entity tbrpadder is
end entity;

architecture beh of tbrpadder is

    constant n : natural := 8;

    component rpadder
    port( a, b : in std_logic_vector(n-1 downto 0);
        ci : in std_logic;
        s : out std_logic_vector(n-1 downto 0);
        cout : out std_logic);
end component;

signal a, b : std_logic_vector(n-1 downto 0);
signal ci : std_logic;
signal s, sc : std_logic_vector(n-1 downto 0);
signal cout : std_logic;

constant period : time := 5 ns;

begin
    p0: process
    begin
        for i in 0 to 2**n-1 loop
        a <= conv_std_logic_vector(i,n);
        for j in 0 to 2**n-1 loop
        b <= conv_std_logic_vector(j,n);
        wait for period;
        end loop;
        end loop;
    end process;

    sc <= a+b;

    rpadder1 : rpadder
        port map (a => a, b => b, ci => ci, s => s, cout => cout);

end beh;

library ieee;
    use ieee.std_logic_1164.all;

entity fapg is port(
    a, b, ci : in std_logic;
    s, p, g : out std_logic);
end fapg;

architecture rtl of fapg is
    signal gsig, psig : std_logic;
begin
    gsig <= a and b;
    psig <= a xor b;
    s <= psig xor ci;
    g <= gsig;
    p <= psig;
end rtl;

----ripple carry adder
--library ieee;
--use ieee.std_logic_1164.all;
--
--entity fa is
--generic(n : natural := 3);
--port(
-- a, b : in std_logic_vector(n downto 0);
-- z : out std_logic_vector(n downto 0);
-- co : out std_logic);
--end entity;
--
--architecture dataflow of fa is
-- signal carry : std_logic_vector(n +1 downto 0);
--begin
-- carry(0) <= '0';
--
-- adder : for m in 0 to n generate
-- carry(m +1) <= (a(m) and b(m)) or (carry(m) and (a(m) xor b(m)));
-- z(m) <= a(m) xor b(m) xor carry(m);
-- end generate;
--
-- co <= carry(n +1);
--
--end dataflow;

library ieee;
    use ieee.std_logic_1164.all;

entity clau is port(
    p, g : in std_logic_vector(3 downto 0);
    ci : in std_logic;
    co : out std_logic_vector(3 downto 0);
    gp, gg : out std_logic);
end clau;

architecture rtl of clau is
begin
    co(0) <= ci;
    co(1) <= (ci and p(0)) or g(0);
    co(2) <= (ci and p(0) and p(1)) or (g(0) and p(1)) or g(1);
    co(3) <= (ci and p(0) and p(1) and p(2)) or (g(0) and p(1) and p(2)) or (g(1) and p(2)) or g(2);

    gg <= (g(0) and p(1) and p(2) and p(3)) or (g(1) and p(2) and p(3)) or (g(2) and p(3)) or g(3);
    gp <= p(3) and p(2) and p(1) and p(0);
end rtl;

library ieee;
    use ieee.std_logic_1164.all;

entity cla16 is port(
    a, b : in std_logic_vector(15 downto 0);
    ci : in std_logic;
    s : out std_logic_vector(15 downto 0);
    co : out std_logic);
end cla16;

architecture rtl of cla16 is
    component fapg
    port( a, b, ci : in std_logic;
        s, p, g : out std_logic);
end component;

component clau
port( p, g : in std_logic_vector(3 downto 0);
        ci : in std_logic;
        co : out std_logic_vector(3 downto 0);
        gp, gg : out std_logic);
end component;

constant n : integer := 4; -- number of 4 bits
signal p, g, c : std_logic_vector(n*4-1 downto 0);
signal gp, gg, gc : std_logic_vector(n-1 downto 0);
begin
    fagen : for i in 0 to n*4-1 generate
        fapg0 : fapg port map (a => a(i), b => b(i), ci => c(i), s => s(i), p => p(i), g => g(i));
    end generate;

    claugen : for i in 0 to n-1 generate
        clau0 : clau port map(p => p(i*4+3 downto i*4), g => g(i*4+3 downto i*4), ci => gc(i), co => c(i*4+3 downto i*4), gp => gp(i), gg => gg(i));
    end generate;

    clau1 : clau port map(p => gp, g => gg, ci => ci, co => gc, gp => open, gg => co);
end rtl;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity adder is
    generic(n : in integer := 16);
    port(
        a, b : in std_logic_vector(n-1 downto 0);
        ci : in std_logic;
        s : out std_logic_vector(n-1 downto 0);
        cout : out std_logic);
end adder;

architecture rtl of adder is
    signal result : std_logic_vector(a'length downto 0);
begin
    result <= ('0' & a) + ('0' & b) + ci;
    s <= result(a'length-1 downto 0);
    cout <= result(a'length);
end rtl;

configuration cfg_cla16 of cla16 is
    for rtl
    for fagen
    for all : fapg
    use entity work.fapg(rtl);
end for;
end for;
for claugen
for all : clau
use entity work.clau(rtl);
end for;
end for;
for clau1 : clau
use entity work.clau(rtl);
end for;
end for;
end cfg_cla16;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_arith.all;

entity tbcla16 is
end entity;

architecture beh of tbcla16 is
    component cla16 port(
        a, b : in std_logic_vector(15 downto 0);
        ci : in std_logic;
        s : out std_logic_vector(15 downto 0);
        co : out std_logic);
end component;

component adder
generic(n : natural := 16);
port(
    a, b : in std_logic_vector(n-1 downto 0);
    ci : in std_logic;
    s : out std_logic_vector(n-1 downto 0);
    cout : out std_logic);
end component;

constant period : time := 5 ns;
constant strobe : time := period -1 ns;
constant n : natural := 16;

signal a : std_logic_vector(n-1 downto 0);
signal b : std_logic_vector(n-1 downto 0);
signal ci : std_logic;
signal co, co1 : std_logic;
signal s, s1 : std_logic_vector(n-1 downto 0);
begin
    p0 : process
        variable q : std_logic_vector(n-1 downto 0);
    begin
        a <= (others => '1');
        b <= (others => '1');
        ci <= '1';
        wait for period;
        q := (others => '0');
        loop
        a <= q;
        b <= (q(n-1) xor (not q(2))) & q(n-1 downto 1);
        ci <= q(0) and q(1);
        wait for period;
        q := q(n-2 downto 0) & (q(n-1) xor (not q(2)));
        end loop;
    end process;

    check : process
    begin
        wait for strobe;
        loop
        if(s /= s1) or (co /= co1) then
        assert false report "no match" severity warning;
        end if;
        wait for period;
        end loop;
    end process;
    cla0 : cla16
        port map(a => a, b => b, ci => ci, s => s, co => co);
    adder0 : adder
        generic map(n => n)
        port map(a => a, b => b, ci => ci, s => s1, cout => co1);
end beh;
configuration cfg_tbcla16 of tbcla16 is
    for beh
    for all : cla16
    use configuration work.cfg_cla16;
end for;
for all : adder
use entity work.adder(rtl);
end for;
end for;
end cfg_tbcla16;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity countone is port(
    din : in std_logic_vector(31 downto 0);
    num : out std_logic_vector(5 downto 0));
end countone;

architecture rtl1 of countone is
begin
    comb : process(din)
        variable temp : std_logic_vector(5 downto 0);
begin
    temp := (others => '0');
    for j in din'range loop
        if(din(j)) = '1' then
        temp := temp +1;
        end if;
    end loop;
    num <= temp;
end process;
end rtl1;

architecture rtl2 of countone is
begin
    comb : process(din)
        constant parts : integer := 8;
    variable temp : std_logic_vector(5 downto 0);
    variable temp1 : std_logic_vector(5 downto 0);
begin
    temp := (others => '0');
    for j in 0 to parts -1 loop
        temp1 := (others => '0');
        for k in 32/parts-1 downto 0 loop
        if (din(32/parts * j + k) = '1') then
        temp1 := temp1 + 1;
        end if;
        end loop;
        temp := temp + temp1;
    end loop;
    num <= temp;
end process;
end rtl2;

architecture rtl3 of countone is
begin
    comb : process(din)
        constant parts : integer := 4;
    variable temp : std_logic_vector(5 downto 0);
    variable temp1 : std_logic_vector(5 downto 0);
begin
    temp := (others => '0');
    for j in 0 to parts -1 loop
        temp1 := (others => '0');
        for k in 32/parts-1 downto 0 loop
        if (din(32/parts * j + k) = '1') then
        temp1 := temp1 + 1;
        end if;
        end loop;
        temp := temp + temp1;
    end loop;
    num <= temp;
end process;
end rtl3;

architecture rtl4 of countone is
begin
    comb : process(din)
        variable temp : std_logic_vector(5 downto 0);
    variable cin, cout : std_logic;
begin
    temp := (others => '0');
    for j in din'reverse_range loop
        if din(j) = '1' then
        cin := '1';
        for k in temp'reverse_range loop
        cout := temp(k) and cin;
        temp(k) := temp(k) xor cin;
        cin := cout;
        end loop;
        end if;
    end loop;
    num <= temp;
end process;
end rtl4;

library ieee;
    use ieee.std_logic_1164.all;

entity tbcountone is
end entity;

architecture beh of tbcountone is

    component countone port(
        din : in std_logic_vector(31 downto 0);
        num : out std_logic_vector(5 downto 0));
end component;

signal din : std_logic_vector(31 downto 0);
signal y1,y2,y3,y4 : std_logic_vector(5 downto 0);

constant period : time := 5 ns;
constant strobe : time := period -1 ns;
begin
    p0 : process
        variable q : std_logic_vector(31 downto 0);
    begin
        din <= (others => '0');
        wait for period;
        q := (others => '0');
        loop
        din <= q;
        wait for period;
        q := q(30 downto 0) & (q(31) xor (not q(2)));
        end loop;
    end process;

    check : process
    begin
        wait for strobe;
        loop
        if(y1 /= y2) or (y2 /= y3) or (y3 /= y4) then
        assert false report "no match" severity warning;
        end if;
        wait for period;
        end loop;
    end process;

    countone1 : countone port map(din => din, num => y1);
    countone2 : countone port map(din => din, num => y2);
    countone3 : countone port map(din => din, num => y3);
    countone4 : countone port map(din => din, num => y4);
end beh;

configuration cfg_tbcountone of tbcountone is
    for beh
    for countone1 : countone
    use entity work.countone(rtl1);
end for;
for countone2 : countone
use entity work.countone(rtl2);
end for;
for countone3 : countone
use entity work.countone(rtl3);
end for;
for countone4 : countone
use entity work.countone(rtl4);
end for;
end for;
end configuration;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity leadzero is port(
    din : in std_logic_vector(31 downto 0);
    zero : out std_logic_vector(4 downto 0));
end leadzero;

architecture rtl1 of leadzero is
begin
    p0 : process(din)
        variable num : std_logic_vector(4 downto 0);
begin
    num := (others => '0');
    for j in 31 downto 0 loop
        if din(j) = '0' then
        num := num +1;
        else exit;
    end if;
end loop;
zero <= num;
end process;
end rtl1;

architecture rtl2 of leadzero is
begin
    p0 : process(din)
        variable num : std_logic_vector(4 downto 0);
    variable cin, cout : std_logic;
begin
    num := (others => '0');
    for j in 31 downto 0 loop
        if(din(j) = '0') then
        cin := '1';
        for k in 0 to 4 loop
        cout := num(k) and cin;
        num(k):= num(k) xor cin;
        cin := cout;
        if cout = '0' then
        exit; end if;
        end loop;
        else
        exit;
        end if;
        end loop;
        zero <= num;
    end process;
end rtl2;

architecture rtl3 of leadzero is
begin
    p0 : process(din)
        variable zvec : std_logic_vector(31 downto 0);
begin
    zvec := (others => '0');
    zero <= (others => '0');
    for j in 0 to 31 loop
        if din(31 downto j) = zvec(31 downto j) then
        zero <= "00000" -j;
        exit;
        end if;
    end loop;
end process;
end rtl3;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_arith.all;
    use ieee.std_logic_textio.all;
    use std.textio.all;

entity tbleadzero is generic(
    period : time := 50 ns;
    strobe : time := 45 ns;
    filename : string := "tb.out");
end tbleadzero;

architecture beh of tbleadzero is
    component leadzero port(
        din : in std_logic_vector(31 downto 0);
        zero : out std_logic_vector(4 downto 0));
end component;

signal din : std_logic_vector(31 downto 0);
signal y, y1, y2, y3 : std_logic_vector(4 downto 0);
begin
    p0: process
    begin
        for j in 31 downto 0 loop
        y <= conv_std_logic_vector(j,5);
        din <= (others => '0');
        din(31-j) <= '1';
        wait for period;
        end loop;
        din <= (others => '0');
        y <= "00000";
        wait;
    end process;

    check : process
        variable err_cnt : integer := 0;
        file fout : text is out filename;
        variable l : line;
    begin
        wait for strobe;
        if y /= y1 or y /= y2 or y /= y3 then
        write(l, string'("not compared at time "));
        write(l,now);
        writeline(fout,l);
        err_cnt := err_cnt +1;
        end if;
        wait for period;
        if err_cnt = 0 then
        write(l, string'("test pass"));
        else
        write(l, string'("test fail"));
        end if;
        writeline(fout, l);
        wait;
    end process;

    leadzero1 : leadzero
        port map(din => din, zero => y1);
    leadzero2 : leadzero
        port map(din => din, zero => y2);
    leadzero3 : leadzero
        port map(din => din, zero => y3);
end beh;

configuration cfg_tbleadzero of tbleadzero is
    for beh
    for leadzero1 : leadzero
    use entity work.leadzero(rtl1);
end for;
for leadzero2 : leadzero
use entity work.leadzero(rtl2);
end for;
for leadzero3 : leadzero
use entity work.leadzero(rtl3);
end for;
end for;
end configuration;

library ieee;
    use ieee.std_logic_1164.all;

entity chop is port(
    clk, clkn, rstn, source : in std_logic;
    tgt_h, tgt_fh, tgt_f, tgt_ff : out std_logic);
--source is the signal that is long and will be chopped
--tgt_h chops source at the first falling_edge of clk
--tgt_fh chops source at full half of clk period starting at falling_edge clk
--tgt_f chops source at first rising_edge clk
--tgt_ff chops source having a full length of clk starting at first rising_edge clk
end chop;

architecture rtl of chop is
    signal ffh0, ffh1, fff0, fff1 : std_logic;
begin
    posedge : process(rstn, clk)
    begin
        if(rstn = '0') then
        fff0 <= '0';
        fff1 <= '0';
        ffh1 <= '0';
        elsif rising_edge(clk) then
        fff0 <= source;
        fff1 <= fff0;
        ffh1 <= ffh0;
        end if;
    end process;
    tgt_f <= (not source) nor fff0;
    tgt_ff <= (not fff0) nor fff1;

    negedge : process(rstn, clkn)
    begin
        if rstn = '0' then
        ffh0 <= '0';
        elsif rising_edge(clkn) then
        ffh0 <= source;
        end if;
    end process;
    tgt_h <= (not source) nor ffh0;
    tgt_fh <= (not ffh0) nor ffh1;
end rtl;

library ieee;
    use ieee.std_logic_1164.all;

entity tbchop is
end entity;

architecture beh of tbchop is
    component chop is port(
        clk, clkn, rstn, source : in std_logic;
        tgt_h, tgt_fh, tgt_f, tgt_ff : out std_logic);
end component;

constant halfclk : time := 50 ns;
constant delay : time := 30 ns;

signal clk, clkn, rstn, source : std_logic;
signal tgt_h, tgt_fh, tgt_f, tgt_ff : std_logic;
begin
    rstn <= '1', '0' after halfclk *3 + delay,
    '1' after halfclk *7 + delay;
    clkp : process
    begin
        clk <= '0'; wait for halfclk;
        clk <= '1'; wait for halfclk;
    end process;

    clkn <= not clk;

    datap : process
        variable vec : std_logic_vector(7 downto 0) := "01100011";
    begin
        vec := vec(6 downto 0) & (vec(7) xor (not vec(2)));
        source <= '0' after delay;
        wait until rising_edge(clk);
        if vec(6) = '1' then
        wait until falling_edge(clk);
        end if;
        source <= '1' after delay;
        for j in 1 to 4 loop
        wait until rising_edge(clk);
        end loop;
    end process;

    chop0 : chop
        port map(clk => clk, clkn => clkn, rstn => rstn, source => source,
        tgt_h => tgt_h, tgt_fh => tgt_fh, tgt_f => tgt_f, tgt_ff => tgt_ff);
end beh;

--signal target1 is asserted at the same time as source and deasserted at
--the first rising edge of the clk when source is deasserted. target2 is
--asserted at the rising edge of the clk and deasserted two clk rising
--edges after source is deasserted. target3 is asserted at the same time
--as source and deasserted two clock rising edges after source is deasserted.
--tail1 is asserted when source is deasserted. tail2 is exactle one full clock cycle wide.

library ieee;
    use ieee.std_logic_1164.all;

entity extend is port(
    clk, rstn, source : in std_logic;
    trgt1, trgt2, trgt3, tail1, tail2 : out std_logic);
end extend;

architecture rtl of extend is
    signal ff0, ff1 : std_logic;
begin
    posedge : process(rstn, clk)
    begin
        if rstn = '0' then
        ff0 <= '0';
        ff1 <= '0';
        elsif rising_edge(clk) then
        ff0 <= source;
        ff1 <= ff0;
        end if;
    end process;

    trgt1 <= source or ff0;
    trgt2 <= ff0 or ff1;
    trgt3 <= source or ff0 or ff1;

    tail1 <= source nor (not ff0);
    tail2 <= ff0 nor (not ff1);
end rtl;

library ieee;
    use ieee.std_logic_1164.all;

entity tbextend is
end entity;

architecture beh of tbextend is
    component extend is port(
        clk, rstn, source : in std_logic;
        trgt1, trgt2, trgt3, tail1, tail2 : out std_logic);
end component;

signal clk, rstn, source : std_logic;
signal trgt1, trgt2, trgt3, tail1, tail2 : std_logic;

constant halfclk : time := 50 ns;
constant delay : time := 30 ns;
begin
    rstn <= '1', '0' after halfclk *3 + delay,
    '1' after halfclk *7 + delay;
    clkp : process
    begin
        clk <= '1'; wait for halfclk;
        clk <= '0'; wait for halfclk;
    end process;

    datap : process
        variable vec : std_logic_vector(7 downto 0) := "01111001";
    begin
        vec := vec(6 downto 0) & (vec(7) xor (not vec(2)));
        source <= '0' after delay;
        wait until rising_edge(clk);
        if vec(6) = '1' then
        wait until falling_edge(clk);
        end if;
        source <= '1' after delay;
        for j in 1 to 4 loop
        wait until rising_edge(clk);
        end loop;
    end process;

    extend0 : extend
        port map(clk => clk, rstn => rstn, source => source, trgt1 => trgt1,
        trgt2 => trgt2, trgt3 => trgt3, tail1 => tail1, tail2 => tail2);
end beh;

--JK Flip Flop
--JK "00" - no change
--JK "01" - flip flop is cleared to '0'
--JK "10" - flip flop is set to '1'
--JK "11" - flip flop reversed

library ieee;
    use ieee.std_logic_1164.all;

entity my_jkff is port(
    clk, rstn, j, k : in std_logic;
    q, qn : out std_logic);
end my_jkff;

architecture rtl of my_jkff is
    signal ff : std_logic;
begin
    jkff0 : process(clk, rstn)
        variable jk : std_logic_vector(1 downto 0);
begin
    if rstn = '0' then
        ff <= '0';
    elsif rising_edge(clk) then
        jk := j & k;
        case jk is
        when "01" => ff <= '0';
        when "10" => ff <= '1';
        when "11" => ff <= not ff;
        when others => ff <= ff;
        end case;
    end if;
end process;

q <= ff after 2 ns; qn <= not ff after 2 ns;
end rtl;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity pwm_mod is port(
    clk, rst : std_logic;
    led0: out std_logic);
end entity;

architecture arch of pwm_mod is
    signal clk_div_reg, clk_div_next : unsigned (13 downto 0);
    signal pwm0_reg, pwm0_next, pwm1_reg, pwm1_next : unsigned (7 downto 0);
    signal led_inv_0, led_inv_1, clk_div : std_logic;
begin

    process(clk, rst)
    begin
        if rst = '0' then
        clk_div_reg <= (others => '0');
        elsif rising_edge(clk) then
        clk_div_reg <= clk_div_next;
        end if;
    end process;

    clk_div_next <= (others => '0') when clk_div_reg = 5000 else clk_div_reg + 1;

    clk_div <= '1' when clk_div_reg = 5000 else '0';

    process(clk_div, rst)
    begin
        if rst = '0' then
        pwm0_reg <= (others => '0');
        pwm1_reg <= (others => '0');
        elsif rising_edge(clk_div) then
        pwm0_reg <= pwm0_next;
        pwm1_reg <= pwm1_next;
        end if;
    end process;

    pwm0_next <= (others => '0') when pwm0_reg = 254 else pwm0_reg + 1;
    pwm1_next <= (others => '0') when pwm1_reg = 252 else pwm1_reg + 1;

    led_inv_0 <= '1' when pwm0_reg > 127 else '0';
    led_inv_1 <= '1' when pwm1_reg > 126 else '0';
    led0 <= led_inv_0 xor led_inv_1;

end arch;

library ieee;
    use ieee.std_logic_1164.all;

entity flag_buf is
    generic(w: integer := 8);
    port(
        clk, rst: in std_logic;
        clr_flag, set_flag: in std_logic;
        din: in std_logic_vector(w-1 downto 0);
        dout: out std_logic_vector(w-1 downto 0);
        flag: out std_logic);
end flag_buf;

architecture arch of flag_buf is
    signal buf_reg, buf_next: std_logic_vector(w-1 downto 0);
    signal flag_reg, flag_next: std_logic;
begin
    --ff & register
    process(clk, rst)
    begin
        if rst = '1' then
        buf_reg <= (others => '0');
        flag_reg <= '0';
        elsif(rising_edge(clk)) then
        buf_reg <= buf_next;
        flag_reg <= flag_next;
        end if;
    end process;
    --next-state logic
    process(buf_reg, flag_reg, set_flag, clr_flag, din)
    begin
        buf_next <= buf_reg;
        flag_next <= flag_reg;
        if (set_flag = '1') then
        buf_next <= din;
        flag_next <= '1';
        elsif (clr_flag = '1') then
        flag_next <= '0';
        end if;
    end process;
    --output logic
    dout <= buf_reg;
    flag <= flag_reg;
end arch;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee. numeric_std.all;

entity uart_tx is
    generic(
        dbit: integer := 8; --# data bits
        sb_tick: integer := 16); --# ticks for stop bits
    port(
        clk, rst: in std_logic;
        tx_start: in std_logic;
        s_tick: in std_logic;
        din: in std_logic_vector(7 downto 0);
        tx_done_tick: out std_logic;
        tx: out std_logic);

end uart_tx;

architecture arch of uart_tx is
    type state_type is(idle, start, data, stop);
    signal state_reg, state_next: state_type;
    signal s_reg, s_next: unsigned(3 downto 0);
    signal n_reg, n_next: unsigned(2 downto 0);
    signal b_reg, b_next: std_logic_vector(7 downto 0);
    signal tx_reg, tx_next: std_logic;
begin
    --FSMD state & data registers
    process(clk, rst)
    begin
        if rst = '1' then
        state_reg <= idle;
        s_reg <= (others => '0');
        n_reg <= (others => '0');
        b_reg <= (others => '0');
        tx_reg <= '1';
        elsif rising_edge(clk) then
        state_reg <= state_next;
        s_reg <= s_next;
        n_reg <= n_next;
        b_reg <= b_next;
        tx_reg <= tx_next;
        end if;
    end process;
    --next-state logic & data path function units/routing
    process(state_reg, s_reg, n_reg, b_reg, s_tick, tx_reg, tx_start, din)
    begin
        state_next <= state_reg;
        s_next <= s_reg;
        n_next <= n_reg;
        b_next <= b_reg;
        tx_next <= tx_reg;
        tx_done_tick <= '0';

        case state_reg is
        when idle =>
        tx_next <= '1';
        if tx_start = '1' then
        state_next <= start;
        s_next <= (others => '0');
        b_next <= din;
        end if;

        when start =>
        tx_next <= '0';
        if (s_tick = '1') then
        if s_reg = 15 then
        state_next <= data;
        s_next <= (others => '0');
        n_next <= (others => '0');
        else
        s_next <= s_reg +1;
        end if;
        end if;

        when data =>
        tx_next <= b_reg(0);
        if s_tick = '1' then
        if s_reg = 15 then
        s_next <= (others => '0');
        b_next <= '0' & b_reg(7 downto 1);
        if n_reg = dbit-1 then
        state_next <= stop;
        else
        n_next <= n_reg +1;
        end if;
        else
        s_next <= s_reg +1;
        end if;
        end if;

        when stop =>
        tx_next <= '1';
        if s_tick = '1' then
        if s_reg = sb_tick -1 then
        state_next <= idle;
        tx_done_tick <= '1';
        else
        s_next <= s_reg +1;
        end if;
        end if;

        end case;
    end process;
    tx <= tx_reg;
end arch;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity uart is
    generic(
        --default setting:
        --19200 baud, 8 data bits, 1 stop bit, 2^2 FIFO
        dbit: integer := 8; --# data bits
        sb_tick: integer := 16; --# ticks for stop bits, 16/24/32
        --for 1/1.5/2 stop bits
        dvsr: integer := 163; --baud rate divisor
        --dvsr = 50M/(16*baud rate)
        dvsr_bit: integer := 8; --#bits of dvsr
        fifo_w: integer := 2); --#addr bits of FIFO
    --#words in FIFO = 2^fifo_w
    port(
        -- clk, rst: in std_logic;
        -- rd_uart, wr_uart: in std_logic;
        -- rx: in std_logic;
        -- w_data: in std_logic_vector(7 downto 0);
        -- tx_full, rx_empty: out std_logic;
        r_data: out std_logic_vector(7 downto 0);
        -- tx: out std_logic);
        clk, rst: in std_logic;
        rx_done_tick: out std_logic;
        rx: in std_logic);
end uart;

architecture str_arch of uart is
    signal tick: std_logic;
    -- signal rx_done_tick: std_logic;
    -- signal tx_fifo_out: std_logic_vector(7 downto 0);
    signal rx_data_out: std_logic_vector(7 downto 0);
    -- signal tx_empty, tx_fifo_not_empty: std_logic;
    -- signal tx_done_tick: std_logic;

begin
    baud_gen_unit: entity work.mod_m_counter(arch)
        generic map(m => dvsr, n => dvsr_bit)
        port map(clk => clk, rst => rst, q => open, max_tick => tick);

    uart_rx_unit: entity work.uart_rx(arch)
        generic map(dbit => dbit, sb_tick => sb_tick)
        port map(clk => clk, rst => rst, rx => rx, s_tick => tick,
        rx_done_tick => rx_done_tick, data_out => r_data);

    -- fifo_rx_unit: entity work.fifo(arch)
    -- generic map(b => dbit, w => fifo_w)
    -- port map(clk => clk, rst => rst, rd => rd_uart, wr => rx_done_tick,
    -- w_data => rx_data_out, empty => rx_empty, full => open, r_data => r_data);

    -- fifo_tx_unit: entity work.fifo(arch)
    -- generic map(b => dbit, w => fifo_w)
    -- port map(clk => clk, rst => rst, rd => tx_done_tick, wr => wr_uart, w_data => w_data,
    -- empty => tx_empty, full => tx_full, r_data => tx_fifo_out);
    --
    -- uart_tx_unit: entity work.uart_tx(arch)
    -- generic map(dbit => dbit, sb_tick => sb_tick)
    -- port map(clk => clk, rst => rst, tx_start => tx_fifo_not_empty, s_tick => tick,
    -- din => tx_fifo_out, tx_done_tick => tx_done_tick, tx => tx);
    --
    -- tx_fifo_not_empty <= not tx_empty;
end str_arch;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity uart is port(
    clk, rx : in std_logic;
    rst : in boolean;
    tx : out std_logic);
end uart;

architecture str_arch of uart is
    signal ld, rxready, load, ready: std_logic;
    signal din, dout, data_in, data_out: std_logic_vector(7 downto 0);

begin
    tx_rx_unit: entity work.uartmodule(arch)
        port map(clk => clk, rst => rst, tx => tx, rx => rx, ld => ld, din => din, dout => dout, rxready => rxready);

    acc_unit: entity work.accumulator(arch)
        port map(clk => clk, rst => rst, data_out => din, data_in => dout,
        load => ld, ready => rxready);

end str_arch;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity uart_test is port(
    clk, rst: in std_logic;
    btn: std_logic_vector(2 downto 0);
    rx: in std_logic;
    tx: out std_logic;
    led: out std_logic_vector(7 downto 0);
    sseg: out std_logic_vector(7 downto 0);
    an: out std_logic_vector(3 downto 0));
end uart_test;

architecture arch of uart_test is
    signal tx_full, rx_empty: std_logic;
    signal rec_data, rec_data1: std_logic_vector(7 downto 0);
    signal btn_tick: std_logic;
begin
    --instantiate uart
    uart_unit: entity work.uart(str_arch)
        port map(clk => clk, rst => rst, rd_uart => btn_tick,
        wr_uart => btn_tick, rx => rx, w_data => rec_data1,
        tx_full => tx_full, rx_empty => rx_empty,
        r_data => rec_data, tx => tx);

    --increment data loop back
    rec_data1 <= std_logic_vector(unsigned(rec_data)+1);
    --led display
    led <= rec_data;
    an <= "1110";
    sseg <= '1' & (not tx_full) & "11" & (not rx_empty) & "111";
end arch;

--https://www.youtube.com/watch?v=Fimf3jypV_o

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity uartmodule is port(
    clk, ld, rx : in std_logic;
    rst : in boolean;
    din : in std_logic_vector(7 downto 0);
    dout : out std_logic_vector(7 downto 0);
    tx, txbusy, rxready : out std_logic);
end uartmodule;

architecture arch of uartmodule is
    constant width_1 : natural := 8;
    constant width_2 : natural := 7;

    type tx_state is (idle_tx, shift_tx);
    signal txfsm : tx_state;

    type rx_state is (idle_rx, shift_rx);
    signal rxfsm : rx_state;

    signal tx_reg : std_logic_vector(9 downto 0);
    signal txbitcnt : unsigned(3 downto 0);
    signal txclkdiv : unsigned(width_1 downto 0);
    signal txclkdiv_sum : unsigned(width_1 +1 downto 0);
    signal ticktx : std_logic;
    signal txclkena : std_logic;

    signal rx_reg : std_logic_vector(9 downto 0);
    signal rxbitcnt : unsigned(4 downto 0);
    signal rxclkdiv : unsigned(width_2 downto 0);
    signal rxclkdiv_sum : unsigned(width_2 +1 downto 0);
    signal tickrx : std_logic;
    signal rxclkena : std_logic;

begin

    --clk divider tx
    txclkdiv_sum <= resize(txclkdiv,width_1 +2) -1;
    process(clk,rst)
    begin
        if not rst then
        txclkdiv <= "110110010";
        elsif rising_edge(clk) then
        if ticktx = '1' then
        txclkdiv <= "110110010";
        elsif txclkena = '1' then
        txclkdiv <= txclkdiv_sum(width_1 downto 0);
        end if;
        end if;
    end process;
    ticktx <= txclkdiv_sum(width_1 +1);

    --clk divider rx
    rxclkdiv_sum <= resize(rxclkdiv,width_2 +2) -1;
    process(clk,rst)
    begin
        if not rst then
        rxclkdiv <= "01101001";
        elsif rising_edge(clk) then
        if tickrx = '1' then
        rxclkdiv <= "01101001";
        elsif rxclkena = '1' then
        rxclkdiv <= rxclkdiv_sum(width_2 downto 0);
        end if;
        end if;
    end process;
    tickrx <= rxclkdiv_sum(width_2 +1);

    --transmit state machine
    tx_fsm: process(clk, rst)
    begin
        if not rst then
        tx_reg <= (others => '1');
        txbitcnt <= (others => '0');
        txfsm <= idle_tx;
        txbusy <= '0';
        elsif rising_edge(clk) then
        case txfsm is
        when idle_tx =>
        if ld = '0' then --latch the input data immediately
        tx_reg <= '1' & din & '0'; --stop bit & data & start bit
        txbusy <= '1';
        txbitcnt <= "1010";
        txfsm <= shift_tx;
        txclkena <= '1';
        else
        txbusy <= '0';
        txclkena <= '0';
        end if;

        when shift_tx =>
        txbitcnt <= txbitcnt -1;
        tx_reg <= '1' & tx_reg(tx_reg'high downto 1);
        if txbitcnt = 0 then
        txfsm <= idle_tx;
        end if;

        when others =>
        txfsm <= idle_tx;
        end case;
        end if;
    end process;
    tx <= tx_reg(0);

    --receive state machine
    rx_fsm: process(clk, rst)
    begin
        if not rst then
        rx_reg <= (others => '0');
        rxbitcnt <= (others => '0');
        rxfsm <= idle_rx;
        elsif rising_edge(clk) then
        case rxfsm is
        when idle_rx => --wait on start bit
        if rx = '0' then
        rxfsm <= shift_rx;
        rxbitcnt <= "10101";
        rxclkena <= '1'; --synchronize the divisor
        else
        rxclkena <= '0';
        end if; --else false start, stay in idle

        when shift_rx => --sample data
        if tickrx = '1' then
        rxbitcnt <= rxbitcnt -1; --shift right
        rx_reg <= rx & rx_reg(rx_reg'high downto 1);
        if rxbitcnt <= 0 then
        rxfsm <= idle_rx;
        rxready <= '1';
        else rxready <= '0';
        end if;
        end if;

        when others =>
        rxfsm <= idle_rx;
        end case;
        end if;
    end process;
    dout <= rx_reg(8 downto 1);
end arch;

library ieee;
    use ieee.std_logic_1164.all;

entity tbacnt is
end tbacnt;

architecture beh of tbacnt is
    component acnt port(
        rstn, en : in std_logic;
        cntr : out std_logic_vector(7 downto 0));
end component;

signal rstn, en : std_logic;
signal cntr : std_logic_vector(7 downto 0);

constant halfclk : time := 50 ns;
constant delay : time := 30 ns;

begin
    rstn <= '1', '0' after halfclk *3 + delay,
    '1' after halfclk *7 + delay;

    datap : process
        variable vec : std_logic_vector(7 downto 0) := "01100101";
    begin
        vec := vec(6 downto 0) & (vec(7) xor (not vec(2)));
        en <= vec(7) after delay;
        wait for 2 * halfclk;
    end process;

    acnt0 : acnt
        port map( rstn => rstn, en => en, cntr => cntr);
end beh;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity scnt is port(
    clk, rstn, en : in std_logic;
    cntr : out std_logic_vector(7 downto 0));
end scnt;

architecture rtl of scnt is
    signal ff : std_logic_vector(7 downto 0);
begin
    process(clk, rstn)
    begin
        if rstn = '0' then
        ff <= (others => '0');
        elsif rising_edge(clk) then
        if en = '1' then
        ff <= ff +1;
        end if;
        end if;
    end process;
    cntr <= ff;
end rtl;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity scnt32 is port(
    clk, rstn, pl, en : in std_logic;
    din : in std_logic_vector(31 downto 0);
    ec : out std_logic;
    cntr : out std_logic_vector(31 downto 0));
end scnt32;

architecture rtl1 of scnt32 is
    signal ff : std_logic_vector(31 downto 0);
begin
    scnt32_0 : process(rstn, clk)
    begin
        if rstn = '0' then
        ff <= (others => '0');
        elsif rising_edge(clk) then
        if pl = '1' then
        ff <= din;
        elsif en = '1' then
        if ff < x"8CEF8CEF" then
        ff <= ff +1;
        else ff <= (others => '0');
        end if;
        end if;
    end if;
end process;

cntr <= ff;
ec <= '1'when ff = x"8CEF8CEF" and en = '1' else '0';
end rtl1;

architecture rtl2 of scnt32 is
    signal ff : std_logic_vector(31 downto 0);
begin
    scnt32_1 : process(rstn, clk)
    begin
        if rstn = '0' then
        ff <= (others => '0');
        ec <= '0';
        elsif rising_edge(clk) then
        if pl = '1' then
        ff <= din;
        ec <= '0';
        elsif en = '1' then
        if ff < x"8CEF8CEF" then
        ec <= '1';
        ff <= (others => '0');
        else
        ec <= '0';
        ff <= ff +1;
        end if;
        end if;
        end if;
    end process;

    cntr <= ff;
end rtl2;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity tbscnt32 is
end entity;

architecture beh of tbscnt32 is
    component scnt32 is port(
        clk, rstn, pl, en : in std_logic;
        din : in std_logic_vector(31 downto 0);
        ec : out std_logic;
        cntr : out std_logic_vector(31 downto 0));
end component;

constant period : time := 50 ns;
constant delay : time := 80 ns;
constant strobe : time := 2 *period -5 ns;

signal clk, rstn, pl, en : std_logic;
signal din, cntr1, cntr2 : std_logic_vector(31 downto 0);
signal ec1, ec2, diff : std_logic;

begin
    rstn <= '0', '1' after 10 * period;
    clkgen : process
    begin
        clk <= '0'; wait for period;
        clk <= '1'; wait for period;
    end process;

    dgen : process
    begin
        pl <= '0'; en <= '0';
        din <= (others => '0'); din(1) <= '1';
        for k in 0 to 15 loop
        wait until rising_edge(clk);
        end loop;

        en <= '1' after delay;

        for k in 0 to 15 loop
        wait until rising_edge(clk);
        end loop;

        pl <= '1' after delay;
        wait until rising_edge(clk);
        pl <= '0' after delay;

        for k in 0 to 15 loop
        wait until rising_edge(clk);
        end loop;

        din <= x"8CEF8CED" after delay;

        pl <= '1' after delay;
        wait until rising_edge(clk);
        pl <= '0' after delay;

        for k in 0 to 15 loop
        wait until rising_edge(clk);
        end loop;

        pl <= '1' after delay;
        din <= x"8CEF8CFF" after delay;
        wait until rising_edge(clk);
        pl <= '0' after delay;

        for k in 0 to 15 loop
        wait until rising_edge(clk);
        end loop;
    end process;

    diff <= '0' when(ec1 = ec2) and (cntr1 = cntr2) else '1';

    check : process
    begin
        loop
        wait until rising_edge(clk);
        wait for strobe;
        assert (diff = '0') report "not equal" severity note;
        end loop;
    end process;
    scnt32_0 : scnt32
        port map(clk => clk, rstn => rstn, pl => pl, en => en, din => din, ec => ec1, cntr => cntr1);
    scnt32_1 : scnt32
        port map(clk => clk, rstn => rstn, pl => pl, en => en, din => din, ec => ec2, cntr => cntr2);
end beh;

configuration cfg_tbscnt32 of tbscnt32 is
    for beh
    for scnt32_0 : scnt32
    use entity work.scnt32(rtl1);
end for;
for scnt32_1 : scnt32
use entity work.scnt32(rtl2);
end for;
end for;
end cfg_tbscnt32;

library ieee;
    use ieee.std_logic_1164.all;

entity shiftr is port(
    clk, rstn, si, pl, en, lrn : in std_logic;
    din : in std_logic_vector(7 downto 0);
    so : out std_logic);
end entity;

architecture rtl1 of shiftr is
    signal ff8 : std_logic_vector(7 downto 0);
begin
    posedge : process(clk, rstn)
    begin
        if rstn = '0' then
        ff8 <= (others => '0');
        elsif rising_edge(clk) then
        if pl = '1' then
        ff8 <= din;
        elsif en = '1' then
        if lrn = '1' then
        ff8 <= si & ff8(ff8'high downto 1);
        else ff8 <= ff8(ff8'high -1 downto 0) & si;
        end if;
        end if;
    end if;
end process;

so <= ff8(ff8'low) when lrn = '1' else ff8(ff8'high);
end rtl1;

architecture rtl2 of shiftr is
    signal ff8 : std_logic_vector(din'range);
begin
    posedge : process(clk, rstn)
    begin
        if rstn = '0' then
        ff8 <= (others => '0');
        so <= '0';
        elsif rising_edge(clk) then
        if pl = '1' then
        ff8 <= din;
        --so <= '0';
        elsif en = '1' then
        if lrn = '1' then
        ff8 <= si & ff8(ff8'high downto 1);
        so <= ff8(ff8'low);
        else
        ff8 <= ff8(ff8'high -1 downto 0) & si;
        so <= ff8(ff8'high);
        end if;
        end if;
        end if;
    end process;

end rtl2;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity tbshiftr is
end entity;

architecture beh of tbshiftr is
    component shiftr port(
        clk, rstn, si, pl, en, lrn : in std_logic;
        din : in std_logic_vector(7 downto 0);
        so : out std_logic);
end component;

constant period : time := 50 ns;
constant delay : time := 80 ns;
constant strobe : time := 2 *period -5 ns;

signal clk, rstn, si, pl, en, lrn : std_logic;
signal din : std_logic_vector(7 downto 0) := (others => '0');
signal so1, so2 : std_logic;
begin
    rstn <= '0','1' after period *3; --1 after 150ns

    clkgen : process
    begin
        clk <= '1'; wait for period; --change ebery 50ns
        clk <= '0'; wait for period;
    end process;

    dgen : process --all 'after 80ns happen together at the same time until rising_edge
    begin
        for i in 0 to 1 loop --resets after 1 to 0
        if (i = 0) then
        si <= '0' after delay; --after 80ns AA
        else
        si <= '1' after delay;
        end if;
        for j in 0 to 1 loop
        din <= din(6 downto 0) & (not din(7) xor din(2)) after delay; --after 80ns AA
        lrn <= din(7) after delay; --after 80ns AA
        pl <= '1' after delay; --after 80ns AA
        wait until rising_edge(clk);
        lrn <= din(4) after delay; --after 180ns BB
        pl <= '0' after delay; --after 180ns BB
        wait until rising_edge(clk);
        for k in 0 to 15 loop
        wait until rising_edge(clk);
        end loop;
        end loop;
        end loop;
    end process;

    check : process
    begin
        loop
        wait until rising_edge(clk);
        wait for strobe;
        assert (so1 = so2) report "not compared" severity note;
        end loop;
    end process;

    shiftr0 : shiftr
        port map (clk => clk, rstn => rstn, si => si, pl => pl, en => en, lrn => lrn, din => din, so => so1);

    shiftr1 : shiftr
        port map (clk => clk, rstn => rstn, si => si, pl => pl, en => en, lrn => lrn, din => din, so => so2);

end beh;

configuration cfg_tbshift of tbshiftr is
    for beh
    for shiftr0 : shiftr
    use entity work.shiftr(rtl1);
end for;

for shiftr1 : shiftr
use entity work.shiftr(rtl2);
end for;
end for;
end configuration;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee. std_logic_unsigned.all;

entity lfsr is port(
    clk, rstn : in std_logic;
    cnt : out std_logic_vector(3 downto 0));
end lfsr;

architecture rtl of lfsr is
    signal ff : std_logic_vector(cnt'range);
begin
    posedge : process(clk, rstn)
    begin
        if rstn = '0' then
        ff <= (others => '0');
        elsif rising_edge(clk) then
        ff <= ff(2 downto 0) & not(ff(0) xor ff(3));
        end if;
    end process;
    cnt <= ff;
end rtl;

--architecture rtl1 of lfsr is
-- signal ff : std_logic_vector(3 downto 0);
--begin
-- posedge : process(clk, rstn)
-- begin
-- if rstn = '0' then
-- ff <= (others => '0');
-- elsif rising_edge(clk) then
-- ff(0) <= not(ff(3) xor ff(0));
-- ff(1) <= ff(0);
-- ff(2) <= ff(1);
-- ff(3) <= ff(2);
-- end if;
-- end process;
--
-- cnt <= ff;
--end rtl1;

--architecture rtl of lfsr is
-- signal ff : std_logic_vector(cnt'range);
--begin
-- posedge : process(clk, rstn)
-- begin
-- if rstn = '0' then
-- ff <= (others => '0');
-- elsif rising_edge(clk) then
-- ff <= ff +1;
-- end if;
-- end process;
-- cnt <= ff;
--end rtl;

library ieee;
    use ieee.std_logic_1164.all;

entity otm is port(
    rstn, clk : in std_logic;
    so : out std_logic);
end entity;

architecture rtl of otm is
    signal ff : std_logic_vector(7 downto 0);
    constant seed : std_logic_vector(7 downto 0) := (others => '1');
begin
    lfsr : process(rstn, clk)
    begin
        if rstn = '0' then
        ff <= seed;
        elsif rising_edge(clk) then
        ff(0) <= ff(7);
        ff(1) <= ff(0);
        ff(2) <= ff(1) xor ff(7);
        ff(3) <= ff(2) xor ff(7);
        ff(4) <= ff(3) xor ff(7);
        ff(7 downto 5) <= ff(6 downto 4);
        end if;
    end process;

    so <= ff(7);
end rtl;

library ieee;
    use ieee.std_logic_1164.all;
    use work.pack.all;

entity p2s is port(
    rstn, clk, pl : in std_logic;
    din : in std_logic_vector(7 downto 0);
    serout : out std_logic);
end p2s;

architecture rtl of p2s is
    signal dff : std_logic_vector(7 downto 0);
    signal start, parbit : std_logic;
begin
    p0 : process(rstn, clk)
    begin
        if rstn = '0' then
        start <= '0';
        parbit <= '0';
        dff <= (others => '0');
        elsif rising_edge(clk) then
        if pl = '1' then
        start <= '1';
        dff <= din;
        parbit <= reduce_xor(din);
        else
        start <= dff(7);
        dff <= dff(6 downto 0) & parbit;
        parbit <= '0';
        end if;
        end if;
    end process;
    serout <= start;
end rtl;

library ieee;
    use ieee.std_logic_1164.all;
package pack is
    function reduce_xor(din : in std_logic_vector) return std_logic;
end pack;

package body pack is
    function reduce_xor(din : in std_logic_vector) return std_logic is
        variable result : std_logic;
    begin
        result := '0';
        for i in din'range loop -- range' (high downto low)
        result := result xor din(i);
        end loop;
        return result;
    end reduce_xor;
end pack;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned;

entity tbp2s is end entity;

architecture beh of tbp2s is
    component p2s is port(
        rstn, clk, pl : in std_logic;
        din : in std_logic_vector(7 downto 0);
        serout : out std_logic);
end component;

signal rstn, clk, pl : std_logic;
signal din : std_logic_vector(7 downto 0) := (others => '0');
signal serout : std_logic;

constant period : time := 50 ns;
constant delay : time := 80 ns;

begin

    rstn <= '0', '1' after period *3;

    clock0 : process
    begin
        clk <= '0'; wait for period;
        clk <= '1'; wait for period;
    end process;

    tx0 : process
    begin
        for i in 0 to 1 loop
        din <= din(din'high -1 downto 0) & (not din(din'high) xor din(2)) after delay;
        pl <= '1' after delay;
        wait until rising_edge(clk);
        pl <= '0' after delay;
        for j in 0 to 8 loop
        wait until rising_edge(clk);
        end loop;
        end loop;
    end process;

    p2s0 : p2s
        port map(rstn => rstn, clk => clk, pl => pl, din => din ,serout => serout);

end beh;

configuration cfg_tbp2s of tbp2s is
    for beh end for;
end configuration;

-- signal clkdiv : std_logic_vector(4 downto 0);
--
-- clkdiv0 : process(clk, rstn)
-- begin
-- if rstn = '0' then
-- clkdiv <= (others => '0');
-- elsif rising_edge(clk) then
-- clkdiv <= clkdiv(3 downto 0) & not(clkdiv(4) xor clkdiv(1));
-- end if;
-- end process;
--
-- clk_trg <= not(clkdiv(4) or clkdiv(3) or clkdiv(2) or clkdiv(1) or clkdiv(0));

-- the transmission begins with the start bit, '1', serial data, 8-bit, followed by even parity.
-- after parity, drdy outputs '1' in the next clock cycle. Drdy is used to tell another circuit block to get the parallel data from dout right away,
-- otherwise data is lost when next word comes. This allows drdy and the start bit to be asserted at the same time.
-- dout's value is changed right after drdy is deasserted.

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;
    use work.pack.all;

--drdy is asserted when start bit, 8 data bits and parity are received. '1' when bit counter is max;
--perrn is deasserted whenthe parity received doesn't match the internaly generated parity
--parity error resets the circuit

entity s2p is port(
    rstn, clk, sin : in std_logic;
    perrn, drdy : out std_logic;
    dout : out std_logic_vector(7 downto 0));
end entity;

architecture rtl of s2p is
    signal dff : std_logic_vector(dout'range);
    signal cnt : std_logic_vector(2 downto 0);
    signal cnt7_ff, sl_en, normal : std_logic;
    signal perrn_ff, par_en, cnt_en : std_logic;
begin
    regs : process(clk, rstn)
    begin
        if rstn = '0' then
        dff <= (others => '0');
        normal <= '1';
        perrn_ff <= '1';
        drdy <= '0';
        par_en <= '0';
        cnt7_ff <= '0';
        cnt <= (others => '0');
        elsif rising_edge(clk) then
        if sl_en = '1' then
        dff <= dff(6 downto 0) & sin;
        end if;
        if perrn_ff = '0' then
        normal <= '0';
        end if;
        if cnt_en = '1' then
        cnt <= cnt +1;
        end if;
        if par_en = '1' then --par_en is for parity check ff
        perrn_ff <= not (reduce_xor(dff) xor sin);-- compare generated parity with received parity
        end if;
        drdy <= par_en;
        cnt7_ff <= cnt(2) and cnt(1) and cnt(0);
        par_en <= cnt7_ff;
        end if;
    end process;
    sl_en <= normal and (cnt7_ff or cnt(2) or cnt(1) or cnt(0));
    cnt_en <= '1' when(normal = '1') and (par_en = '0') and
    (cnt7_ff = '0') and (perrn_ff = '1') and
    ((cnt = "000" and sin = '1') or
     (cnt /= "000")) else '0';
        perrn <= perrn_ff;
        dout <= dff;
    end rtl;

    library ieee;
        use ieee.std_logic_1164.all;

    entity tbs2p is end entity;

    architecture beh of tbs2p is

        component s2p is port(
        rstn, clk, sin : in std_logic;
        perrn, drdy : out std_logic;
        dout : out std_logic_vector(7 downto 0));
    end component;

    signal rstn, clk, sin : std_logic;
    signal perrn, drdy : std_logic;
    signal dout : std_logic_vector(7 downto 0);

    constant period : time := 50 ns;
    constant delay : time := 25 ns;

begin

    rstn <= '0', '1' after period *3;

    clk0 : process
    begin
        clk <= '1'; wait for period;
        clk <= '0'; wait for period;
        if perrn = '0' then
        -- rstn <= '0'; wait for delay *3;
        -- rstn <= '1'; wait for delay *3;
        end if;
    end process;

    rx0 : process
        variable var : std_logic_vector(4 downto 0) := "01001";
    begin
        wait until rising_edge(clk);
        var := var(3 downto 0) & (var(4) xor var(2));
        sin <= var(3) after 1.5 us;
    end process;

    s2p0 : s2p
        port map(rstn => rstn, clk => clk, sin => sin, perrn => perrn, drdy => drdy, dout => dout);
end beh;

configuration cfg_tbs2p of tbs2p is
    for beh end for;
end configuration;

library ieee;
    use ieee.std_logic_1164.all;

entity itreg is port(
    rstn, clk : in std_logic;
    addr : in std_logic_vector(5 downto 0); -- 6 bit address input
    cben : in std_logic_vector(3 downto 0); -- command byte enable 4 bit active low. each bit controlls a byte lane
    adi : in std_logic_vector(31 downto 0); -- data to be written to registers
    wren : in std_logic;
    fifo_ovf : in std_logic; --indictes overflow
    dma_done : in std_logic; --indictes dma is done
    timer_int : in std_logic_vector(3 downto 0); --indictes timers are time out
    intn : in std_logic_vector(3 downto 0);
    intan : out std_logic; --active low indicated when interrupt is generated
    int_req : out std_logic_vector(9 downto 0); -- interrupt registers
    int_mask : out std_logic_vector(9 downto 0); -- interrupt registers
    int_pend : out std_logic_vector(9 downto 0));-- interrupt registers
end itreg;

architecture rtl of itreg is
    signal req, maskff, pendff : std_logic_vector(9 downto 0);
begin
    fegn : process(rstn, clk)
        variable int_or : std_logic;
begin
    if rstn = '0' then
        maskff <= (others => '0'); --interrupt mask register
        pendff <= (others => '0'); --interrupt pending register
        intan <= '1';
    elsif rising_edge(clk) then
        --interrupt mask register
        if wren = '1' and addr = "000000" and cben(0) = '0' then
        maskff(7 downto 0) <= adi(7 downto 0);
        --int mask reg is used to ena/dis any one of the interrupt sources
        end if;
        --interrupt mask register
        if wren = '1' and addr = "000000" and cben(1) = '0' then
        maskff(9 downto 8) <= adi(9 downto 8);
        end if;
        -- interrupt request register
        if wren = '1' and addr = "000010" and cben(0) = '0' then
        --clears all int pend reg when int req reg is written
        pendff(7 downto 0) <= "00000000";
        --interrupt pending register
        elsif wren = '1' and addr = "000001" and cben(0) = '0' then
        -- each individual interrupt pending bit can be cleared by writing '1';
        --int pend reg remembers interrupt sources that are in queue
        for j in 0 to 7 loop
        if adi(j) = '1' then
        pendff(j) <= '0';
        end if;
        end loop;
        else
        pendff(7 downto 0) <= (timer_int & (not intn)) or pendff(7 downto 0);
        -- if neither req / pend reg are written, pend reg remembers states and
        -- records incomming interrupts.
        end if;

        if wren = '1' and addr = "000010" and cben(1) = '0' then
        pendff(9 downto 8) <= "00";
        elsif wren = '1' and addr = "000001" and cben (1) = '0' then
        for j in 8 to 9 loop
        if adi(j) = '1' then
        pendff(j) <= '0';
        end if;
        end loop;
        else
        pendff(9 downto 8) <= (fifo_ovf & dma_done) or pendff(9 downto 8);
        end if;
        int_or := req(0);
        for i in 1 to req'length -1 loop
        int_or := int_or or req(i);
        end loop;
        intan <= not int_or;
    end if;
end process;
int_mask <= maskff;
int_pend <= pendff;
req <= pendff and maskff;
-- req reg is logic and of mask and pending regs.
int_req <= req;
end rtl;

-- the dma controller will start to transfer the data to the starting address. the
-- address is automatically incremented to transfer the next data until all the
-- words are transfered.

library ieee;
    use ieee.std_logic_1164.all;

entity spreg is port(
    rstn0, rstn1, clk0, clk1 : in std_logic;
    addr : in std_logic_vector(5 downto 0);
    cben : in std_logic_vector(3 downto 0); -- command byte enable 4 bit active low. each bit controlls a byte lane
    adi : in std_logic_vector(31 downto 0); -- data/control to be written to registers
    wren : in std_logic;
    dma_done : in std_logic; --indictes dma is done
    dma_en : out std_logic; -- control wheter the dma or fifo are enabled
    fifo_en : out std_logic; --dma control register bit 1
    soft_rstn : out std_logic; --dma control register bit 0
    dmaad : out std_logic_vector(31 downto 2); -- starting address register for data trasnfer
    dmaword : out std_logic_vector(31 downto 0)); -- number of words to transfer
end spreg;

architecture rtl of spreg is
begin
    fgen : process(rstn0, clk0)
    begin
        if rstn0 = '0' then
        soft_rstn <= '1';
        dma_en <= '0';
        fifo_en <= '0';
        elsif rising_edge(clk0) then
        soft_rstn <= '1';
        -- dma control
        if wren = '1' and addr = "010000" and cben(0) = '0' then
        dma_en <= adi(2);
        fifo_en <= adi(1);
        soft_rstn <= not adi(0);
        elsif dma_done = '1' then
        dma_en <= '0';
        end if;
        end if;
    end process;

    dmasgen : process(rstn0, clk0)
    begin
        if rstn0 = '0' then
        dmaad <= (others => '0');
        elsif rising_edge(clk0) then
        -- dma address
        if wren = '1' and addr = "010001" then
        for j in 1 to 3 loop
        if cben(j) = '0' then
        dmaad((j +1) *8 -1 downto j *8) <= adi((j +1) *8 -1 downto j *8);
        end if;
        if cben(0) = '0' then
        dmaad(7 downto 2) <= adi(7 downto 2);
        end if;
        end loop;
        end if;
        end if;
    end process;

    dmacntgen : process(rstn1, clk1)
    begin
        if rstn1 = '0' then
        dmaword <= (others => '0');
        elsif rising_edge(clk1) then
        -- dma word -> for dma to know how many words to transfer before dma_done is asserted.
        if wren = '1' and addr = "010010" then
        for j in 0 to 3 loop
        if cben(j) = '0' then
        dmaword((j +1) *8 -1 downto j *8) <= adi((j +1) *8 -1 downto j *8);
        end if;
        end loop;
        end if;
        end if;
    end process;
end rtl;

library ieee;
    use ieee.std_logic_1164.all;

entity regmux is port(
    clk : in std_logic;
    rstn : in std_logic;
    addr : in std_logic_vector(3 downto 0);
    adi : in std_logic_vector(31 downto 0);
    cben : in std_logic_vector(3 downto 0);
    cfg_wrn : in std_logic;
    m_abort : in std_logic; -- pci protocol
    t_abort : in std_logic; -- pci protocol
    bist_code : in std_logic_vector(4 downto 0);
    int_req : in std_logic_vector(9 downto 0);
    int_mask : in std_logic_vector(9 downto 0);
    int_pend : in std_logic_vector(9 downto 0);
    dma_en : in std_logic;
    fifo_en : in std_logic;
    fifocnt : in std_logic_vector(5 downto 0);
    dmaad : in std_logic_vector(31 downto 2);
    dmaword : in std_logic_vector(31 downto 0);
    dmacntr : in std_logic_vector(31 downto 0);
    rdaddr : in std_logic_vector(5 downto 0);
    bist_start : out std_logic; -- start build in self test circuit
    target_b2b : out std_logic;
    master_en : out std_logic;
    respond_en : out std_logic;
    base_addr : out std_logic_vector(11 downto 0);
    latency_pci : out std_logic_vector(4 downto 0);
    dout : out std_logic_vector(31 downto 0));
end regmux;

architecture rtl of regmux is
    constant asic_id : std_logic_vector(15 downto 0) := "0101010100100100";
    constant comp_id : std_logic_vector(15 downto 0) := "0001010101011100";
    constant class_code : std_logic_vector(23 downto 0) := "111111110000000000000000";
    constant revision : std_logic_vector(7 downto 0) := "00000010";
    constant basereg19_0 : std_logic_vector(19 downto 0) := "00000000000000000000";
    constant int_pin : std_logic_vector(7 downto 0) := "00000001";

    signal devid_reg : std_logic_vector(31 downto 0);
    signal devctl_reg : std_logic_vector(31 downto 0);
    signal revid_reg : std_logic_vector(31 downto 0);
    signal latency_reg : std_logic_vector(31 downto 0);
    signal base_reg : std_logic_vector(31 downto 0);
    signal basereg31_20 : std_logic_vector(11 downto 0);
    signal int_pin_reg : std_logic_vector(31 downto 0);
    signal mabort_ff : std_logic;
    signal tabort_ff : std_logic;
    signal target_b2b_ff : std_logic;
    signal master_en_ff : std_logic;
    signal respond_en_ff : std_logic;
    signal latency_ff : std_logic_vector(4 downto 0);
    signal int_line_ff : std_logic_vector(7 downto 0);
    signal bist_code_ff : std_logic_vector(3 downto 0);
    signal bist_start_ff, bist_start_dl : std_logic;
    signal ad3_0 : std_logic_vector(3 downto 0);
    signal ad1_0, ad5_4 : std_logic_vector(1 downto 0);
    signal itout, mask_reg, pend_reg, req_reg, dmaout,
    dmaad_reg, cfgout, dmactl_reg : std_logic_vector(31 downto 0);

begin
    target_b2b <= target_b2b_ff;
    master_en <= master_en_ff;
    respond_en <= respond_en_ff;
    devid_reg <= asic_id & comp_id;
    revid_reg <= class_code & revision;
    base_addr <= basereg31_20;
    latency_pci <= latency_ff;
    devctl_gen : process(rstn, clk)
    begin
        if rstn = '0' then
        mabort_ff <= '0';
        tabort_ff <= '0';
        target_b2b_ff <= '0'; -- default no back to back
        master_en_ff <= '0'; --default master not enabled
        respond_en_ff <= '0'; --default no respond
        elsif rising_edge(clk) then
        if cfg_wrn = '0' and addr = "0001" then
        if cben(1) = '0' then
        target_b2b_ff <= adi(9);
        end if;
        if cben(0) = '0' then
        master_en_ff <= adi(2);
        respond_en_ff <= adi(1);
        end if;
        end if;
        if(cfg_wrn = '0') and addr = "0001" and
        cben(3) = '0' and adi(29) = '1' then
        mabort_ff <= '0';
        elsif mabort_ff = '0' then
        mabort_ff <= m_abort;
        end if;
        if cfg_wrn = '0' and addr = "0001" and
        cben(3) = '0' and adi(28) = '1' then
        tabort_ff <= '0'; -- clear by writing 1
        elsif tabort_ff = '0' then -- when 0 clock in
        tabort_ff <= t_abort;
        end if;
        end if;
    end process;

    devctl_reg <= "00" & mabort_ff & tabort_ff & "001010000000" & "000000" &
        target_b2b_ff & "000000" & master_en_ff & respond_en_ff & '0';

    bist_start <= bist_start_ff and (not bist_start_dl);

    basereg_gen : process(rstn, clk)
    begin
        if rstn = '0' then
        basereg31_20 <= "111111000000";
        latency_ff <= "00000";
        int_line_ff <= "00000000";
        bist_start_ff <= '0';
        bist_start_dl <= '0';
        bist_code_ff <= "0000";
        elsif rising_edge(clk) then
        if cfg_wrn = '0' and addr = "0100" then
        if cben(3) = '0' then
        basereg31_20(11 downto 4) <= adi(31 downto 24);
        end if;
        if cben(2) = '0' then
        basereg31_20(3 downto 0) <= adi(23 downto 20);
        end if;
        end if;
        if cfg_wrn = '0' and addr = "0011" and cben(1) = '0' then
        latency_ff <= adi(15 downto 11);
        end if;
        if cfg_wrn = '0' and addr = "0011" and
        cben(3) = '0' and adi(30) = '1' then
        bist_start_ff <= '1'; --when write '1' start bist_code
        elsif (bist_code(4) = '0') then
        bist_start_ff <= '0'; -- clear when bist done
        end if;
        bist_start_dl <= bist_start_ff;
        bist_code_ff <= bist_code(3 downto 0);
        if cfg_wrn = '0' and addr = "1111" and cben(0) = '0' then
        int_line_ff <= adi(7 downto 0);
        end if;
        end if;
    end process;

    base_reg <= basereg31_20 & basereg19_0;
    latency_reg <= '1' & bist_start_ff & "00" & bist_code_ff & "00000000"
    & latency_ff & "00000000000";
    int_pin_reg <= "0000000000000000" & int_pin & int_line_ff;

    ad3_0 <= rdaddr(3 downto 0); ad1_0 <= rdaddr(1 downto 0);
    ad5_4 <= rdaddr(5 downto 4);

    cfggen : process(ad3_0, devid_reg, devctl_reg, revid_reg, latency_reg, base_reg, int_pin_reg)
    begin
        case ad3_0 is
        when "0000" => cfgout <= devid_reg;
        when "0001" => cfgout <= devctl_reg;
        when "0010" => cfgout <= revid_reg;
        when "0011" => cfgout <= latency_reg;
        when "0100" => cfgout <= base_reg;
        when "1111" => cfgout <= int_pin_reg;
        when others => cfgout <= (others => '0');
        end case;
    end process;

    mask_reg <= "0000000000000000000000" & int_mask;
    pend_reg <= "0000000000000000000000" & int_pend;
    req_reg <= "0000000000000000000000" & int_req;

    itmux : with ad1_0 select
    itout <= mask_reg when "00",
    pend_reg when "01",
    req_reg when others;
    dmaad_reg <= dmaad & "00";
    dmactl_reg <= "000000000000000000" & fifocnt & "00000" & fifo_en & dma_en & '0';

    dmamux : with ad1_0 select
    dmaout <= dmactl_reg when "00",
    dmaad_reg when "01",
    dmaword when "10",
    dmacntr when others;
end rtl;

library ieee;
    use ieee. std_logic_1164.all;

entity reg is port(
    rstn : in std_logic_vector(3 downto 0);
    clk : in std_logic_vector(3 downto 0);
    wraddr : in std_logic_vector(5 downto 0);
    cben : in std_logic_vector(3 downto 0);
    adi : in std_logic_vector(31 downto 0);
    wren : in std_logic;
    fifo_ovf : in std_logic;
    dma_done : in std_logic;
    timer_int : in std_logic_vector(3 downto 0);
    intn : in std_logic_vector(3 downto 0);
    intan : out std_logic;
    dma_en : out std_logic;
    fifo_en : out std_logic;
    soft_rstn : out std_logic;
    dmaad : out std_logic_vector(31 downto 2);
    dmaword : out std_logic_vector(31 downto 0);
    cfg_wrn : in std_logic;
    m_abort : in std_logic;
    t_abort : in std_logic;
    bist_code : in std_logic_vector(4 downto 0);
    fifocnt : in std_logic_vector(5 downto 0);
    dmacntr : in std_logic_vector(31 downto 0);
    rdaddr : in std_logic_vector(5 downto 0);
    bist_start : out std_logic;
    target_b2b : out std_logic;
    master_en : out std_logic;
    respond_en : out std_logic;
    base_addr : out std_logic_vector(11 downto 0);
    latency_pci : out std_logic_vector(4 downto 0);
    dout : out std_logic_vector(31 downto 0));
end reg;

architecture rtl of reg is
    component itreg port(
        rstn, clk : in std_logic;
        addr : in std_logic_vector(5 downto 0); -- 6 bit address input
        cben : in std_logic_vector(3 downto 0); -- command byte enable 4 bit active low. each bit controlls a byte lane
        adi : in std_logic_vector(31 downto 0); -- data to be written to registers
        wren : in std_logic;
        fifo_ovf : in std_logic; --indictes overflow
        dma_done : in std_logic; --indictes dma is done
        timer_int : in std_logic_vector(3 downto 0); --indictes timers are time out
        intn : in std_logic_vector(3 downto 0);
        intan : out std_logic; --active low indicated when interrupt is generated
        int_req : out std_logic_vector(9 downto 0); -- interrupt registers
        int_mask : out std_logic_vector(9 downto 0); -- interrupt registers
        int_pend : out std_logic_vector(9 downto 0));-- interrupt registers
end component;

component spreg port(
    rstn0, rstn1, clk0, clk1 : in std_logic;
    addr : in std_logic_vector(5 downto 0);
    cben : in std_logic_vector(3 downto 0); -- command byte enable 4 bit active low. each bit controlls a byte lane
    adi : in std_logic_vector(31 downto 0); -- data to be written to registers
    wren : in std_logic;
    dma_done : in std_logic; --indictes dma is done
    dma_en : out std_logic; -- control wheter the dma or fifo are enabled
    fifo_en : out std_logic; --dma control register bit 1
    soft_rstn : out std_logic; --dma control register bit 0
    dmaad : out std_logic_vector(31 downto 2); -- starting address register for data trasnfer
    dmaword : out std_logic_vector(31 downto 0)); -- number of words to transfer
end component;

component regmux port(
    clk : in std_logic;
    rstn : in std_logic;
    addr : in std_logic_vector(3 downto 0);
    adi : in std_logic_vector(31 downto 0);
    cben : in std_logic_vector(3 downto 0);
    cfg_wrn : in std_logic;
    m_abort : in std_logic;
    t_abort : in std_logic;
    bist_code : in std_logic_vector(4 downto 0);
    int_req : in std_logic_vector(9 downto 0);
    int_mask : in std_logic_vector(9 downto 0);
    int_pend : in std_logic_vector(9 downto 0);
    dma_en : in std_logic;
    fifo_en : in std_logic;
    fifocnt : in std_logic_vector(5 downto 0);
    dmaad : in std_logic_vector(31 downto 2);
    dmaword : in std_logic_vector(31 downto 0);
    dmacntr : in std_logic_vector(31 downto 0);
    rdaddr : in std_logic_vector(5 downto 0);
    bist_start : out std_logic;
    target_b2b : out std_logic;
    master_en : out std_logic;
    respond_en : out std_logic;
    base_addr : out std_logic_vector(11 downto 0);
    latency_pci : out std_logic_vector(4 downto 0);
    dout : out std_logic_vector(31 downto 0));
end component;

signal int_req : std_logic_vector(9 downto 0);
signal int_mask : std_logic_vector(9 downto 0);
signal int_pend : std_logic_vector(9 downto 0);
signal dma_en_s : std_logic;
signal fifo_en_s : std_logic;
signal dmaad_s : std_logic_vector(31 downto 2);
signal dmaword_s : std_logic_vector(31 downto 0);
signal target_b2b_s : std_logic;
signal master_en_s : std_logic;
signal respond_en_s : std_logic;
signal base_addr_s : std_logic_vector(11 downto 0);
signal latency_pci_s : std_logic_vector(4 downto 0);
begin
    dma_en <= dma_en_s;
    fifo_en <= fifo_en_s;
    dmaad <= dmaad_s;
    dmaword <= dmaword_s;
    target_b2b <= target_b2b_s;
    master_en <= master_en_s;
    respond_en <= respond_en_s;
    base_addr <= base_addr_s;

    itreg0 : itreg
        port map( rstn => rstn(1), clk => clk(1), addr => wraddr, cben => cben,
        adi => adi, wren => wren, fifo_ovf => fifo_ovf,
        dma_done => dma_done, timer_int => timer_int,
        intn => intn, intan => intan, int_req => int_req,
        int_mask => int_mask, int_pend => int_pend);

    spreg0 : spreg
        port map(rstn0 => rstn(1), rstn1 => rstn(2), clk0 => clk(1),
        clk1 => clk(2), addr => wraddr, cben => cben,
        adi => adi, wren => wren, dma_done => dma_done,
        dma_en => dma_en_s, fifo_en => fifo_en_s,
        soft_rstn => soft_rstn, dmaad => dmaad_s,
        dmaword => dmaword_s);

    regmux0 : regmux
        port map(clk => clk(3), rstn => rstn(3), addr => wraddr(3 downto 0),
        adi => adi, cben => cben, cfg_wrn => cfg_wrn, m_abort => m_abort,
        t_abort => t_abort, bist_code => bist_code, int_req => int_req,
        int_mask => int_mask, int_pend => int_pend, dma_en => dma_en_s,
        fifo_en => fifo_en_s, fifocnt => fifocnt, dmaad => dmaad_s,
        dmaword => dmaword_s, dmacntr => dmacntr, rdaddr => rdaddr,
        bist_start => bist_start, target_b2b => target_b2b_s,
        master_en => master_en_s, respond_en => respond_en_s,
        base_addr => base_addr_s, latency_pci => latency_pci,
        dout => dout);
end rtl;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity tbreg is end tbreg;

architecture beh of tbreg is
    component reg port(
        rstn : in std_logic_vector(3 downto 0);
        clk : in std_logic_vector(3 downto 0);
        wraddr : in std_logic_vector(5 downto 0);
        cben : in std_logic_vector(3 downto 0);
        adi : in std_logic_vector(31 downto 0);
        wren : in std_logic;
        fifo_ovf : in std_logic;
        dma_done : in std_logic;
        timer_int : in std_logic_vector(3 downto 0);
        intn : in std_logic_vector(3 downto 0);
        intan : out std_logic;
        dma_en : out std_logic;
        fifo_en : out std_logic;
        soft_rstn : out std_logic;
        dmaad : out std_logic_vector(31 downto 2);
        dmaword : out std_logic_vector(31 downto 0);
        cfg_wrn : in std_logic;
        m_abort : in std_logic;
        t_abort : in std_logic;
        bist_code : in std_logic_vector(4 downto 0);
        fifocnt : in std_logic_vector(5 downto 0);
        dmacntr : in std_logic_vector(31 downto 0);
        rdaddr : in std_logic_vector(5 downto 0);
        bist_start : out std_logic;
        target_b2b : out std_logic;
        master_en : out std_logic;
        respond_en : out std_logic;
        base_addr : out std_logic_vector(11 downto 0);
        latency_pci : out std_logic_vector(4 downto 0);
        dout : out std_logic_vector(31 downto 0));
end component;

constant period : time := 50 ns;
constant delay : time := 80 ns;

signal rstn, clk : std_logic;
signal wren, fifo_ovf, dma_done, intan : std_logic;
signal dma_en, fifo_en, soft_rstn : std_logic;
signal cfg_wrn, m_abort, t_abort : std_logic;
signal bist_start, target_b2b, master_en, respond_en : std_logic;
signal cben, timer_int, intn, rstns, clks : std_logic_vector(3 downto 0);
signal dmaword, adi, dmacntr, dout : std_logic_vector(31 downto 0);
signal bist_code, latency_pci : std_logic_vector(4 downto 0);
signal fifocnt, wraddr, rdaddr : std_logic_vector(5 downto 0);
signal base_addr : std_logic_vector(11 downto 0);
signal dmaad : std_logic_vector(31 downto 2);
begin
    rstn <= '0', '1' after 10 *period;
    clkgen : process
    begin
        clk <= '0'; wait for period;
        clk <= '1'; wait for period;
    end process;

    clks <= clk & clk & clk & clk;
    rstns <= rstn & rstn & rstn & rstn;

    adgen : process
        variable d6 : std_logic_vector(5 downto 0) := "000000";
    begin
        d6 := d6 +1;
        rdaddr <= d6 after period;
        wraddr <= d6 after period;

        wait until rising_edge(clk);
    end process;

    dgen : process
        variable d32 : std_logic_vector(31 downto 0) := (others => '0');
    begin
        bist_code <= d32(31 downto 27) after delay;
        for i in 0 to 31 loop
        d32 := d32(30 downto 0) & (not d32(31) xor d32(2));
        dmacntr <= d32(20 downto 1) & d32(11 downto 0) after 1 ns;
        adi <= d32 after delay;
        cben <= d32(27 downto 24) after delay;
        fifocnt <= d32(17 downto 12) after 1 ns;
        intn <= d32(19 downto 16) after delay;
        cfg_wrn <= d32(12) after delay;
        wren <=d32(13) or d32(12) after delay;
        m_abort <= d32(11) after delay;
        t_abort <= d32(12) after delay;
        dma_done <= d32(9) after delay;
        fifo_ovf <= d32(10) after delay;
        wait until rising_edge(clk);
        end loop;
    end process;

    reg0 : reg
        port map(rstn => rstns, clk => clks, wraddr => wraddr, cben => cben,
        adi => adi, wren => wren, fifo_ovf => fifo_ovf,
        dma_done => dma_done, timer_int => timer_int,
        intn => intn, intan => intan, dma_en => dma_en,
        fifo_en => fifo_en, soft_rstn => soft_rstn,
        dmaad => dmaad, dmaword => dmaword, cfg_wrn => cfg_wrn,
        m_abort => m_abort, t_abort => t_abort, bist_code => bist_code,
        fifocnt => fifocnt, dmacntr => dmacntr, rdaddr => rdaddr,
        bist_start => bist_start, target_b2b => target_b2b,
        master_en => master_en, respond_en => respond_en,
        base_addr => base_addr, latency_pci => latency_pci, dout => dout);
end beh;

configuration cfg_tbreg of tbreg is
    for beh end for;
end configuration;

library ieee;
    use ieee.std_logic_1164.all;

entity itreg is port(
    rstn, clk : in std_logic;
    addr : in std_logic_vector(5 downto 0); -- 6 bit address input
    cben : in std_logic_vector(3 downto 0); -- command byte enable 4 bit active low. each bit controlls a byte lane
    adi : in std_logic_vector(31 downto 0); -- data to be written to registers
    wren : in std_logic;
    fifo_ovf : in std_logic; --indictes overflow
    dma_done : in std_logic; --indictes dma is done
    timer_int : in std_logic_vector(3 downto 0); --indictes timers are time out
    intn : in std_logic_vector(3 downto 0);
    intan : out std_logic; --active low indicated when interrupt is generated
    int_req : out std_logic_vector(9 downto 0); -- interrupt registers
    int_mask : out std_logic_vector(9 downto 0); -- interrupt registers
    int_pend : out std_logic_vector(9 downto 0));-- interrupt registers
end itreg;

architecture rtl of itreg is
    signal req, maskff, pendff : std_logic_vector(9 downto 0);
begin
    fegn : process(rstn, clk)
        variable int_or : std_logic;
begin
    if rstn = '0' then
        maskff <= (others => '0'); --interrupt mask register
        pendff <= (others => '0'); --interrupt pending register
        intan <= '1';
    elsif rising_edge(clk) then
        --interrupt mask register
        if wren = '1' and addr = "000000" and cben(0) = '0' then
        maskff(7 downto 0) <= adi(7 downto 0);
        --int mask reg is used to ena/dis any one of the interrupt sources
        end if;
        --interrupt mask register
        if wren = '1' and addr = "000000" and cben(1) = '0' then
        maskff(9 downto 8) <= adi(9 downto 8);
        end if;
        -- interrupt request register
        if wren = '1' and addr = "000010" and cben(0) = '0' then
        --clears all int pend reg when int req reg is written
        pendff(7 downto 0) <= "00000000";
        --interrupt pending register
        elsif wren = '1' and addr = "000001" and cben(0) = '0' then
        -- each individual interrupt pending bit can be cleared by writing '1';
        --int pend reg remembers interrupt sources that are in queue
        for j in 0 to 7 loop
        if adi(j) = '1' then
        pendff(j) <= '0';
        end if;
        end loop;
        else
        pendff(7 downto 0) <= (timer_int & (not intn)) or pendff(7 downto 0);
        -- if neither req / pend reg are written, pend reg remembers states and
        -- records incomming interrupts.
        end if;

        if wren = '1' and addr = "000010" and cben(1) = '0' then
        pendff(9 downto 8) <= "00";
        elsif wren = '1' and addr = "000001" and cben (1) = '0' then
        for j in 8 to 9 loop
        if adi(j) = '1' then
        pendff(j) <= '0';
        end if;
        end loop;
        else
        pendff(9 downto 8) <= (fifo_ovf & dma_done) or pendff(9 downto 8);
        end if;
        int_or := req(0);
        for i in 1 to req'length -1 loop
        int_or := int_or or req(i);
        end loop;
        intan <= not int_or;
    end if;
end process;
int_mask <= maskff;
int_pend <= pendff;
req <= pendff and maskff;
-- req reg is logic and of mask and pending regs.
int_req <= req;
end rtl;

-- the dma controller will start to transfer the data to the starting address. the
-- address is automatically incremented to transfer the next data until all the
-- words are transfered.

library ieee;
    use ieee.std_logic_1164.all;

entity spreg is port(
    rstn0, rstn1, clk0, clk1 : in std_logic;
    addr : in std_logic_vector(5 downto 0);
    cben : in std_logic_vector(3 downto 0); -- command byte enable 4 bit active low. each bit controlls a byte lane
    adi : in std_logic_vector(31 downto 0); -- data/control to be written to registers
    wren : in std_logic;
    dma_done : in std_logic; --indictes dma is done
    dma_en : out std_logic; -- control wheter the dma or fifo are enabled
    fifo_en : out std_logic; --dma control register bit 1
    soft_rstn : out std_logic; --dma control register bit 0
    dmaad : out std_logic_vector(31 downto 2); -- starting address register for data trasnfer
    dmaword : out std_logic_vector(31 downto 0)); -- number of words to transfer
end spreg;

architecture rtl of spreg is
begin
    fgen : process(rstn0, clk0)
    begin
        if rstn0 = '0' then
        soft_rstn <= '1';
        dma_en <= '0';
        fifo_en <= '0';
        elsif rising_edge(clk0) then
        soft_rstn <= '1';
        -- dma control
        if wren = '1' and addr = "010000" and cben(0) = '0' then
        dma_en <= adi(2);
        fifo_en <= adi(1);
        soft_rstn <= not adi(0);
        elsif dma_done = '1' then
        dma_en <= '0';
        end if;
        end if;
    end process;

    dmasgen : process(rstn0, clk0)
    begin
        if rstn0 = '0' then
        dmaad <= (others => '0');
        elsif rising_edge(clk0) then
        -- dma address
        if wren = '1' and addr = "010001" then
        for j in 1 to 3 loop
        if cben(j) = '0' then
        dmaad((j +1) *8 -1 downto j *8) <= adi((j +1) *8 -1 downto j *8);
        end if;
        if cben(0) = '0' then
        dmaad(7 downto 2) <= adi(7 downto 2);
        end if;
        end loop;
        end if;
        end if;
    end process;

    dmacntgen : process(rstn1, clk1)
    begin
        if rstn1 = '0' then
        dmaword <= (others => '0');
        elsif rising_edge(clk1) then
        -- dma word -> for dma to know how many words to transfer before dma_done is asserted.
        if wren = '1' and addr = "010010" then
        for j in 0 to 3 loop
        if cben(j) = '0' then
        dmaword((j +1) *8 -1 downto j *8) <= adi((j +1) *8 -1 downto j *8);
        end if;
        end loop;
        end if;
        end if;
    end process;
end rtl;

library ieee;
    use ieee.std_logic_1164.all;

entity regmux is port(
    clk : in std_logic;
    rstn : in std_logic;
    addr : in std_logic_vector(3 downto 0);
    adi : in std_logic_vector(31 downto 0);
    cben : in std_logic_vector(3 downto 0);
    cfg_wrn : in std_logic;
    m_abort : in std_logic; -- pci protocol
    t_abort : in std_logic; -- pci protocol
    bist_code : in std_logic_vector(4 downto 0);
    int_req : in std_logic_vector(9 downto 0);
    int_mask : in std_logic_vector(9 downto 0);
    int_pend : in std_logic_vector(9 downto 0);
    dma_en : in std_logic;
    fifo_en : in std_logic;
    fifocnt : in std_logic_vector(5 downto 0);
    dmaad : in std_logic_vector(31 downto 2);
    dmaword : in std_logic_vector(31 downto 0);
    dmacntr : in std_logic_vector(31 downto 0);
    rdaddr : in std_logic_vector(5 downto 0);
    bist_start : out std_logic; -- start build in self test circuit
    target_b2b : out std_logic;
    master_en : out std_logic;
    respond_en : out std_logic;
    base_addr : out std_logic_vector(11 downto 0);
    latency_pci : out std_logic_vector(4 downto 0);
    dout : out std_logic_vector(31 downto 0));
end regmux;

architecture rtl of regmux is
    constant asic_id : std_logic_vector(15 downto 0) := "0101010100100100";
    constant comp_id : std_logic_vector(15 downto 0) := "0001010101011100";
    constant class_code : std_logic_vector(23 downto 0) := "111111110000000000000000";
    constant revision : std_logic_vector(7 downto 0) := "00000010";
    constant basereg19_0 : std_logic_vector(19 downto 0) := "00000000000000000000";
    constant int_pin : std_logic_vector(7 downto 0) := "00000001";

    signal devid_reg : std_logic_vector(31 downto 0);
    signal devctl_reg : std_logic_vector(31 downto 0);
    signal revid_reg : std_logic_vector(31 downto 0);
    signal latency_reg : std_logic_vector(31 downto 0);
    signal base_reg : std_logic_vector(31 downto 0);
    signal basereg31_20 : std_logic_vector(11 downto 0);
    signal int_pin_reg : std_logic_vector(31 downto 0);
    signal mabort_ff : std_logic;
    signal tabort_ff : std_logic;
    signal target_b2b_ff : std_logic;
    signal master_en_ff : std_logic;
    signal respond_en_ff : std_logic;
    signal latency_ff : std_logic_vector(4 downto 0);
    signal int_line_ff : std_logic_vector(7 downto 0);
    signal bist_code_ff : std_logic_vector(3 downto 0);
    signal bist_start_ff, bist_start_dl : std_logic;
    signal ad3_0 : std_logic_vector(3 downto 0);
    signal ad1_0, ad5_4 : std_logic_vector(1 downto 0);
    signal itout, mask_reg, pend_reg, req_reg, dmaout,
    dmaad_reg, cfgout, dmactl_reg : std_logic_vector(31 downto 0);

begin
    target_b2b <= target_b2b_ff;
    master_en <= master_en_ff;
    respond_en <= respond_en_ff;
    devid_reg <= asic_id & comp_id;
    revid_reg <= class_code & revision;
    base_addr <= basereg31_20;
    latency_pci <= latency_ff;
    devctl_gen : process(rstn, clk)
    begin
        if rstn = '0' then
        mabort_ff <= '0';
        tabort_ff <= '0';
        target_b2b_ff <= '0'; -- default no back to back
        master_en_ff <= '0'; --default master not enabled
        respond_en_ff <= '0'; --default no respond
        elsif rising_edge(clk) then
        if cfg_wrn = '0' and addr = "0001" then
        if cben(1) = '0' then
        target_b2b_ff <= adi(9);
        end if;
        if cben(0) = '0' then
        master_en_ff <= adi(2);
        respond_en_ff <= adi(1);
        end if;
        end if;
        if(cfg_wrn = '0') and addr = "0001" and
        cben(3) = '0' and adi(29) = '1' then
        mabort_ff <= '0';
        elsif mabort_ff = '0' then
        mabort_ff <= m_abort;
        end if;
        if cfg_wrn = '0' and addr = "0001" and
        cben(3) = '0' and adi(28) = '1' then
        tabort_ff <= '0'; -- clear by writing 1
        elsif tabort_ff = '0' then -- when 0 clock in
        tabort_ff <= t_abort;
        end if;
        end if;
    end process;

    devctl_reg <= "00" & mabort_ff & tabort_ff & "001010000000" & "000000" &
        target_b2b_ff & "000000" & master_en_ff & respond_en_ff & '0';

    bist_start <= bist_start_ff and (not bist_start_dl);

    basereg_gen : process(rstn, clk)
    begin
        if rstn = '0' then
        basereg31_20 <= "111111000000";
        latency_ff <= "00000";
        int_line_ff <= "00000000";
        bist_start_ff <= '0';
        bist_start_dl <= '0';
        bist_code_ff <= "0000";
        elsif rising_edge(clk) then
        if cfg_wrn = '0' and addr = "0100" then
        if cben(3) = '0' then
        basereg31_20(11 downto 4) <= adi(31 downto 24);
        end if;
        if cben(2) = '0' then
        basereg31_20(3 downto 0) <= adi(23 downto 20);
        end if;
        end if;
        if cfg_wrn = '0' and addr = "0011" and cben(1) = '0' then
        latency_ff <= adi(15 downto 11);
        end if;
        if cfg_wrn = '0' and addr = "0011" and
        cben(3) = '0' and adi(30) = '1' then
        bist_start_ff <= '1'; --when write '1' start bist_code
        elsif (bist_code(4) = '0') then
        bist_start_ff <= '0'; -- clear when bist done
        end if;
        bist_start_dl <= bist_start_ff;
        bist_code_ff <= bist_code(3 downto 0);
        if cfg_wrn = '0' and addr = "1111" and cben(0) = '0' then
        int_line_ff <= adi(7 downto 0);
        end if;
        end if;
    end process;

    base_reg <= basereg31_20 & basereg19_0;
    latency_reg <= '1' & bist_start_ff & "00" & bist_code_ff & "00000000"
    & latency_ff & "00000000000";
    int_pin_reg <= "0000000000000000" & int_pin & int_line_ff;

    ad3_0 <= rdaddr(3 downto 0); ad1_0 <= rdaddr(1 downto 0);
    ad5_4 <= rdaddr(5 downto 4);

    cfggen : process(ad3_0, devid_reg, devctl_reg, revid_reg, latency_reg, base_reg, int_pin_reg)
    begin
        case ad3_0 is
        when "0000" => cfgout <= devid_reg;
        when "0001" => cfgout <= devctl_reg;
        when "0010" => cfgout <= revid_reg;
        when "0011" => cfgout <= latency_reg;
        when "0100" => cfgout <= base_reg;
        when "1111" => cfgout <= int_pin_reg;
        when others => cfgout <= (others => '0');
        end case;
    end process;

    mask_reg <= "0000000000000000000000" & int_mask;
    pend_reg <= "0000000000000000000000" & int_pend;
    req_reg <= "0000000000000000000000" & int_req;

    itmux : with ad1_0 select
    itout <= mask_reg when "00",
    pend_reg when "01",
    req_reg when others;
    dmaad_reg <= dmaad & "00";
    dmactl_reg <= "000000000000000000" & fifocnt & "00000" & fifo_en & dma_en & '0';

    dmamux : with ad1_0 select
    dmaout <= dmactl_reg when "00",
    dmaad_reg when "01",
    dmaword when "10",
    dmacntr when others;
end rtl;

library ieee;
    use ieee. std_logic_1164.all;

entity reg is port(
    rstn : in std_logic_vector(3 downto 0);
    clk : in std_logic_vector(3 downto 0);
    wraddr : in std_logic_vector(5 downto 0);
    cben : in std_logic_vector(3 downto 0);
    adi : in std_logic_vector(31 downto 0);
    wren : in std_logic;
    fifo_ovf : in std_logic;
    dma_done : in std_logic;
    timer_int : in std_logic_vector(3 downto 0);
    intn : in std_logic_vector(3 downto 0);
    intan : out std_logic;
    dma_en : out std_logic;
    fifo_en : out std_logic;
    soft_rstn : out std_logic;
    dmaad : out std_logic_vector(31 downto 2);
    dmaword : out std_logic_vector(31 downto 0);
    cfg_wrn : in std_logic;
    m_abort : in std_logic;
    t_abort : in std_logic;
    bist_code : in std_logic_vector(4 downto 0);
    fifocnt : in std_logic_vector(5 downto 0);
    dmacntr : in std_logic_vector(31 downto 0);
    rdaddr : in std_logic_vector(5 downto 0);
    bist_start : out std_logic;
    target_b2b : out std_logic;
    master_en : out std_logic;
    respond_en : out std_logic;
    base_addr : out std_logic_vector(11 downto 0);
    latency_pci : out std_logic_vector(4 downto 0);
    dout : out std_logic_vector(31 downto 0));
end reg;

architecture rtl of reg is
    component itreg port(
        rstn, clk : in std_logic;
        addr : in std_logic_vector(5 downto 0); -- 6 bit address input
        cben : in std_logic_vector(3 downto 0); -- command byte enable 4 bit active low. each bit controlls a byte lane
        adi : in std_logic_vector(31 downto 0); -- data to be written to registers
        wren : in std_logic;
        fifo_ovf : in std_logic; --indictes overflow
        dma_done : in std_logic; --indictes dma is done
        timer_int : in std_logic_vector(3 downto 0); --indictes timers are time out
        intn : in std_logic_vector(3 downto 0);
        intan : out std_logic; --active low indicated when interrupt is generated
        int_req : out std_logic_vector(9 downto 0); -- interrupt registers
        int_mask : out std_logic_vector(9 downto 0); -- interrupt registers
        int_pend : out std_logic_vector(9 downto 0));-- interrupt registers
end component;

component spreg port(
    rstn0, rstn1, clk0, clk1 : in std_logic;
    addr : in std_logic_vector(5 downto 0);
    cben : in std_logic_vector(3 downto 0); -- command byte enable 4 bit active low. each bit controlls a byte lane
    adi : in std_logic_vector(31 downto 0); -- data to be written to registers
    wren : in std_logic;
    dma_done : in std_logic; --indictes dma is done
    dma_en : out std_logic; -- control wheter the dma or fifo are enabled
    fifo_en : out std_logic; --dma control register bit 1
    soft_rstn : out std_logic; --dma control register bit 0
    dmaad : out std_logic_vector(31 downto 2); -- starting address register for data trasnfer
    dmaword : out std_logic_vector(31 downto 0)); -- number of words to transfer
end component;

component regmux port(
    clk : in std_logic;
    rstn : in std_logic;
    addr : in std_logic_vector(3 downto 0);
    adi : in std_logic_vector(31 downto 0);
    cben : in std_logic_vector(3 downto 0);
    cfg_wrn : in std_logic;
    m_abort : in std_logic;
    t_abort : in std_logic;
    bist_code : in std_logic_vector(4 downto 0);
    int_req : in std_logic_vector(9 downto 0);
    int_mask : in std_logic_vector(9 downto 0);
    int_pend : in std_logic_vector(9 downto 0);
    dma_en : in std_logic;
    fifo_en : in std_logic;
    fifocnt : in std_logic_vector(5 downto 0);
    dmaad : in std_logic_vector(31 downto 2);
    dmaword : in std_logic_vector(31 downto 0);
    dmacntr : in std_logic_vector(31 downto 0);
    rdaddr : in std_logic_vector(5 downto 0);
    bist_start : out std_logic;
    target_b2b : out std_logic;
    master_en : out std_logic;
    respond_en : out std_logic;
    base_addr : out std_logic_vector(11 downto 0);
    latency_pci : out std_logic_vector(4 downto 0);
    dout : out std_logic_vector(31 downto 0));
end component;

signal int_req : std_logic_vector(9 downto 0);
signal int_mask : std_logic_vector(9 downto 0);
signal int_pend : std_logic_vector(9 downto 0);
signal dma_en_s : std_logic;
signal fifo_en_s : std_logic;
signal dmaad_s : std_logic_vector(31 downto 2);
signal dmaword_s : std_logic_vector(31 downto 0);
signal target_b2b_s : std_logic;
signal master_en_s : std_logic;
signal respond_en_s : std_logic;
signal base_addr_s : std_logic_vector(11 downto 0);
signal latency_pci_s : std_logic_vector(4 downto 0);
begin
    dma_en <= dma_en_s;
    fifo_en <= fifo_en_s;
    dmaad <= dmaad_s;
    dmaword <= dmaword_s;
    target_b2b <= target_b2b_s;
    master_en <= master_en_s;
    respond_en <= respond_en_s;
    base_addr <= base_addr_s;

    itreg0 : itreg
        port map( rstn => rstn(1), clk => clk(1), addr => wraddr, cben => cben,
        adi => adi, wren => wren, fifo_ovf => fifo_ovf,
        dma_done => dma_done, timer_int => timer_int,
        intn => intn, intan => intan, int_req => int_req,
        int_mask => int_mask, int_pend => int_pend);

    spreg0 : spreg
        port map(rstn0 => rstn(1), rstn1 => rstn(2), clk0 => clk(1),
        clk1 => clk(2), addr => wraddr, cben => cben,
        adi => adi, wren => wren, dma_done => dma_done,
        dma_en => dma_en_s, fifo_en => fifo_en_s,
        soft_rstn => soft_rstn, dmaad => dmaad_s,
        dmaword => dmaword_s);

    regmux0 : regmux
        port map(clk => clk(3), rstn => rstn(3), addr => wraddr(3 downto 0),
        adi => adi, cben => cben, cfg_wrn => cfg_wrn, m_abort => m_abort,
        t_abort => t_abort, bist_code => bist_code, int_req => int_req,
        int_mask => int_mask, int_pend => int_pend, dma_en => dma_en_s,
        fifo_en => fifo_en_s, fifocnt => fifocnt, dmaad => dmaad_s,
        dmaword => dmaword_s, dmacntr => dmacntr, rdaddr => rdaddr,
        bist_start => bist_start, target_b2b => target_b2b_s,
        master_en => master_en_s, respond_en => respond_en_s,
        base_addr => base_addr_s, latency_pci => latency_pci,
        dout => dout);
end rtl;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity tbreg is end tbreg;

architecture beh of tbreg is
    component reg port(
        rstn : in std_logic_vector(3 downto 0);
        clk : in std_logic_vector(3 downto 0);
        wraddr : in std_logic_vector(5 downto 0);
        cben : in std_logic_vector(3 downto 0);
        adi : in std_logic_vector(31 downto 0);
        wren : in std_logic;
        fifo_ovf : in std_logic;
        dma_done : in std_logic;
        timer_int : in std_logic_vector(3 downto 0);
        intn : in std_logic_vector(3 downto 0);
        intan : out std_logic;
        dma_en : out std_logic;
        fifo_en : out std_logic;
        soft_rstn : out std_logic;
        dmaad : out std_logic_vector(31 downto 2);
        dmaword : out std_logic_vector(31 downto 0);
        cfg_wrn : in std_logic;
        m_abort : in std_logic;
        t_abort : in std_logic;
        bist_code : in std_logic_vector(4 downto 0);
        fifocnt : in std_logic_vector(5 downto 0);
        dmacntr : in std_logic_vector(31 downto 0);
        rdaddr : in std_logic_vector(5 downto 0);
        bist_start : out std_logic;
        target_b2b : out std_logic;
        master_en : out std_logic;
        respond_en : out std_logic;
        base_addr : out std_logic_vector(11 downto 0);
        latency_pci : out std_logic_vector(4 downto 0);
        dout : out std_logic_vector(31 downto 0));
end component;

constant period : time := 50 ns;
constant delay : time := 80 ns;

signal rstn, clk : std_logic;
signal wren, fifo_ovf, dma_done, intan : std_logic;
signal dma_en, fifo_en, soft_rstn : std_logic;
signal cfg_wrn, m_abort, t_abort : std_logic;
signal bist_start, target_b2b, master_en, respond_en : std_logic;
signal cben, timer_int, intn, rstns, clks : std_logic_vector(3 downto 0);
signal dmaword, adi, dmacntr, dout : std_logic_vector(31 downto 0);
signal bist_code, latency_pci : std_logic_vector(4 downto 0);
signal fifocnt, wraddr, rdaddr : std_logic_vector(5 downto 0);
signal base_addr : std_logic_vector(11 downto 0);
signal dmaad : std_logic_vector(31 downto 2);
begin
    rstn <= '0', '1' after 10 *period;
    clkgen : process
    begin
        clk <= '0'; wait for period;
        clk <= '1'; wait for period;
    end process;

    clks <= clk & clk & clk & clk;
    rstns <= rstn & rstn & rstn & rstn;

    adgen : process
        variable d6 : std_logic_vector(5 downto 0) := "000000";
    begin
        d6 := d6 +1;
        rdaddr <= d6 after period;
        wraddr <= d6 after period;

        wait until rising_edge(clk);
    end process;

    dgen : process
        variable d32 : std_logic_vector(31 downto 0) := (others => '0');
    begin
        bist_code <= d32(31 downto 27) after delay;
        for i in 0 to 31 loop
        d32 := d32(30 downto 0) & (not d32(31) xor d32(2));
        dmacntr <= d32(20 downto 1) & d32(11 downto 0) after 1 ns;
        adi <= d32 after delay;
        cben <= d32(27 downto 24) after delay;
        fifocnt <= d32(17 downto 12) after 1 ns;
        intn <= d32(19 downto 16) after delay;
        cfg_wrn <= d32(12) after delay;
        wren <=d32(13) or d32(12) after delay;
        m_abort <= d32(11) after delay;
        t_abort <= d32(12) after delay;
        dma_done <= d32(9) after delay;
        fifo_ovf <= d32(10) after delay;
        wait until rising_edge(clk);
        end loop;
    end process;

    reg0 : reg
        port map(rstn => rstns, clk => clks, wraddr => wraddr, cben => cben,
        adi => adi, wren => wren, fifo_ovf => fifo_ovf,
        dma_done => dma_done, timer_int => timer_int,
        intn => intn, intan => intan, dma_en => dma_en,
        fifo_en => fifo_en, soft_rstn => soft_rstn,
        dmaad => dmaad, dmaword => dmaword, cfg_wrn => cfg_wrn,
        m_abort => m_abort, t_abort => t_abort, bist_code => bist_code,
        fifocnt => fifocnt, dmacntr => dmacntr, rdaddr => rdaddr,
        bist_start => bist_start, target_b2b => target_b2b,
        master_en => master_en, respond_en => respond_en,
        base_addr => base_addr, latency_pci => latency_pci, dout => dout);
end beh;

configuration cfg_tbreg of tbreg is
    for beh end for;
end configuration;

library ieee;
    use ieee.std_logic_1164.all;

entity regh is port(
    clk, rstn, en : in std_logic;
    din : in std_logic_vector(31 downto 0);
    dout : out std_logic_vector(31 downto 0));
end entity;

architecture rtl of regh is
begin
    process(clk, rstn)
    begin
        if rstn = '0' then
        dout <= (others => '0');
        elsif rising_edge(clk) then
        if en = '1' then
        dout <= din;
        end if;
        end if;
    end process;
end rtl;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity regs is port(
    rstn, clk, wren : in std_logic;
    wad : in std_logic_vector(3 downto 0);
    din : in std_logic_vector(31 downto 0);
    rad1, rad2 : in std_logic_vector(3 downto 0);
    dout1, dout2 : out std_logic_vector(31 downto 0));
end regs;

architecture rtl of regs is
    type regary is array(0 to 15 ) of std_logic_vector(31 downto 0);
    signal en : std_logic_vector(15 downto 0);
    signal ff : regary;

    component regh port(
        clk, rstn, en : in std_logic;
        din : in std_logic_vector(31 downto 0);
        dout : out std_logic_vector(31 downto 0));
end component;
begin

    p0 : process(wad, wren)
    begin
        en <= (others => '0');
        en(conv_integer(wad)) <= wren;
    end process;

    g0 : for j in 0 to 15 generate
        regh0 : regh
        port map(clk => clk, rstn => rstn, en => en(j), din => din, dout => ff(j));
    end generate;

    dout1 <= ff(conv_integer(rad1));
    dout2 <= ff(conv_integer(rad2));
end rtl;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity tbregs is end entity;

architecture beh of tbregs is
    component regs port(
        rstn, clk, wren : in std_logic;
        wad : in std_logic_vector(3 downto 0);
        din : in std_logic_vector(31 downto 0);
        rad1, rad2 : in std_logic_vector(3 downto 0);
        dout1, dout2 : out std_logic_vector(31 downto 0));
end component;

signal rstn, clk, wren : std_logic;
signal wad : std_logic_vector(3 downto 0);
signal din : std_logic_vector(31 downto 0);
signal rad1, rad2 : std_logic_vector(3 downto 0);
signal dout1, dout2 : std_logic_vector(31 downto 0);
signal data : std_logic_vector(31 downto 0) := (others => '0');
signal sel : std_logic_vector(3 downto 0) := (others => '0');

constant period : time := 50 ns;
constant delay : time := 80 ns;

begin

    rstn <= '0', '1' after delay *3;

    clk0 : process
    begin
        clk <= '0'; wait for period;
        clk <= '1'; wait for period;
    end process;

    wren <= '1';

    tbregs0 : process
    begin
        for i in 0 to 15 loop
        data <= data(30 downto 0) & not(data(1) xor data(5) xor data(6) xor data(31));
        din <= data after delay;
        wad <= std_logic_vector(to_unsigned(i,4)) after delay;

        sel <= sel(2 downto 0) & not(sel(0) xor sel(3)) after delay;
        rad1 <= sel after delay;
        rad2 <= not(sel) after delay;
        wait until rising_edge(clk);
        end loop;
    end process;

    regs0 : regs
        port map(rstn => rstn, clk => clk, wren => wren,
        wad => wad, din => din, rad1 => rad1, rad2 => rad2,
        dout1 => dout1, dout2 => dout2);

end beh;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

entity dualram is
    generic( n : integer := 4; -- width of each data in the memory
        words : integer := 128; -- total number of memory words
        m : integer := 7; -- width of the address bus(2 **m words
        bpc : integer := 2;
        floopplan : integer := 0;
        buffer_size : string := "default");

    port( a : in std_logic_vector(m -1 downto 0); -- a address bus
        adin : in std_logic_vector(n -1 downto 0);
        awr : in std_logic; -- low pulse to write
        b : in std_logic_vector(m -1 downto 0); -- b address bus
        bdin : in std_logic_vector(n -1 downto 0);
        bwr : in std_logic; -- low pulse to write
        adout : out std_logic_vector(n -1 downto 0);
        bdout : out std_logic_vector(n -1 downto 0));
end dualram;

architecture beh of dualram is
    constant dly : time := 3 ns;
    subtype bitsn is std_logic_vector(n -1 downto 0);
    type arytype is array(natural range <>) of bitsn;
    signal mem : arytype(0 to words -1);
    signal addr_match : std_logic; -- to indicate that hte addresses in both ports are identical
    signal abusyns, bbusyns : std_logic := '1'; -- indicate the busy situation
    signal writeas, writebs : std_logic := '1'; -- indicate the write operation
begin

    addr_match <= '1' when(a = b) and (not is_x(a)) else '0';

    p0 : process(a, awr, b, bwr, addr_match, mem)
        variable writea, writeb : std_logic := '0'; -- indicate write and busy status on both ports
        variable abusyn, bbusyn : std_logic := '1';
    begin
        if falling_edge(awr) then -- check status when awr is asserted low
        if abusyn = '1' then -- if port a is busy, the awr pulse is ignored
        if addr_match = '1' then -- checks whether the addresses are identical
        abusyn := not writeb; -- abusyn is asserted when port b has not completed its write operation
        bbusyn := writeb; writea := not writeb; -- if b does not have a pending write operation, bbusyn is asserted low and variable writea is set when port b does not have a pending write operation.
        else
        writea := '1'; -- always sets writeA variable when addresses don't match
        end if; -- this allows both ports to perform write operations independently since their addresses are not the same.
        end if;
        end if;

        if falling_edge(bwr) then
        if bbusyn = '1' then
        if addr_match = '1' then
        bbusyn := not writea; abusyn := writea;
        writeb := not writea;
        else
        writeb := '1';
        end if;
        end if;
        end if;

        if rising_edge(awr) then
        if abusyn = '1' and writea = '1' then
        mem(to_integer(unsigned(a))) <= adin;
        writea := '0'; bbusyn := '1';
        end if;
        abusyn := '1';
        end if;

        if rising_edge(bwr) then
        if bbusyn = '1' and writeb = '1' then
        mem(to_integer(unsigned(b))) <= bdin;
        writeb := '0'; abusyn := '1';
        end if;
        bbusyn := '1';
        end if;

        if abusyn = '1' then
        adout <= mem(to_integer(unsigned(a))) after dly;
        end if;

        if bbusyn = '1' then
        bdout <= mem(to_integer(unsigned(b))) after dly;
        end if;

        abusyns <= abusyn; bbusyns <= bbusyn;
        writeas <= writeA; writebs <= writeb;
    end process;
end beh;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity tbdualram is end entity;

architecture beh of tbdualram is

    component dualram is
        generic( n : integer := 4; -- width of each data in the memory
        words : integer := 128; -- total number of memory words
        m : integer := 7; -- width of the address bus(2 **m words
        bpc : integer := 2;
        floopplan : integer := 0;
        buffer_size : string := "default");

        port( a : in std_logic_vector(m -1 downto 0); -- a address bus
        adin : in std_logic_vector(n -1 downto 0);
        awr : in std_logic; -- low pulse to write
        b : in std_logic_vector(m -1 downto 0); -- b address bus
        bdin : in std_logic_vector(n -1 downto 0);
        bwr : in std_logic; -- low pulse to write
        adout : out std_logic_vector(n -1 downto 0);
        bdout : out std_logic_vector(n -1 downto 0));
    end component;

    constant dly : time := 10 ns;
    constant period : time := 50 ns;
    constant n : integer := 8;
    constant words : integer := 16;
    constant m : integer := 4;

    signal a : std_logic_vector(m -1 downto 0); -- a address bus
    signal adin : std_logic_vector(n -1 downto 0);
    signal awr : std_logic; -- low pulse to write
    signal b : std_logic_vector(m -1 downto 0); -- b address bus
    signal bdin : std_logic_vector(n -1 downto 0);
    signal bwr : std_logic; -- low pulse to write
    signal adout : std_logic_vector(n -1 downto 0);
    signal bdout : std_logic_vector(n -1 downto 0);
    signal clk : std_logic;

begin
    p0 : process
        variable d : std_logic_vector(n -1 downto 0);
    begin
        a <= (others => '0');
        adin <= (others => '0');
        awr <= '1';
        b <= (others => '0');
        bdin <= (others => '0');
        bwr <= '1';
        d := (others => '0');
        -----write from A
        wait until rising_edge(clk);
        assert false report "write from A" severity note;
        for j in 1 to words loop
        a <= a +1;
        adin <= d;
        awr <= '0' after dly, '1' after period;
        wait until rising_edge(clk);
        d := d(n -2 downto 0) & not (d(n -1) xor d(0));
        end loop;

        for j in 0 to 4 loop
        wait until rising_edge(clk);
        end loop;
        -----write from b
        assert false report "write from B" severity note;
        for j in 1 to words loop
        b <= b +1;
        bdin <= d;
        bwr <= '0' after dly, '1' after period;
        wait until rising_edge(clk);
        d := d(n -2 downto 0) & not (d(n -1) xor d(0));
        end loop;

        for j in 0 to 4 loop
        wait until rising_edge(clk);
        end loop;
        -----write from both sides
        assert false report "write from both sides" severity note;
        loop -- infinte loop, interesting....
        a <= d(a'range);
        adin <= not(d(n -1) xor d(0)) & d(n -1 downto 1);
        b <= b +1;
        bdin <= d;
        if d(0) = '0' then -- force the same address
        b <= d(b'range);
        end if;
        case d(2 downto 0) is
        when "000" => -- awr first
        assert false report " awr first " severity note;
        awr <= '0' after dly, '1' after period;
        bwr <= '0' after 2 *dly, '1' after period;
        when "001" => -- bwr first
        assert false report " bwr first " severity note;
        awr <= '0' after 2 *dly, '1' after period;
        bwr <= '0' after dly, '1' after period;
        when "010" =>
        assert false report " same same time" severity note;
        awr <= '0' after dly, '1' after period;
        bwr <= '0' after dly, '1' after period;
        when "011" => -- awr covers bwr
        assert false report " awr covers bwr" severity note;
        awr <= '0' after dly, '1' after period +dly;
        bwr <= '0' after 2 *dly, '1' after period;
        when "100" => -- bwr covers awr
        assert false report " bwr covers awr" severity note;
        bwr <= '0' after dly, '1' after period +dly;
        awr <= '0' after 2 *dly, '1' after period;
        when "101" => --bwr overlap awr
        assert false report " bwr overlap awr" severity note;
        bwr <= '0' after dly, '1' after period -dly;
        awr <= '0' after 2 *dly, '1' after period;
        when "110" => -- awr overlap 2 bwr
        assert false report " awr overlap 2 bwr" severity note;
        awr <= '0' after dly, '1' after 2 *period -dly;
        bwr <= '0' after 2 *dly, '1' after period,
        '0' after period +dly,
        '1' after 2 * period -2 *dly;
        when others => -- bwr overlap 2 awr
        assert false report " bwr overlap 2 awr" severity note;
        bwr <= '0' after dly, '1' after 2 *period -dly;
        awr <= '0' after 2 *dly, '1' after period,
        '0' after period + dly,
        '1' after 2 * period -2 *dly;
        end case;
        wait until rising_edge(clk);
        d := d +1;
        end loop;
    end process;

    clkgen : process
    begin
        clk <= '0'; wait for period;
        clk <= '1'; wait for period;
    end process;

    dualram0 : dualram
        generic map(n => n, words => words, m => m, bpc => 2, floopplan => 0, buffer_size => "2")
        port map(a => a, adin => adin, awr => awr, b => b, bdin => bdin , bwr => bwr , adout => adout ,bdout => bdout);
end beh;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity fifosyn is port(
    clk, rstn, rn, wn : in std_logic;
    emptyn, fulln : out std_logic;
    d : in std_logic_vector(7 downto 0);
    q : out std_logic_vector(7 downto 0));
end fifosyn;

-- word is size of grouped bits
architecture rtl of fifosyn is
    constant m : integer := 8; -- width of the data
    constant n : integer := 8; -- number of words in the fifo
    signal rcntr, wcntr : std_logic_vector(2 downto 0); --R/W counter / pointer
    subtype wrdtype is std_logic_vector(n -1 downto 0);
    type regtype is array(0 to m -1) of wrdtype;
    signal reg : regtype;
    signal rw : std_logic_vector(1 downto 0);
    signal fullnf, emptynf : std_logic;
begin
    rw <= rn & wn; -- concatenation of read and write line to simultaniously check them in the if statement
    seq : process(rstn, clk)
    begin
        if rstn = '0' then
        rcntr <= (others => '0');
        wcntr <= (others => '0');
        emptynf <= '0';
        fullnf <= '1';

        for j in 0 to m -1 loop
        reg(j) <= (others => '0');
        end loop;
        elsif rising_edge(clk) then
        case rw is
        when "00" => -- read and write at the same time
        rcntr <= rcntr +1; -- increment and store in the same clk cycle
        wcntr <= wcntr +1;
        reg(conv_integer(wcntr)) <= d;
        when "01" => -- only read
        if emptynf = '1' then -- not empty
        if rcntr +1 = wcntr then -- if reading last byte then
        emptynf <= '0'; -- set empty flag
        end if;
        rcntr <= rcntr +1;
        end if;
        fullnf <= '1'; -- not full
        when "10" => -- only write
        emptynf <= '1'; -- not empty
        if fullnf = '1' then -- not full
        reg(conv_integer(wcntr)) <= d;
        if wcntr +1 = rcntr then
        fullnf <= '0'; -- full
        end if;
        wcntr <= wcntr +1;
        end if;
        when others => null;
        end case;
        end if;
    end process;

    q <= reg(conv_integer(rcntr));
    fulln <= fullnf;
    emptyn <= emptynf;
end rtl;

library ieee;
    use ieee.std_logic_1164.all;

entity tbfifosyn is end entity;

architecture beh of tbfifosyn is
    component fifosyn port(
        clk, rstn, rn, wn : in std_logic;
        emptyn, fulln : out std_logic;
        d : in std_logic_vector(7 downto 0);
        q : out std_logic_vector(7 downto 0));
end component;

signal clk, rstn, rn, wn : std_logic;
signal emptyn, fulln : std_logic;
signal d : std_logic_vector(7 downto 0);
signal q : std_logic_vector(7 downto 0);
signal rw : std_logic_vector(1 downto 0);

constant period : time := 50 ns;
constant delay : time := 80 ns;

begin
    rstn <= '0', '1' after delay *3;

    clk0 : process
    begin
        clk <= '0'; wait for period;
        clk <= '1'; wait for period;
    end process;

    -- data0 : process
    -- variable var : std_logic_vector(d'range) := (others => '0');
    -- begin
    -- var := var((var'high -1) downto 0) & (var(var'high) xor (not var(2)));
    -- d <= var after delay;
    -- rn <= var(4) after delay;
    -- wn <= var(3) after delay;
    -- wait until rising_edge(clk);
    -- end process;

    p0: process
        variable v : std_logic_vector(7 downto 0) := "00000000";
        variable cnt : integer := 0;
    begin
        d <= v after delay;
        if cnt > 10 and cnt < 20 then
        rn <= '1' after delay; wn <= '0' after delay;
        elsif cnt > 20 and cnt < 30 then
        rn <= '0' after delay; wn <= '1' after delay;
        else
        rn <= v(2) after delay; wn <= v(6) after delay;
        end if;
        wait until rising_edge(clk);
        v := v(6 downto 0) & (v(7) xor (not v(2)));
        cnt := cnt +1;
    end process;

    fifosyn0 : fifosyn
        port map( clk => clk,
        rstn => rstn,
        rn => rn,
        wn => wn,
        emptyn => emptyn,
        fulln => fulln,
        d => d,
        q => q);

end beh;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity tbdram is end entity;

architecture beh of tbdram is
    component dram
    generic(
        asize : natural := 9; -- address width
        dsize : natural := 16; -- data width
        t_asr : time := 0 ns; -- row address setup
        t_rah : time := 10 ns;-- row address holg
        t_asc : time := 0 ns; -- column address setup
        t_cah : time := 10 ns;-- column address hold
        t_oe : time := 15 ns;-- output enable time
        t_od : time := 3 ns; -- output disable time
        t_ds : time := 0 ns; -- write data setup time
        t_dh : time := 8 ns; -- write data hold time
        t_off : time := 3 ns; -- data to z time
        check_on : boolean := false);-- check timing or not
    port(
        a : in std_logic_vector(asize -1 downto 0);
        dq : inout std_logic_vector(dsize -1 downto 0);
        rasn : in std_logic;
        casn : in std_logic;
        wen : in std_logic;
        oen : in std_logic);
end component;

constant period : time := 20 ns;
constant asize : natural := 9;
constant dsize : natural := 8;
constant check_on : boolean := true;

signal a : std_logic_vector(asize -1 downto 0);
signal dq : std_logic_vector(dsize -1 downto 0);
signal rasn : std_logic;
signal casn : std_logic;
signal wen : std_logic;
signal oen : std_logic;
signal clk : std_logic;

procedure do_one(
    constant rw : in integer;
    constant t_a, t_dq, t_rasn, t_casn, t_wen, t_oen : in time;
    constant data : in std_logic_vector(dsize -1 downto 0);
    constant ca : in std_logic_vector(asize -1 downto 0);
    signal clk : in std_logic;
    signal a : out std_logic_vector(asize -1 downto 0);
    signal dq : out std_logic_vector(dsize -1 downto 0);
    signal rasn, casn, wen, oen : out std_logic) is
begin
    wait until rising_edge(clk);
    a <= ca after t_a; casn <= '0' after t_casn;
    wen <= '1' after t_wen; oen <= '1' after t_oen;
    dq <= (others => 'Z') after t_dq;
    if rw = 0 then -- read
        oen <= '0' after t_oen;
    elsif rw = 1 then -- write
        wen <= '0' after t_wen; dq <= data after t_dq;
    else -- read and then write
        oen <= '0' after t_oen;
        wait until rising_edge(clk);
        a <= (others => 'Z') after t_a;
        oen <= '1' after t_oen;
        wait until rising_edge(clk);
        wen <= '0' after t_wen; dq <= data after t_dq;
    end if;
    wait until rising_edge(clk);
    casn <= '1' after t_casn;
    wen <= '1' after t_wen; oen <= '1' after t_oen;
    dq <= (others => 'Z') after t_dq;
    a <= (others => 'Z') after t_a;
end do_one;

procedure rwcycle(
    constant rw : in natural; -- r = 0, w = 1, rw = 2
    constant word_cnt : in natural;
    constant va : std_logic_vector(asize -1 downto 0);
    constant vd : std_logic_vector(dsize -1 downto 0);
    signal clk : in std_logic;
    signal a : out std_logic_vector(asize -1 downto 0);
    signal dq : out std_logic_vector(dsize -1 downto 0);
    signal rasn, casn, wen, oen : out std_logic) is
    variable t_a, t_dq, t_rasn, t_casn : time := 0 ns;
    variable t_wen, t_oen : time := 0 ns;
    variable ca : std_logic_vector(asize -1 downto 0);
    variable cd : std_logic_vector(dsize -1 downto 0);
begin
    ca := va; cd := vd;
    wait until rising_edge(clk);
    for j in 1 to word_cnt loop
        t_a := conv_integer(vd(2 downto 0)) * 1 ns;
        t_dq := conv_integer(vd(3 downto 1)) * 1 ns;
        t_rasn := conv_integer(vd(4 downto 2)) * 1 ns;
        t_casn := conv_integer(vd(5 downto 3)) * 1 ns;
        t_wen := conv_integer(vd(6 downto 4)) * 1 ns;
        t_oen := conv_integer(vd(7 downto 5)) * 1 ns;
        a <= va after t_a; rasn <= '0' after t_rasn;
        ca := (not ca(0) xor ca(1)) & ca(asize -1 downto 1);
        do_one(rw, t_a, t_dq, t_rasn, t_casn, t_wen, t_oen, cd, ca,
        clk, a, dq, rasn, casn, wen, oen);
        cd := (not cd(0) xor cd(1)) & cd(dsize -1 downto 1);
    end loop;
    rasn <= '1' after t_rasn;
    wait until rising_edge(clk);
end rwcycle;

function lfb(constant d : std_logic_vector) return std_logic_vector is
    alias ad : std_logic_vector(d'length -1 downto 0) is d;
begin
    return ad(ad'length -2 downto 0) & (ad(ad'length -1) xor not ad(0));
end lfb;

begin
    -----
    p0 : process
        variable va : std_logic_vector(asize -1 downto 0) := (others => '0');
        variable vd : std_logic_vector(dsize -1 downto 0) := (others => '0');
    begin
        wen <= '1'; oen <= '1'; rasn <= '1'; casn <= '1';
        a <= (others => 'Z');
        dq <= (others => 'Z');
        rwcycle(0, 1, va, vd, clk, a, dq, rasn, casn, wen, oen);
        rwcycle(1, 1, va, vd, clk, a, dq, rasn, casn, wen, oen);
        rwcycle(0, 1, va, vd, clk, a, dq, rasn, casn, wen, oen);
        va := lfb(va); vd := lfb(vd);
        rwcycle(1, 1, va, vd, clk, a, dq, rasn, casn, wen, oen);
        rwcycle(0, 1, va, vd, clk, a, dq, rasn, casn, wen, oen);
        va := lfb(va); vd := lfb(vd);
        rwcycle(2, 3, va, vd, clk, a, dq, rasn, casn, wen, oen);
        rwcycle(0, 3, va, vd, clk, a, dq, rasn, casn, wen, oen);
        va := lfb(va); vd := lfb(vd);
        rwcycle(2, 3, va, vd, clk, a, dq, rasn, casn, wen, oen);
        rwcycle(0, 3, va, vd, clk, a, dq, rasn, casn, wen, oen);
        va := lfb(va); vd := lfb(vd);
    end process;

    clkgen : process
    begin
        clk <= '0'; wait for period;
        clk <= '1'; wait for period;
    end process;

    dram0 : dram
        generic map ( asize => asize,
        dsize => dsize,
        check_on => true)

        port map( a => a,
        dq => dq,
        rasn => rasn,
        casn => casn,
        wen => wen,
        oen => oen);
end beh;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;
    use ieee.std_logic_arith.all;
    use std.textio.all;
    use ieee.std_logic_textio.all;

entity dram is
    generic(
        asize : natural := 9; -- address width
        dsize : natural := 16; -- data width
        t_asr : time := 0 ns; -- row address setup
        t_rah : time := 10 ns;-- row address holg
        t_asc : time := 0 ns; -- column address setup
        t_cah : time := 10 ns;-- column address hold
        t_oe : time := 15 ns;-- output enable time
        t_od : time := 3 ns; -- output disable time
        t_ds : time := 0 ns; -- write data setup time
        t_dh : time := 8 ns; -- write data hold time
        t_off : time := 3 ns; -- data to z time
        check_on : boolean := false);-- check timing or not
    port(
        a : in std_logic_vector(asize -1 downto 0);
        dq : inout std_logic_vector(dsize -1 downto 0);
        rasn : in std_logic;
        casn : in std_logic;
        wen : in std_logic;
        oen : in std_logic);
end dram;

architecture beh of dram is
    constant asize2 : natural := 2 *asize; -- memory a size
    constant psize : natural := (asize2 - asize); -- # of page
    subtype word_type is std_logic_vector(dsize -1 downto 0); -- page of data
    type page_type is array(0 to 2**asize -1) of word_type; -- page of data
    type page_ptr_type is access page_type; -- access type that is a pointer to the page_type
    -- the page can then be dynamically allocated when the data in the pageis required.
    -- this dynamic memory allocation reduces the run time memory requirement when just a small portion of the memory is accessed.
    constant xval : word_type := (others => 'X');
    type page_tab_type is array(0 to 2**psize -1) of page_ptr_type;
    type page_tab_ptr_type is access page_tab_type;
begin
    memory : process(a, rasn, casn, dq, oen, wen)
        variable page_table : page_tab_ptr_type := null;
    variable page : page_ptr_type;
    variable ma : std_logic_vector(asize2 -1 downto 0);
    variable page_index : natural range 0 to 2**psize -1;
    variable word_index : natural range 0 to 2**asize -1;
    variable ma_x : boolean;
    variable m_wr : boolean;
    variable m_oe : boolean;
    variable m_off : boolean;
begin
    if falling_edge(rasn) then
        ma(asize2 -1 downto asize) := a; -- get row address
    elsif falling_edge(casn) then
        ma(asize -1 downto 0) := a; -- get column address
    end if;

    ma_x := is_x(ma); -- check wheather the address is valid
    m_wr := (rasn = '0') and (casn = '0') and -- set m_wr to indicate a write access
    (wen = '0') and (oen /= '0');
    m_oe := (rasn = '0') and (casn = '0') and -- set m_oe to indicate a read access
    (wen = '1') and (oen = '0');
    m_off:= ((rasn = '1') or (wen /= '0')) and (oen /= '0'); -- set m_off to indicate no mem access
    if ma_x then -- if address is valid
        page_index := 0; -- set page table
        word_index := 0; -- set word index inside page
    else
        page_index := conv_integer(ma(asize2 -1 downto asize));
        word_index := conv_integer(ma(asize -1 downto 0));
    end if;

    -----write
    -- check wheather this is the first time access and wheather the page table has been allocated
    if m_wr and not ma_x then
        if page_table = null then -- page table empty
        page_table := new page_tab_type; -- allocate table
        -- after page table is allocated initialize all pointers to null
        for j in page_tab_type'range loop
        page_table(j) := null; --invalidate all pointers
        end loop;
        end if;
        -- checks wheather page has been allocated
        if page_table(page_index) = null then
        -- allocate page if has not been allocated and initilaze all data to 'x'
        page := new page_type; -- allocate a new page
        page_table(page_index) := page; -- link the page
        for j in page_type'range loop
        page(j) := xval; -- invalidate all data
        end loop;
        end if;
        -- data is written when data is valid
        page := page_table(page_index); -- point to page
        if is_x(dq) then
        assert false report "write invalid data" severity warning;
        page(word_index) := xval;
        else
        page(word_index) := dq; -- write new data
        end if;
    end if;

    -----read
    if m_off then -- check wheather memory is idle
        dq <= (others => 'Z') after t_off; -- releases DQ
    elsif m_oe and ma_x then -- undefined address. check whether the address is valid during the read cycle
        dq <= xval after t_oe;
    elsif m_oe then -- read
        -- check wheather page exists before reading
        if (page_table /= null) and (page_table(page_index) /= null) then
        page := page_table(page_index); -- get the page
        dq <= page(word_index) after t_oe; -- read data -put data on bus
        else
        dq <= xval after t_oe; -- page never written
        assert false report "read uninitialized page" severity note;
        end if;
    end if;
end process;

-----address timing check
ra_setup : process
begin
    wait until check_on and falling_edge(rasn);
    assert (a'stable(t_asr) or t_asr = 0 ns) report "row address setup error" severity note;
end process;

ra_hold : process
begin
    wait until check_on and a'event and rasn = '0' and casn /= '0';
    assert (rasn'last_event > t_rah) or
    (rasn'last_event = 0 ns) report "row address hold error" severity note;
    wait until falling_edge(casn); -- skip A glitch
end process;

ca_setup : process
begin
    wait until check_on and falling_edge(casn);
    assert (a' stable(t_asc) or t_asc = 0 ns) report "column address setup error" severity note;
    wait until rising_edge(casn); -- skip A glitch
end process;

ca_hold : process
begin
    wait until check_on and a'event and casn = '0';
    assert (casn'last_event > t_cah) or (casn'last_event = 0 ns) report "column address hold error" severity note;
    wait until rising_edge(casn); -- skip A glitch
end process;

-----data timing check
d_setup : process
begin
    wait until check_on and
    casn'event and wen = '0' and casn = '0';
    assert dq'stable(t_ds) or t_ds = 0 ns report "write data setup-time error" severity note;
    wait until rising_edge(casn);--skip A glitch
end process;

d_hold : process
begin
    wait until check_on and dq'event and wen = '0' and casn = '0';
    assert (dq'last_event > t_dh) or ( dq'last_event = 0 ns) report "write data hold time error" severity note;
    wait until rising_edge(casn); --skip A glitch
end process;
end beh;

-- a fir filter usually has many stages. each stage is referref to as a tap. each stage
-- has a 16-bit coefficient register. input signal I, 16-bit wide, is going through two stage
-- registers. the first stage of the register is multiplied with the coefficient. the product (32 bits)
-- is registered. the registered product is signal extended to add with the 64-bit input PI.
-- the sum is again registered in a 64 bit register. both the second stage registered input I and the
-- registered sum outputs are fed to the next stage of the tap.

library ieee;
    use ieee.std_logic_1164.all;

entity firchip is port(
    rstn : in std_logic_vector(0 downto 0);
    clk : in std_logic_vector(0 downto 0);
    ldcoeff : in std_logic_vector(0 downto 0);
    start : in std_logic_vector(0 downto 0);
    oen : in std_logic_vector(0 downto 0);
    bypass : in std_logic_vector(0 downto 0);
    i : in std_logic_vector(15 downto 0);
    pi : in std_logic_vector(63 downto 0);
    o : out std_logic_vector(15 downto 0);
    po : out std_logic_vector(63 downto 0);
    vdds : inout std_logic_vector(20 downto 0);
    gnds : inout std_logic_vector(20 downto 0));
end firchip;

-----file firchip_beh.chd
library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_arith.all;

architecture rtl of firchip is
    constant k : integer := 32;
    subtype size16 is std_logic_vector(15 downto 0);
    subtype size32 is std_logic_vector(31 downto 0);
    subtype size64 is std_logic_vector(63 downto 0);
    type kx16 is array (k -1 downto 0) of size16;
    type klx16 is array(k downto 0) of size16;
    type kx32 is array (k -1 downto 0) of size32;
    type kx64 is array (k -1 downto 0) of size64;
    type klx64 is array(k downto 0) of size64;

    signal ireg1, ireg2 : klx16; -- input registers
    signal coef : klx16; -- multiplier register
    signal mult32 : kx32;-- signal for the mult32
    signal mult64 : kx64; -- signal to be sign extended to 64 bits
    signal psum : klx64; -- sum register
    signal o_s : size16;
    signal po_s : size64;
    signal rstn_f1, rstn_s, clock : std_logic;
begin
    clock <= clk(0);
    ireg2(k) <= i when start(0) = '1' else (others => '0');
    ireg1(k) <= (others => '0');
    psum(k) <= pi;
    coef(k) <= i;

    sync : process(clock)
    begin
        if rising_edge(clock)then
        rstn_f1 <= rstn(0);
        rstn_s <= rstn_f1;
        end if;
    end process;

    gen32 : for j in k -1 downto 0 generate
        ffs : process(rstn_s, clock)
        begin
        if rstn_s = '0' then
        ireg1(j) <= (others => '0');
        ireg2(j) <= (others => '0');
        coef(j) <= (others => '0');
        mult32(j)<= (others => '0');
        psum(j) <= (others => '0');
        elsif rising_edge(clock) then
        ireg1(j) <= ireg2(j +1);
        ireg2(j) <= ireg1(j);
        if ldcoeff(0) = '1' then
        coef(j) <= coef(j +1);
        end if;

        mult32(j) <= signed(ireg1(j)) * signed(coef(j));
        psum(j) <= signed(mult64(j)) + signed(psum(j +1));
        end if;

        end process;

        signext : for m in 63 downto 32 generate
        mult64(j)(m) <= mult32(j)(31);
        end generate;
        mult64(j)(31 downto 0) <= mult32(j);
    end generate;
    o_s <= i when bypass(0) = '1' else
        ireg2(0) when ldcoeff(0) = '1' else
        coef(0);
        po_s <= pi when bypass(0) = '1' else psum(0);
        o <= o_s when oen(0) = '0' else (others => 'Z');
        po <= po_s when oen(0) = '0' else (others => 'Z');
        end rtl;

        -- rstn
        -- clk
        -- ldcoeff
        -- start
        -- oen
        -- bypass
        -- i
        -- pi
        -- o
        -- po
        -- vdds
        -- gnds

        library ieee;
        use ieee.std_logic_1164.all;

        package ones_pkg is
        function count_ones(s : std_logic_vector) return natural;
        end ones_pkg;

        package body ones_pkg is
        function count_ones(s : std_logic_vector) return natural is
        variable temp : natural := 0;
        begin
        for i in s'range loop
        if s(i) = '1' then
        temp := temp +1;
        end if;
        end loop;

        return temp;
        end count_ones;
        end package body;

        library ieee;
        use ieee.std_logic_1164.all;
        use ieee.numeric_std.all;
        use work.ones_pkg.all;

        entity ones is port(
        clk, rst : in std_logic;
        din : in std_logic_vector(7 downto 0);
        n_bits : out std_logic_vector(3 downto 0));
    end ones;

    architecture rtl1 of ones is
    begin

        process(clk, rst)
        begin
        if rising_edge(clk) then
        n_bits <= std_logic_vector(to_unsigned(count_ones(din),4));
        end if;
        end process;
    end rtl1;

    library ieee;
        use ieee.std_logic_1164.all;

    entity non_pipelined is port(
        clk : in std_logic;
        data_in : in std_logic_vector(8 downto 0);
        data_out : out std_logic);
end entity;

architecture beh of non_pipelined is
    signal data : std_logic_vector(8 downto 0);
    --non pipleined
    signal result : std_logic;
    --pipleined
    signal temp1, temp2 : std_logic;

begin

    --process for registerinf data_in
    process(clk)
    begin
        if rising_edge(clk) then
        data <= data_in;
        end if;
    end process;

    --and gate equation
    result <= data(0) and data(1) and data(2) and data(3) and
    data(4) and data(5) and data(6) and data(7) and data(8);

    data_out <= result;

    --process for and gate equation
    -- process(clk)
    -- begin
    -- if rising_edge(clk) then
    -- temp1 <= data(0) and data(1) and data(2) and data(3);
    -- temp2 <= data(4) and data(5) and data(6) and data(7);
    -- data_out <= temp1 and temp2 and data(8);
    -- end if;
    -- end process;
end beh;

#************************************************************
# THIS is A WIZARD-GENERATED file.
        #
# Version 13.1.0 Build 162 10/23/2013 SJ Web Edition
        #
#************************************************************

# Copyright (C) 1991-2013 Altera Corporation
# Your use of Altera Corporation's design tools, logic functions
# and other software and tools, and its AMPP partner logic
# functions, and any output files from any of the foregoing
# (including device programming or simulation files), and any
# associated documentation or information are expressly subject
# to the terms and conditions of the Altera Program License
# Subscription Agreement, Altera MegaCore function License
# Agreement, or other applicable license agreement, including,
# without limitation, that your use is for the sole purpose of
# programming logic devices manufactured by Altera and sold by
# Altera or its authorized distributors. Please refer to the
# applicable agreement for further details.

# Clock constraints

create_clock -name "clk" -period 10.000ns [get_ports {clk}]

# Automatically constrain PLL and other generated clocks
derive_pll_clocks -create_base_clocks

# Automatically calculate clock uncertainty to jitter and other effects.
derive_clock_uncertainty

# tsu/th constraints

# tco constraints

# tpd constraints

library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
use ieee.numeric_std.all;

entity div is port(
    clk, rst : in std_logic;
    busy : out std_logic;
    ---quotient
    quo_out : out std_logic_vector(7 downto 0);
    ---denomintor
    denomintor : in std_logic_vector(7 downto 0);
    den_pl : in std_logic;
    ---numerator
    numerator : in std_logic_vector(7 downto 0));
end div;

architecture rtl of div is
    constant c : integer := 8;
    subtype bit24 is std_logic_vector(2*c -1 downto 0);
    subtype bit12 is std_logic_vector(c -1 downto 0);

    signal n, n_reg : bit24;
    signal d_reg : bit24;
    signal q_reg, q_hold : std_logic_vector(c -1 downto 0);
    signal compare : std_logic;
    signal difference : bit24;
    signal cnt_en : std_logic := '0';
    signal sel : std_logic;
    signal cnt: std_logic_vector(3 downto 0);

begin

    n(2*c -1 downto c) <= (others => '0');
    ---numerator
    process(clk, rst)
    begin
        if rst = '0' then
        n_reg <= (others => '0');
        elsif rising_edge(clk) then
        n_reg <= n;
        end if;
    end process;

    n(c -1 downto 0) <= numerator when den_pl = '1'
    else difference(c -1 downto 0) when compare = '1'
    else n_reg(c -1 downto 0);

    ---denomintor
    process(clk, rst)
    begin
        if rst = '0' then
        d_reg <= (others => '0');
        elsif rising_edge(clk) then
        if den_pl = '1' then
        d_reg(2*c -1 downto c) <= denomintor;
        else
        d_reg <= '0' & d_reg(2*c -1 downto 1);
        end if;
        end if;
    end process;

    compare <= '1' when n_reg >= d_reg else '0';
    difference <= n_reg - d_reg;

    ---counter/compare
    process(clk, den_pl)
    begin
        if den_pl = '1' then
        cnt <= std_logic_vector(to_unsigned(c +1, 4));
        elsif rising_edge(clk) then
        if cnt_en = '1' then
        cnt <= cnt -1;
        end if;
        end if;
    end process;

    ---quotient
    process(clk, den_pl)
    begin
        if den_pl = '1' then
        q_reg <= (others => '0');
        elsif rising_edge(clk) then
        if cnt_en = '1' then
        q_reg <= q_reg(6 downto 0) & compare;
        end if;
        end if;

    end process;

    cnt_en <= '0' when cnt = 0 else '1';
    quo_out <= q_reg when cnt_en = '0' else (others => '0');
    busy <= cnt_en;
end rtl;

library ieee;
    use ieee.std_logic_1164.all;

entity tbdiv is
end entity;

architecture tbtest of tbdiv is

    component div is port(
        clk, rst : in std_logic;
        busy : out std_logic;
        ---quotient
        quo_out : out std_logic_vector(7 downto 0);
        ---denomintor
        denomintor : in std_logic_vector(7 downto 0);
        den_pl : in std_logic;
        ---numerator
        numerator : in std_logic_vector(7 downto 0));
end component;

constant halfclk : time := 50 ns;
constant delay : time := 30 ns;

signal clk, rst : std_logic;
signal busy : std_logic;
signal quo_out : std_logic_vector(7 downto 0);
signal denomintor: std_logic_vector(7 downto 0) := "00000110";
signal den_pl : std_logic := '0';
signal numerator : std_logic_vector(7 downto 0) := "00110010";
begin
    rst <= '1', '0' after halfclk*3 + delay, '1' after halfclk*7 + delay;

    clock : process
    begin
        clk <= '1'; wait for halfclk;
        clk <= '0'; wait for halfclk;
    end process;

    den_pl <= '1' after halfclk*11 + delay, '0' after halfclk*13;

    load_num : process
    begin
        wait;
    end process;

    div0 : div
        port map (clk => clk, rst => rst, busy => busy, quo_out => quo_out, denomintor => denomintor, den_pl => den_pl, numerator => numerator);

end tbtest;

--for modelsim
--library ieee;
--use ieee.std_logic_1164.all;
--
--use ieee.fixed_pkg.all;
--
--entity uns_sub is port(
-- data_in_a, data_in_b : in ufixed(3 downto -3);
-- data_out : out ufixed(4 downto -3));
--end uns_sub;
--
--architecture arch of uns_sub is
--begin
-- data_out <= data_in_a - data_in_b;
--end arch;

--for quartus
library ieee;
    use ieee.std_logic_1164.all;
library floatfixlib;
    use floatfixlib.fixed_pkg.all;

entity uns_sub is port(
    data_in_a, data_in_b : in ufixed(6 downto -3);
    data_out : out ufixed(6 downto -4));
end uns_sub;

architecture arch of uns_sub is
begin
    data_out <= data_in_a + data_in_b;
end arch;

library ieee;
    use ieee.std_logic_1164.all;

entity sm is port(
    clk, rst, ena : in std_logic;
    decode_out : out std_logic);
end sm;

architecture beh of sm is
    subtype sm_vector is std_logic_vector(2 downto 0);

    signal byte_cnt_ns : sm_vector;
    signal byte_cnt_ps : sm_vector;

    constant cnt1 : sm_vector := "000";
    constant cnt2 : sm_vector := "101";
    constant cnt3 : sm_vector := "110";
    constant cnt4 : sm_vector := "011";

begin
    byte_cntr : process(clk, rst, ena, byte_cnt_ps, byte_cnt_ns)
    begin
        if(rst = '1')then
        byte_cnt_ps <= cnt1;
        elsif rising_edge(clk) then
        byte_cnt_ps <= byte_cnt_ns;
        end if;

        case byte_cnt_ps is
        when cnt1 =>
        if(ena = '1') then byte_cnt_ns <= cnt2;
        else byte_cnt_ns <= cnt1;
        end if;
    when cnt2 =>
        if(ena = '1') then byte_cnt_ns <= cnt3;
    else byte_cnt_ns <= cnt2;
end if;
when cnt3 =>
    if(ena = '1') then byte_cnt_ns <= cnt4;
else byte_cnt_ns <= cnt3;
end if;
when cnt4 =>
    if(ena = '1') then byte_cnt_ns <= cnt1;
else byte_cnt_ns <= cnt4;
end if;
when others =>
    byte_cnt_ns <= (others => '-');
        end case;
    end process;
    decode_out <= byte_cnt_ps(2);
end beh;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity bidir_port is
    generic (
        DATA_WIDTH :integer := 8;
        ADDR_WIDTH :integer := 8);
    port (
        clk :in std_logic; -- Clock Input
        address :in std_logic_vector (ADDR_WIDTH-1 downto 0); -- address Input
        data :inout std_logic_vector (DATA_WIDTH-1 downto 0); -- data bi-directional
        cs :in std_logic; -- Chip Select
        we :in std_logic; -- Write Enable/Read Enable
        oe :in std_logic); -- Output Enable
end entity;

architecture rtl of bidir_port is
    ----------------Internal variables----------------
    constant RAM_DEPTH :integer := 2**ADDR_WIDTH;

    signal data_out :std_logic_vector (DATA_WIDTH-1 downto 0);

    type RAM is array (integer range <>)of std_logic_vector (DATA_WIDTH-1 downto 0);
    signal mem : RAM (0 to 255);
begin

    ----------------Code Starts Here------------------
    -- Tri-State Buffer control
    -- output : When we = 0, oe = 1, cs = 1
    -- THE TO_X01 DOESN'T MAKE ANY DIFF IN TB
    data <= TO_X01(data_out) when (cs = '1' and oe = '1' and we = '0') else (others => 'Z');
    --ram is outputting data --wait for data in
    -- Memory Write Block
    -- Write Operation : When we = 1, cs = 1
    MEM_WRITE:process (clk) begin
        if (rising_edge(clk)) then
        if (cs = '1' and we = '1') then
        mem(conv_integer(address)) <= data;
        end if;
        end if;
    end process;

    -- Memory Read Block
    -- Read Operation : When we = 0, oe = 1, cs = 1
    MEM_READ:process (clk) begin
        if (rising_edge(clk)) then
        if (cs = '1' and oe = '1' and we = '0') then
        data_out <= mem(conv_integer(address));
        end if;
        end if;
    end process;

end architecture;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity tb_bidir_port is
end tb_bidir_port;

architecture TB of tb_bidir_port is
    component bidir_port is
        generic (
        DATA_WIDTH :integer := 8;
        ADDR_WIDTH :integer := 8);
        port (
        clk :in std_logic; -- Clock Input
        address :in std_logic_vector (7 downto 0); -- address Input
        data :inout std_logic_vector (7 downto 0); -- data bi-directional
        cs :in std_logic; -- Chip Select
        we :in std_logic; -- Write Enable/Read Enable
        oe :in std_logic); -- Output Enable
    end component;

    signal T_Clock, T_Enable, T_WriteEn: std_logic;
    signal T_Data,T_Tx_Data, T_Rx_Data: std_logic_vector(7 downto 0);
    signal T_Address: std_logic_vector(7 downto 0);
    signal T_OE: std_logic;
begin

    T_Data <= T_Tx_Data when T_WriteEn = '1' else (others => 'Z');
    --when writing to ram --waiting for ram data out
    T_Rx_Data <= T_Data when T_WriteEn = '0' and T_OE = '1' else (others => 'Z');

    Clk_sig: process
    begin
        -- clock cycle 10 ns
        T_Clock<='1'; wait for 5 ns;
        T_Clock<='0'; wait for 5 ns;
    end process;

    process
        variable err_cnt: integer := 0;
    begin

        T_Enable <= '0';
        T_Address <= (T_Address'range => '0');
        T_Tx_Data <= (T_Tx_Data'range => '0');
        wait for 15 ns;

        --TEST WRITE
        T_Enable <= '1'; --ENABLE MEMORY
        T_OE <= '0'; --DISABLE OUTPUT TO WRITE IN MEM
        T_WriteEn <= '1'; --ENABLE WRITE
        wait until rising_edge(T_Clock);

        for i in 0 to 2 loop
        wait for 5 ns; -- UPDATE NEW VALUES
        T_Address <= T_Address + '1';
        T_Tx_Data <= T_Tx_Data + '1';
        wait until rising_edge(T_Clock); -- WAIT FOR MEM TO UPDATE
        end loop;

        --TEST READ
        wait for 5 ns; -- UPDATE NEW VALUES
        T_OE <= '1'; -- ENABLE OUTPUT TO READ FROM MEM
        T_WriteEn <= '0'; -- DISABLE READ
        T_Address <= (T_Address'range => '0'); -- RESET ADDRESS
        wait until rising_edge(T_Clock);
        for i in 0 to 3 loop
        wait for 5 ns;
        T_Address <= T_Address + '1';
        wait until rising_edge(T_Clock);
        end loop;
        wait;
    end process;

    bidir_port0 : bidir_port
        generic map(DATA_WIDTH => 8,
        ADDR_WIDTH => 8)
        port map( clk => T_Clock,
        address => T_Address,
        data => T_Data, f
        cs => T_Enable,
        we => T_WriteEn,
        oe => T_OE);

end TB;

library ieee;
    use ieee.std_logic_1164.all;

entity cpu is port(
    data : in std_logic_vector(7 downto 0);
    count : out std_logic);
end cpu;

architecture beh of cpu is
    procedure ones(signal data: in std_logic_vector;
        signal count: out std_logic) is
        variable parity: std_logic:='0';
    begin
        for i in data'range loop
        parity := parity xor data(i);
        end loop;
        count <= parity;
    end procedure ones;
begin
    ones(data, count); -- concurrent procedure call
end architecture beh;

--library ieee;
--use ieee.std_logic_1164.all;
--use ieee.numeric_std.all;
--use ieee.std_logic_unsigned.all;
--
--entity fa is
-- generic(n : in integer := 3);
-- port(
-- add_sub : in std_logic;
-- sig_uns : in std_logic;
-- x, y : in std_logic_vector(n downto 0);
-- sig_ovf : out std_logic;
-- uns_ovf : out std_logic;
-- s : out std_logic_vector(n downto 0));
-- end fa;
--
--architecture rtl of fa is
-- signal result : unsigned(n +1 downto 0);
-- signal int_result : std_logic_vector(n +1 downto 0);
-- signal uns_x, uns_y : unsigned(n +1 downto 0);
--begin
-- uns_x <= resize(unsigned(x), result'length);
-- uns_y <= resize(unsigned(y), result'length);
--
---- process(add_sub, x, y)
---- begin
-- result <= uns_x + uns_y;
---- if add_sub = '1' then
---- result <= uns_x - uns_y;
---- end if;
---- end process;
--
-- int_result <= std_logic_vector(result);
-- s <= int_result(n downto 0);
-- uns_ovf <= int_result(int_result'high);
--
--end rtl;

library ieee;
    use ieee.std_logic_1164.all;
    use ieee.std_logic_unsigned.all;

entity fa is
    generic( n : natural := 7); -- default number of bits
    port( s : in std_logic; --select subtract signal
        a : in std_logic_vector(n downto 0);
        b : in std_logic_vector(n downto 0);
        f : out std_logic_vector(n downto 0);
        uns_ovf : out std_logic;
        sig_ovf : out std_logic);
end fa;

architecture arch of fa is
    -- temp result for extracting the unsigned overflow bit
    signal result : std_logic_vector(n +1 downto 0);
    -- temp result for extracting the c3 bit
    signal c3 : std_logic_vector(n downto 0);
begin
    process(a, b, s)
    begin
        if s = '0' then --addition
        -- the two operands are zero extended one extra bit before adding
        result <= ('0' & a) + ('0' & b);
        c3 <= ('0' & a(n -1 downto 0)) + ('0' & b(n -1 downto 0));
        f <= result(n downto 0); --extract the n-bit result
        uns_ovf <= result(n +1); --extract the n bit result
        sig_ovf <= result(n +1) xor c3(n); --get signed ovf bit
        else
        -- the two operands are zero extended one extra bit before subtracting
        result <= ('0' & a) - ('0' & b);
        c3 <= ('0' & a(n -1 downto 0)) + ('0' & b(n -1 downto 0));
        f <= result(n downto 0); --extract the n-bit result
        uns_ovf <= result(n +1); --extract the n bit result
        sig_ovf <= result(n +1) xor c3(n); --get signed ovf bit
        end if;
    end process;
end arch;

library ieee;
    use ieee.std_logic_1164.all;

entity tbfa is
end entity;

architecture beh of tbfa is

    component fa is
        generic( n : natural := 3); -- default number of bits
        port( s : in std_logic; --select subtract signal
        a : in std_logic_vector(n downto 0);
        b : in std_logic_vector(n downto 0);
        f : out std_logic_vector(n downto 0);
        uns_ovf : out std_logic;
        sig_ovf : out std_logic);
    end component;

    constant period : time := 5 ns;
    constant strobe : time := period -1 ns;
    constant n : natural := 3;

    signal s : std_logic;
    signal a : std_logic_vector(n downto 0);
    signal b : std_logic_vector(n downto 0);
    signal f : std_logic_vector(n downto 0);
    signal uns_ovf : std_logic;
    signal sig_ovf : std_logic;

begin
    p0 : process
        variable q : std_logic_vector(n downto 0) := (others => '0');
    begin
        a <= (others => '0');
        b <= (others => '0');

        wait for period;

        loop
        s <= q(n);
        a <= q;
        b <= (q(n) xor (not q(2))) & q(n downto 1);
        wait for period;
        q := q(n -1 downto 0) & (q(n) xor (not q(2)));
        end loop;
    end process;

    fa0 : fa
        port map(a => a, b => b, f => f, s => s, uns_ovf => uns_ovf, sig_ovf => sig_ovf);
end beh;

library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

entity adder is
   port
   (
      nibble1, nibble2 : in unsigned(3 downto 0);
sub_sum	: out unsigned(3 downto 0);
      add_sum : out unsigned(3 downto 0);
      carry_out : out std_logic);
end entity adder;

architecture beh of adder is
   signal add : unsigned(4 downto 0);
signal sub : unsigned(4 downto 0);
begin
   add <= ('0' & nibble1) + nibble2;
   -- OR use the following syntax:
   -- add <= ('0' & nibble1) + ('0' & nibble2);
   add_sum <= add(3 downto 0);
   carry_out <= add(4);

sub <= nibble1 + not nibble2 + "00001";
sub_sum <= sub(3 downto 0);

end architecture beh;

case inst is
when => ld
when => ldx
when => ldy
when => sub
when => asr
when => st
when => add
when => asl
when => cba
when => bgt
when => blt
when => ldx
when => ldy
when => abx
when => aby